## Slide 1: OMA-CD-CPNS-2010-0027R01-INP_PN_Establishment_Flows CPNS PN Establishment Flows
Submitted To: CD-CPNS
Date: 02 Feb. 2010
Availability: Public OMA Confidential
Contact: Johan Hjelm, johan.hjelm@ericsson.com
Source: Ericsson
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: PN Establishment 1: Discovery
Initial situation: No PN GW assigned
Devices assign PN GW based on the device capabilities
Device capabilities include mode information
In step 5, the devices discover that PNE2 has the capability to act as a gateway, and PNE2 takes that role
If a PN GW is already assigned, steps 5-7 does not take place, since the capabilities of the PN GW includes its mode.
Physical pairing (out of scope)
CPNS Entity 2
CPNS Entity 1
1. Entity Registration and Discoivery
2.Enitty Registration and Discovery
3. Device Capabilities Escchange
4. Device Capabilities Escchange
5, Check received and own capabilities for gateway suitability.
6. PNE 2 takes the role as PN GW
7. PNE 2 updates PNE 1 with its new capabilities, includin g new mode.

## Slide 3: PN Establishment 2: Gateway contacts CPNS Server
PN GW 1
PNE 1
CPNS Server
11. Authentication and Authorization response (Security Function)
10. Authentication and Authorization (Security Function)
12. Connection setup confirmation
How?
If IMS is used, by accessing a PSI
If IMS is not used?
9. Connection setup request (Connection Management)
14. Authentication and Authorization response (Security Function)
13. Authentication and Authorization (Security Function)
15. Device Capabilities Update
18. Status management lookup (no change)
17. Status Management update request (status management)
19. Status Management response
20. Create and update PN Inventory
16. Device Capabiliites confirmation
8. Connection setup request (Connection Management)

## Slide 4: PN Establishment 3: Connection Setup and PN Membership Assignment
PN GW 1
PNE 1
CPNS Server
23. PN Membership
26. Connection setup confirmation
PN is established
PN GW 1
PNE 1
CPNS Server
21. PN Membership request (Connection Management)
22. PN Membership
24. PN Membership
25. PN Membership confirmatiion
26. Connection setup confirmation
PN is established