## Slide 1: OMA-CD-MobSocNet-2014-0018-INP_SNEW_P2P_Group_Discovery SNeW P2P (Groups) discovery
Submitted To: OMA CD
Date: 09 May 2014
Availability: Public OMA Confidential
Contact: Laurent Walter Goix, Francesco Arenella
Source: Telecom Italia
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Main scenarios
Proximity advertising of local businesses (& matching)
Proximity friend discovery
Social interest matching
Social profile for proximity interaction
Group discovery

## Slide 3: 1. Proximity advertising of local businesses (& matching) (I/II)
LTE-Direct “Open Discovery”-type of scenario
  Local business advertises a “pilot” signal with a “categorized id” formatted according to a tree-based structure
  User “monitors” a specific category (at any level) via a sort of longest prefix match

## Slide 4: 1. Proximity advertising of local businesses (& matching) (II/II)
SNEW requirements
  “snew” WiFi-Direct service needs to advertise this “categorized” id, e.g. in a generic “id” field with a specific type of URI (e.g. a URN) that includes the category tree
    TBV the reuse of OMA MC indirect code format
  Additional profile information may be “directly” advertised (e.g. avatar, address, display name)
  SNEW-1 may serve as resolution endpoint to access the “social profile” of that categorized id
    TBV the reuse of OMA MC Server

## Slide 5: 2. Proximity friend discovery
Discover nearby friends
  Discovery relies on (temporary) opaque user identifiers to avoid privacy leaks
  SNEW Server provides these identifiers to the user & her friends
SNEW requirements
  “snew” WiFi-Direct service needs to advertise this “opaque” user id, e.g. in a generic “id” field with a specific type of URI (e.g. an ACR) that can include the service provider (server) information
  SNEW-1 interface needs to be updated to add
    Friend opaque Ids (and expiration) when retrieving the list of friends
    User opaque Id (and expiration) when retrieving her own profile and/or via a GSMA ACR-compliant RESTful endpoint provided (indirectly) by the SNEW Server.

## Slide 6: 3. Social interest matching
Discover NEW friends (without connecting)
  Users publicly advertise their interests (associated to a public/opaque id) and/or related profile information
    Information may represent variants of the official/actual user information
  Other users “monitor” a specific (list of) interest(s)
SNEW requirements
  “snew” WiFi-Direct service needs to advertise a list of interests, e.g. in a generic “interests” field with a specific format (e.g. CSV)
  Additional profile information may be advertised (e.g. avatar, gender, age, display name)

## Slide 7: 4. Social profile for proximity interaction
Objects (e.g. Displays) can request to access social profile in proximity for personalization
  Users do not want to publicly advertise their profile information (unlike scenario 3)
  Users advertise the “snew” service together with a list of (snew-related) applications on their device. By default, this advertisement implies that a local SNEW profile server is exposed by the device that can be remotely accessed upon WiFi-Direct connection.
SNEW requirements
  Devices need to expose a OpenSocial People Service endpoint over SNEW-6

## Slide 8: 5. Group discovery
Discover nearby groups (names/topics)
  Some groups may be “private” (invitation only) and thus not discoverable
  In case of “public” groups, members may advertise the id of the GO they are connected to
  Members may also advertise an indicator to state that she is involved/connected to a group *without* revealing which one / who is the GO (and so the "go_id" field may not be transmitted, for example in case of "private" groups)
SNEW requirements
  “snew” WiFi-Direct service needs to advertise one or more “topics” and the GO id
  Devices (when acting as GO) need to expose a OpenSocial Group Service endpoint over SNEW-6, e.g. to retrieve other information such as group location/period etc after being connected to the GO.

## Slide 9: Proposal summary (I/II)
As a summary to cover the previous scenarios the following next steps are proposed
Define a set of key properties for the “snew “ wifi-direct service TXT record
  Id
  Interests
  Topics (for Group Owners)
  GO_Id (for Group members)
  (Avatar, Address, DisplayName, Gender, Age, …)

## Slide 10: Proposal summary (II/II)
Evaluate the extension of the SNEW-1 interface
  To retrieve (opaque) id and expiration information of a user profile (the reference user and/or her friends) to be advertised/monitored in proximity
  To resolve the categorized id of local businesses (as user profile)
Evaluate the dependency to external services
  OMA MC enabler (MC server to resolve indirect categorized ids)
  GSMA ACR RESTful endpoint to retrieve an opaque id for the reference user to be advertised in proximity