## Slide 1: Many devices in home environment
Entertainment ★
Video
IPTV
Streaming music
Off-line storage
Security ★
Intrusion detection
In-home monitoring
Parents controls
Remote video surveillance
Communication ★
Wireless telephony
Instant message
Voice/video conferencing
Electronic messaging
Others ★
Health devices
Home automation
Shared Internet access
Appliances control
Remote Management
Device configuration
Service Configuration
Usage Monitoring

## Slide 2: GwMO Overview
Facilitates interaction between a management server and a management client in situations where direct and unaided interaction between the management server and the management client is not possible
  Device does not have a publicly routable address
  Device sitting behind a firewall
  Device supports a management protocol other than OMA-DM
Enables a single OMA-DM message, issued by a DM Server, to be fanned out to multiple end devices, and an aggregated response to be sent back to the DM Server
Notes: 2

## Slide 3: Modes of Operation
GW MO Enabler provides framework for OMA DM to manage devices indirectly
Compatible DM v1.3 and later versions
Three different supported modes
  Transparent
  Proxy
  Adaptation
The DM Gateway can operate in different modes for different devices simultaneously.

## Slide 4: Transparent Mode
Transparent Mode
  The DM Gateway assists the DM Server in sending a DM Notification to the End Device(s) behind the DM Gateway
    The DM Gateway forwards the DM Notification to the End Device(s)
  The DM Gateway does not participate in the management session that gets established between the DM Server and the End Device(s), after the delivery of the DM Notification to the End Device(s)

## Slide 5: Proxy Mode
Proxy Mode
  The DM Gateway manages End Device(s) behind the DM Gateway on behalf of the DM Server over DM protocol. Scenarios:
    Management of End Device(s) behind Firewall
    Management of End Device(s) which may not have capabilities to access Internet
  Multiple DM sessions are established; One is between DM Server and DM Gateway; Other DM sessions are between DM Gateway and each End Device
  Supports command fanout and response aggregation
  Useful for M2M scenarios
GwMO

## Slide 6: Adaptation Mode
Adaptation Mode
  Similar to the Proxy Mode with the difference that the DM Gateway manages End Device(s) behind the DM Gateway on behalf of the DM Server over non-OMA-DM protocols (such as UPnP DM, TR069, etc.)
GwMO

## Slide 7: GwMO Architecture: Transparent Mode
GwMO-1 interface: Allows a GwMO Server to invoke GwMO Operations on the End Device via the DM Gateway using the underlying DM-1 interface
GwMO-2 interface: Allows the End Device to send GwMO Alerts to the GwMO Server via the DM Gateway using the underlying DM-1 interface
GwMO-3 interface: Allows the GwMO component to send notifications to End Device
GwMO-4 interface: Allows the DM Client to register its End Device to the DM Gateway.
DM-1 interface: Defined in the OMA DM Enabler. It provides a formal interface over which Servers may send device management commands to Clients and Clients may return status and alerts to Servers

## Slide 8: GwMO Architecture: Proxy Mode
GwMO-1 interface: Allows a GwMO Server to invoke GwMO Operations on the End Device via the DM Gateway using the underlying DM-1 interface
GwMO-2 interface: Allows the End Device to send GwMO Alerts to the GwMO Server via the DM Gateway using the underlying DM-1 interface
GwMO-3 interface: Allows the GwMO component to send notifications to End Device
GwMO-4 interface: Allows the DM Client to register its End Device to the DM Gateway.
DM-1 interface: Defined in the OMA DM Enabler. It provides a formal interface over which Servers may send device management commands to Clients and Clients may return status and alerts to Servers

## Slide 9: GwMO Architecture: Adaptation Mode
GwMO-1 interface: Allows a GwMO Server to invoke GwMO Operations on the End Device via the DM Gateway using the underlying DM-1 interface
GwMO-2 interface: Allows the End Device to send GwMO Alerts to the GwMO Server via the DM Gateway using the underlying DM-1 interface
DM-1 interface: Defined in the OMA DM Enabler. It provides a formal interface over which Servers may send device management commands to Clients and Clients may return status and alerts to Servers
NDM-1 interface: Provides an interface over which Servers may send device management commands to Clients and Clients may return status and alerts to Servers using non-OMA DM protocol. This interface is outside the scope of OMA DM.

## Slide 10: Sharing DM Account by Group of Devices
Possible Additional Functionality (to be finalized):
DM Account can be assigned to each device
DM Account can also be shared for management of group of devices

## Slide 11: GwMO: Management Objects
Device Inventory MO
  Maintains a list of Devices in the network that are managed through the DM Gateway
    Device ID
    Dev Info
    Address
    Mode
  MO is populated as and when the DM Gateway becomes aware of new Devices in the network
Gateway Config MO
  Maintains information regarding the handling of different types of Devices by the Gateway
    Bootstrapping information
    Device grouping based on various criteria. The group can be addressed for notification or command fanouts
    Controlling the issuance of the Inventory Alert notification
Additional MOs may be identified as work on the GwMO Enabler proceeds.

## Slide 12: GwMO: Management Objects
Fanout MO
  Maintains information regarding the handling of DM Commands fanout and response aggregation
  Issue the DM Commands to a single targeted End Device (specified by the Device ID in Device Inventory MO) OR issue the DM Commands to a group ID (specified in the Gateway Config MO)
  Supported for Proxy Mode (and not Transparent Mode)
Image Inventory MO
  Allows caching of data in the DM Gateway to optimize delivery of data to End Device(s)
Additional MOs may be identified as work on the GwMO Enabler proceeds.

## Slide 13: GwMO: Management Objects
Alerts to DM Server
  Device Inventory Update Alert
    Issued by DM Gateway to DM Server to notify when there are Devices attached or detached
  Device Attach Alert
    Issued by the DM Gateway to DM Server when the DM Gateway detects a new device
  Device Detach Alert
    Issued by the DM Gateway to the DM Server when the device is detached from the DM Gateway
Additional MOs may be identified as work on the GwMO Enabler proceeds.

## Slide 14: Work Status
RD and AD in Candidate status
Very good progress achieved on the TS
GwMO TS to reach Candidate status during 2011