## Slide 1: Discussion Material for Joint Conference Call with OMA DM
ETSI M2M, Management WG
Yongjing Zhang, Huawei
Joerg Swetina, NEC
Conference Call OMA DM – ETSI M2M 21st April, 2011

## Slide 2: Outline
General Information
  Topic discussed during M2M#14bis (Mar 28 - Apr 1, 2011)
  New WG Organization
  Future Meetings
ETSI M2M Updates
  ETSI-M2M and OMA-DM Architecture Integration
  M2M <mgmtObj> Resource Structure
  M2M Remote Entity Management Procedures
Discussion
References

## Slide 3: Topic discussed during M2M#14bis
13 contributions were received addressing the following management topics:
  Remote Entity Management (REM) API analysis
  M2M resource structure (data model) for REM
  REM procedures
Details can be found in following slides.

## Slide 4: ETSI M2M WG Organization
WG1: Requirements & Use Cases
WG2: Architecture & Network Interworking
WG3: Protocols & Interfaces
WG4: Security Aspects
WG5: Management
ETSI TC M2M
*New WG Organization will be formally operational since M2M#15, May 2011.

## Slide 5: Future Meetings in 2011
Meeting ID | Date | Place | Memo
M2M#15 | 23-27 May | San Diego, US | Joint with OMA DM Stage 2 stable
M2M#15bis | 27 Jun-01 Jul | Sophia Antipolis, FR | 
M2M#16 | 12-16 Sep | TBD, JP? | Stage 3 complete
M2M Workshop #2 | 18-19 Oct | Sophia Antipolis, FR | 
M2M#17 | 28 Nov-02 Dec | TBD | 

## Slide 6: Architecture Integration

## Slide 7: M2M <mgmtObj> Resource and DM MOs
For each remote entity (D/G), one or multiple <mgmtObj> resources may be created in N-SCL for remote management purpose.
N-SCL (NREM) shall translate the RESTful methods performed on <mgmtObj> resources from NA into corresponding DM/TR069 procedures performed on the MOs in the D/G.
D/G-SCL
N-SCL
<mgmtObj> Resource
DM/TR069 MO
NA
mIa (RESTful)
mId (DM/TR069)
DM/TR069 MO
DM/TR069 MO
<mgmtObj> Resource
<mgmtObj> Resource
<mgmtObj> Resource
NREM
(Device Mgmt Server)
D/GREM
(Device Mgmt Client)

## Slide 8: M2M <mgmtObj> Resource Structure
ETSI M2M supports REM function at different management layer:

## Slide 9: M2M <mgmtObj> Resource Structure
<sclBase-N1>
scls
<scl-D1>
mgmtObjs
<mgmtObj-y>
A <mgmtObj> resource is an management data interface that defines the parameters to be manipulated (via RESTful methods) for a certain type of REM function.
N-SCL
<mgmtObj-x>
<scl-G1>
mgmtObjs
<mgmtObj-z>
“attributes”
basic
additional
subscriptions
ESTI-compliant data model
Mapping of DM/TR069 data model, e.g. FUMO, DiagMO
NA may subscribe to the changes of a specific MO parameter for notification
Meta information of this <mgmtObj> resource instance
An instance of <mgmtObj> resource, e.g. “battery”, “memory”, “firmware”
An M2M Device representation
An M2M Gateway representation

## Slide 10: M2M Management Functions Overview
General Management (Gen-xxx):
  Allows retrieving general information of the M2M Device or Gateway, and provides generic mechanism applicable to different specific management functions.
Configuration Management (Cfg-xxx):
  Allows configuration of the device capabilities and features for supporting M2M services and applications, including activating / deactivating device hardware components or I/Os in the M2M Device or Gateway.
Diagnostic & Monitoring Management (D&m-xxx):
  Allows running specific diagnostic tests on a device and collecting the results or alerts from the M2M Device or Gateway. This package is also called Fault and Performance Management.
Software/Firmware Management (sfw-xxx):
  Allows installation /update/removal of application specific or SCL related software / firmware in M2M Device or Gateway.
Gateway Management (Gtw-xxx):
  Allows M2M Gateway-specific configuration and M2M Devices management through a M2M Gateway.
SCL Management (Scl-xxx):
  Allows remote configuration, provisioning and retrieval of M2M Device or Gateway service capability layer parameters.
ETSI M2M shall identify M2M REM functions and parameters with the help of existing DM/TR069 data model.

## Slide 11: M2M REM Procedures
D/GREM
(DM Client)
NREM
(DM Server)
NA
<mgmtObj-x> created (by xREM, NA, or provisioning means)
RESTful (C/R/U/D) access to <mgmtObj-x> or its components
RESTful response (status code, acquired information, …)
mIa (ETSI M2M RESTful)
mId (OMA-DM/TR069)
Resource mapping to existing MOs,
Operation mapping to existing DM methods
DM procedures (add/replace/exec/delete…)

## Slide 12: Discussion
Firmware management partitioning
  Different Management Authorities (e.g. M2M service provider, 3rd party Network Applications, device manufacturers) need to manage different pieces of the device firmware.
Addressing of DM Client
  How does the DM server route messages to the DM Client.
Device identifier
  How do the DM server and Management Authority identify a device
Security mechanism for MOs
  How to protect MOs from illegal access?
The creation/deletion/update of a <mgmtObj> resource by a Network Application triggers the addition/deletion/update of a MO in the management tree of the remote entity.
  Do OMA-DM have some opinion/guideline/advice concerning this behavior? Is it compatible with the OMA-DM spirit ?

## Slide 13: References
Service Requirement (TS 102 689 v1.1.1)
Functional Architecture (TS 102 690 v0.11.2)
Reuse of core network functionality (TR 101 531 v0.1.5)
M2M Management Function List (Working document M2M(11)0258r3)

## Slide 14
THANK YOU!