## Slide 1: OMA-DM-2013-0089-INP_WID_Proposal_Management_Interface_for_M2M Presentation of WID Information: Management Interface for M2M 1.0
Submitted To: OMA DM
Date: 10 Sept 2013
Availability: Public OMA Confidential
Contact: Tim Carey, timothy.carey@alcatel-lucent.com
Pierre H Gross, pierre.gross@alcatel-lucent.com
Source: Alcatel-Lucent
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: General information about the Work Item
WID Information
  WID 0xxx- MIM 1.0 (registered label) – Management Interface for M2M V1.0
  OMA-WID_xxx-OMA-V1_0-2013xxxx-D.zip
Short description
  This WI will focus on developing the requirements for an interface exposed by LWM2M 1.0, OMA DM 1.x, OMA DM 2.0 servers for the purpose of device management.
  The resulting requirements specification will be used to defined the scope for new API development in a subsequent WI.
WG Handling Proposal
  WID socialization with OMA DM
  Prosposed to DM WG , Reference Release with Informal RD review with REQ, followed by CONR for RD. Then RD and RRELD will be submitted for Candidate Approval.

## Slide 3: Problem / Opportunity Statement
In June, 2013 the vote for approval WID 0282 MAI 1.0 was rejected with comments that additional clarifications regarding how this work item would be positioned with the activities from oneM2M. This contribution proposes a new work item that clarifies this positionning.
The new work item will focus on developing the requirements for an interface exposed by LWM2M 1.0, OMA DM 1.x, OMA DM 2.0 servers for the purpose of device management.
One of the drivers for this enabler is oneM2M. The requirements for the interface support the overall oneM2M management requirements and should be shared with oneM2M.

## Slide 4: oneM2M Device Management Work To Date
Agreed to 17 management requirements to managing devices using technology specific device management protocols such as LWM2M and OMA-DM (TS-0002 Requirements) (Normative).
Agreed to a series of Device Management deployment scenarios that currently are existing as well as could potentially exist in a M2M environment (TR-0006 Study on Management Enablement) (Informative).
In the process of defining the Functional Architecture (Normative) that includes descriptions of procedural flows and resources to manage devices.

## Slide 5: Scope of work item in the context of oneM2M
©Sensinode 2013
M2M App
M2M App
M2M Service Layer
(E.g. oneM2M)
Device Management Layer
DM server
Gateway / M2M Device
Gateway / M2M Device
Constrained M2M Device
DM 1.x
DM 2.0
LWM2M 1.0
LWM2M
server
Northbound Interface between the DM/LWM2M Server and the M2M Service Layer for Device Management

## Slide 6: Work Item Scope
Develop Requirements for the management server interface
Objectives
  Develop similar if not the same interface for all OMA DM protocols
  Minimize the number of times Objects are translated
    Device Management Layer exposes the objects in DM protocol format (OMA-DM 1.x, OMA-DM 2.0, LWM2M 1.0).
    Translation of the objects from the M2M Service Layer resources to the OMA Objects (Possibly the responsibility of M2M Service Layer)
  Support M2M Service Layer Role Based Security mechanisms for Objects exposed by the interface
    Enables Use Cases like Shared Device Control between the Network Operator and M2M Service provider.
    Needs to ultimately map to the OMA DM / LWM2M device ACL concepts but may require security mechanisms in the DM Server.

## Slide 7: Use Case: Shared Device Control
The underlying network operator and the M2M Service Provider share control of the device by utilizing the underlying network operator’s management server.
The underlying network operator restricts which resources the M2M Service Provider can control.
Typically this is performed by providing the M2M Service Provider an account, with appropriate access control to the resources, within the underlying network operators management server.
(Source oneM2M TR-0006 section 7.3.1)
Example of ressource split:
  Network operator: FUMO, ConnMO, Diagmon
  M2M SP: SCOMO, Diagmon
M2M App
M2M App
M2M Service Layer
Network Operator OSS
DM server
Device
M2M Service Domain
Network Domain
Service Provider OSS

## Slide 8: Use Cases: Device Management
Device Management Use Cases. For example:
  Firmware update operation for one or more devices
  Application update operations (download, install, activate, deactivate, remove) procedure for one or more devices
  Diagnostics
  Configuration
Note: M2M Service Use Cases are not the focus of this version of the enabler.

## Slide 9: Potential Interface Requirements
  M2M Service Layer to DM/LWM2M Server association establishment
    Establishment and maintenance of an association to a DM/LWM2M server (e.g., credentials, accounts, roles)
  M2M Service Layer to DM/LWM2M Server Event Maintenance
    Maintaining pending or scheduled events (e.g., operations, notifications, bulk data transfers, firmware updates, application updates) between the M2M Service Layer and the DM/LWM2M Server
  M2M Service Layer to DM/LWM2M Server Security Translations
    Define the mechanism to be used to support the Service Layer role based security for DM/LWM2M objects and commands exposed by the management interface
  M2M Service Layer to DM/LWM2M Server Resource (Object) Discovery
    Discovery operation to the DM/LWM2M Server for device resources within the DM/LWM2M Server

## Slide 10: Potential Interface Requirements(cont1)
  M2M Service Layer to DM/LWM2M Server Operations
    Create, Retrieve, Update, Delete (CRUD) operation to the DM/LWM2M Server for resources within the DM/LWM2M Server
    Non-CRUD operation to the DM/LWM2M Server for resources within the DM/LWM2M Server
  DM/LWM2M Server to M2M Service Layer Notification
    Notification of changes between the DM/LWM2M Server and the M2M Service Layer for resources within the DM/LWM2M Server
  DM/LWM2M Server to M2M Service Layer Bulk Data Transfer
    Transfer of a large number of resources between the DM/LWM2M Server and the M2M Service Layer for resources within the DM/LWM2M Server

## Slide 11: How OMA can help
OMA DM group has the expertise of the underlying enablers (OMA DM1.x, DM2.0, LWM2M) and is therefore the best place to provide requirements and specifications for the management interface to the M2M Service Layer (e.g. oneM2M).
OMA ARC group has a track record of successful delivery of Network API specifications for RESTful and SOAP bindings as well as guidelines and specifications for Authorization mechanisms (Autho4API 1.0).

## Slide 12: Impacts, relationships and dependencies
State (potentially) related
  OMA DM 1.x, OMA DM 2.0, OMA DM Lightweight M2M, GwMO, DiagMon
State potential and identified dependencies
  OMA DM 1.x, OMA DM 2.0 , OMA DM Lightweight M2M
Describe impacts on different system elements
  No Impacts expected

## Slide 13: Proposed Timeline
 |  | Approximate duration in months |  | 
 | Date |  |  | 
RD start | 2013-10-03 |  |  | 
New reqs deadline | 2013-12-06 |  |  | 
RD review start | 2013-12-13 |  |  | 
RD as Candidate | 2014-01-30 | 4 |  | 
AD start |  |  |  | 
AD review start |  |  |  | 
AD as Candidate |  | 0 |  | 
Detailed spec start |  |  |  | 
Consistency start |  | 0 | #### | 
Enabler as Candidate | 2014-01-30 |  |  | 4
Chart: Month / Year
| Development time to Candidate | TS | AD | RD
Begin | 41550 | 0 | 0 | 41550
Duration | 119 | 0 | 0 | 119

## Slide 14: Supporting Companies
The companies supporting this work item are:
Company name | Membership type
Alcatel-Lucent | Full

## Slide 15: Proposed Resources
The companies supporting this work item are proposing the following resources:
Deliverable/Role | Proposed volunteer editor/champion
Requirements Document (RD) | TBD
Requirements Document Review Report (RDRR) | TBD
Architecture Document (AD) | N/A
Architecture Document Review Report (ADRR) | N/A
Technical Specification (TS) | N/A
Enabler Test Requirements (ETR) | N/A
Enabler Test Requirements Review Report (ETRRR) | N/A
Enabler Release Definition (ERELD) | TBD
Consistency Review Report (CONRR) | N/A
WID/WISPR Champion | TBD
ARC Champion | N/A
IOP Champion | N/A