## Slide 1: YANG at BBF… and OMA?
William Lupton
Broadband Forum Software Architect
OMA DM | Edinburgh | 04-May-2016
v1

## Slide 2: Outline
YANG introduction
BBF and YANG
YANG translation
Translation examples

## Slide 3: YANG Introduction
What is YANG?
What does YANG look like?
Other key points
Tools: pyang

## Slide 4: What is YANG?
YANG (RFC 6020; Wikipedia) is “a data modeling language used to model configuration and state data manipulated by the Network Configuration Protocol (NETCONF), NETCONF remote procedure calls, and NETCONF notifications”
  YANG is designed to be rich enough to allow configuration and status to be modeled precisely and rigorously
  (from RFC 6020) “The model defines a contract between the NETCONF client and server, which allows both parties to have faith the other knows the syntax and semantics behind the modeled data. The strength of YANG lies in the strength of this contract”
NETCONF and YANG are the IETF replacements (arising from the 2002 IAB Network Management Workshop; RFC 3535) for SNMP and ASN.1 (as used for SNMP MIBs)
Many SDOs other than IETF, including BBF, IEEE, MEF and ONF, have published or are developing YANG data models in their respective areas of expertise
YANG and NETCONF are widely cited in the context of SDN and NFV, e.g.
  ONF’s OF-Config requires support for NETCONF and YANG
  ODL supports NETCONF (with YANG) for managing OpenFlow (etc.) data plane elements
IETF have nearly completed YANG 1.1, defined in RFC 6020 bis, and updated RFC 6087 bis (guidelines)
Notes: YANG is reputed to stand for Yet Another Next Generation, which is probably a reference to RFC 3780 “SMIng - Next Generation Structure of Management Information”
There is (of course) a companion YIN format; YIN stands for YANG Independent Notation and is an equivalent XML syntax (the translation rules are very simple)

## Slide 5: What Does YANG Look Like?
module ietf-interfaces {
namespace “urn:ietf:params:xml:ns:yang:ietf-interfaces”;
prefix if;
import ietf-yang-types { prefix yang; }
organization “IETF NETMOD (NETCONF Data Modeling Language) WG”;
contact “WG Web: <http://tools.ietf.org/wg/netmod/>…”;
description “This module contains a collection of YANG definitions…”;
revision 2014-05-08 {
description ”Initial revision.”;
reference ”RFC 7223: A YANG Data Model for Interface Management”;
}
typedef interface-state-ref {
type leafref {
path “/if:interfaces-state/if:interface/if:name”;
}
}
identity interface-type {
description “Base identity…”;
}
feature arbitrary-names {
description “This feature indicates that…”;
}
Key Points:
C-like syntax: each statement has exactly one argument and an optional body
Each module defines a namespace (a module can be split into submodules)
Modules define a single data tree in which each node is in a given namespace (c.f. XML)
Other modules can augment the data tree (not shown here but IMPORTANT!)
Revisions are identified by date (can be multiple revisions; only one shown here)
Typedefs: similar to C etc.
Identities: multiple inheritance hierarchy
Features: also hierarchical
Notes: This and the next slide are taken from the RFC 7223 ietf-interfaces YANG module.
Many sections have been removed and much text has been truncated.
The idea is to illustrate the most common and important YANG constructs.

## Slide 6: What Does YANG Look Like?
container interfaces {
list interface {
key "name";
leaf name {
type string;
description “The name of the interface…”;
}
leaf type {
type identityref {
base interface-type;
}
mandatory true;
description “The type of the interface…”;
}
…
container interfaces-state {
config false;
list interface {
key "name";
leaf-list higher-layer-if {
type interface-state-ref;
description “A list of references to interfaces layered on top …”;
}
Key Points:
Data model can contain four node types
Container: single instance; level in naming hierarchy; also “presence” containers
List: like a table; uniquely keyed by >=1 leaf node
Leaf: single primitive value
Leaf-list: multiple primitive values
The “usual” primitive data types, plus references, unions etc.
“type” node illustrates identity usage
“higher-layer-if” illustrates leaf-list and leafref
Mandatory: mark a node as being mandatory
Config false: mark a node (and its children) as being state data

## Slide 7: Other Key Points
XPath (1.0) subset is used in several ways
  Must statement has XPath expression that must be true in a valid data tree
  When statement has XPath expression that defines when its parent node is allowed to exist
    Commonly used to specify the condition under which an “augment” applies
  Leafref statement’s path is an XPath expression
  Several YANG-specific XPath functions
Additional statements
  Default
    Value assumed if a node isn’t implemented
  Grouping
    Reusable named group of node definitions
    Think of it as an expandable YANG macro
  Action
    Associated with a specified node
    Can have input and output arguments
  Notification
Notes: Not all statements are mentioned

## Slide 8: Tools: pyang
pyang “is a YANG validator, transformator and code generator, written in python. It can be used to validate YANG modules for correctness, to transform YANG modules into other formats, and to generate code from the modules”
  For example it can generate various tree views, UML, XSD (XML Schema) and YIN (XML)
See later for example pyang tree views
  All IETF YANG RFCs include pyang tree views
See the “YANG resources” slide for links to more tools

## Slide 9: BBF and YANG
BBF YANG projects
Interactions with other SDOs

## Slide 10: BBF YANG Projects
2014: due diligence and decision to use NETCONF and YANG for DPU management (DPU = Distribution Point Unit; see BBF TR-301)
2015: new project for DPU management YANG
2015: VDSL then G.fast models, then xDSL + G.hs, MELT and SELT
2015: new project for Access Node YANG (a DPU is a specialized access node)
2016: first phase of DPU management nearing completion; 8 modules; many sub-modules
2016: second phase of DPU management has already started
2016: new project investigating translation of TR-069 CPE management models to YANG
2016: new project for G.hn YANG
2016: new project for PON ONU YANG
2016: new project for Common YANG (YANG that can be used by multiple BBF work areas)

## Slide 11: Interactions with other SDOs
BCP = Best Current Practice
Common SDO YANG and BCPs
IETF
YANG and BCPs
BBF
YANG and BCPs
XXX
YANG and BCPs
IEEE YANG and BCPs
BBF BCPs: OD-360
IETF BCPs: RFC 6087
IETF core YANG:
ietf-yang-types
ietf-interfaces
ietf-ip
…
IEEE core YANG:
ieee-types
ieee-ethernet
ieee-dot1x
ieee-dot1q
…
(under development)
BBF core YANG:
bbf-xdsl
bbf-fast
bbf-vdsl
…
(under development)

## Slide 12: YANG Translation
Why translate?
General approach
Challenges

## Slide 13: Why Translate?
BBF has considerable investment in TR-069 data models and would like to be able to leverage this work in the YANG world
Service Data Models
Root Data Model
Performance test Objects
TR-143
General purpose Objects
TR-157
Device:2 Root Data Model
TR-181i2
Baseline Data Model template (DM and DT Schemas)
TR-106
CWMP (CPE WAN Management Protocol)
TR-069
Femto Objects
TR-262
VoiceService:1
TR-104
STBService:1
TR-135
StorageService:1
TR-140
FAPService:1
TR-196
FAPService:2
TR-196i2
VoiceService:2
TR-104i2
Notes: Figure adapted from BBF TR-106 Amendment 7 Figure 2

## Slide 14: General Approach
Most BBF DM XML Schema features map easily to the corresponding YANG features
  DM XML Schema is the BBF TR-069 equivalent of OMA DM DDF
  All TR-069 data models are defined as DM instances, e.g. tr-181-2-0-0.xml defines the Device:2.0 Root Data Model
Therefore can write a tool to apply mapping rules and convert TR-069 data models to YANG modules
  Feasible because YANG is in general more fully-featured than the DM Schema
  But the devil is in the detail
A BBF project is actively investigating this
  SD-376: CWMP Data Model/YANG Translation Rules and Tools

## Slide 15: Challenges
Challenges are at two different levels
  Mismatch between DM Schema and YANG features
  Different TR-069 and YANG modeling approaches
The second challenge is harder to address
  Device:2 has its own way of modeling network interfaces and their relationships
    Modeled on SNMP interface MIB (RFC 2863)
    IETF have defined ietf-interface YANG module (RFC 7223)
    This is a core YANG module and has separate config and state trees
    Translated Device:2 modules MUST use rather than replicate the ietf-interface YANG module
  Device:2 has its own objects for many technologies “owned” by other SDOs
    Examples include DSL, Ethernet, 802.1Q bridges and WiFi
    IEEE are working on Ethernet and 802.1Q YANG modules
    Translated Device:2 modules MUST use rather than replicate such modules
Therefore it only makes sense to translate some parts of the BBF data models
  The parts that are in areas of BBF domain expertise and/or that other SDO have no interest in defining
  Examples include ITU-T PHY-layer technologies (VDSL, G.fast, …) and applications (firewall, parental controls, …)

## Slide 16: Translation Examples
BBF TR-069 example
OMA DM example
OMA LWM2M example

## Slide 17: BBF TR-069 Example: DeviceInfo
<object name="Device.DeviceInfo." access="readOnly"
minEntries="1" maxEntries="1">
<description>…</description>
<parameter name="DeviceCategory" access="readOnly">
<description>…</description>
<syntax><list/><string/></syntax>
</parameter>
<object name="Device.DeviceInfo.VendorConfigFile.{i}."
access="readOnly" … minEntries="0" maxEntries="unbounded">
<description>…</description>
<uniqueKey functional="false">
<parameter ref="Alias"/>
</uniqueKey>
<uniqueKey>
<parameter ref="Name"/>
</uniqueKey>
<parameter name="Alias" access="readWrite"
activeNotify="canDeny">
<description>…</description>
<syntax><dataType ref="Alias"/></syntax>
</parameter>
Notes: The brute-force translation was done using a proof-of-concept “dm2yang” tool, with some final manual editing to extract smaller YANG modules (the tool can’t yet do this)

## Slide 18: BBF TR-069 Example: DeviceInfo
<object name="Device.DeviceInfo." access="readOnly"
minEntries="1" maxEntries="1">
<description>…</description>
<parameter name="DeviceCategory" access="readOnly">
<description>…</description>
<syntax><list/><string/></syntax>
</parameter>
<object name="Device.DeviceInfo.VendorConfigFile.{i}."
access="readOnly" … minEntries="0" maxEntries="unbounded">
<description>…</description>
<uniqueKey functional="false">
<parameter ref="Alias"/>
</uniqueKey>
<uniqueKey>
<parameter ref="Name"/>
</uniqueKey>
<parameter name="Alias" access="readWrite"
activeNotify="canDeny">
<description>…</description>
<syntax><dataType ref="Alias"/></syntax>
</parameter>
module DeviceInfo {
namespace "urn:bbf:yang:device-info";
prefix device-info;
container Device {
container DeviceInfo {
leaf DeviceCategory {
type string;
config false;
description "";
}
leaf Manufacturer {
type string {
length "0..64";
}
config false;
}
list VendorConfigFile {
key "Alias";
config false;
leaf Alias {
type string { length "0..64"; }
Notes: The brute-force translation was done using a proof-of-concept “dm2yang” tool, with some final manual editing to extract smaller YANG modules (the tool can’t yet do this)

## Slide 19: BBF TR-069 Example: pyang
% pyang --format=tree DeviceInfo.yang
module: DeviceInfo
+--rw Device
+--rw DeviceInfo
+--ro DeviceCategory? string
+--ro Manufacturer? string
+--ro ManufacturerOUI? string
+--ro ModelName? string
+--ro ModelNumber? string
+--ro Description? string
+--ro ProductClass? string
+--ro SerialNumber? string
+--ro HardwareVersion? string
+--ro SoftwareVersion? string
+--ro AdditionalHardwareVersion? string
+--ro AdditionalSoftwareVersion? string
+--rw ProvisioningCode? string
+--ro UpTime? uint32
+--ro FirstUseDate? yang:date-and-time
+--ro VendorConfigFile* [Alias]
+--ro Alias string
+--ro Name? string
+--ro Version? string
+--ro Date? yang:date-and-time
+--ro Description? string
+--ro UseForBackupRestore? boolean

## Slide 20: OMA DM Example
<MgmtTree> <VerDTD>1.2</VerDTD> <Node> <NodeName>DevDetail</NodeName> <!--Status: Required--> <Path>...</Path> <DFProperties> <AccessType><Get/></AccessType> <DFFormat><node/></DFFormat> <Occurrence><One/></Occurrence> <DFTitle>This interior node specifies…</DFTitle> <DFType> <DDFName>urn:oma:mo:oma-dm-devdetail:1.1</DDFName> </DFType> </DFProperties> <Node> <NodeName>Bearer</NodeName> <!--Status: Optional--> <DFProperties> <AccessType><Get/></AccessType> <DFFormat><node/></DFFormat> <Occurrence><One/></Occurrence> <DFTitle>An optional, interior node…</DFTitle> <DFType><DDFName/></DFType> </DFProperties> </Node>
…
Notes: The translation was manual and is just to show roughly how OMA DM DDF might map to YANG

## Slide 21: OMA DM Example
<MgmtTree> <VerDTD>1.2</VerDTD> <Node> <NodeName>DevDetail</NodeName> <!--Status: Required--> <Path>...</Path> <DFProperties> <AccessType><Get/></AccessType> <DFFormat><node/></DFFormat> <Occurrence><One/></Occurrence> <DFTitle>This interior node specifies…</DFTitle> <DFType> <DDFName>urn:oma:mo:oma-dm-devdetail:1.1</DDFName> </DFType> </DFProperties> <Node> <NodeName>Bearer</NodeName> <!--Status: Optional--> <DFProperties> <AccessType><Get/></AccessType> <DFFormat><node/></DFFormat> <Occurrence><One/></Occurrence> <DFTitle>An optional, interior node…</DFTitle> <DFType><DDFName/></DFType> </DFProperties> </Node>
…
module DM-DevDetail {
namespace "urn:example:yang:dm-dev-detail";
prefix dm-dev-detail;
…
container DevDetail {
config false;
description "This interior node…";
container Bearer {
config false;
description
"An optional, interior node…";
}
container URI {
config false;
description
"This interior node…";
leaf MaxDepth {
mandatory true;
config false;
type string;
description
"Specifies the maximum depth…";
}
Notes: The translation was manual and is just to show roughly how OMA DM DDF might map to YANG

## Slide 22: OMA DM Example: pyang
% pyang --format=tree DM-DevDetail.yang
module: DM-DevDetail
+--ro DevDetail
+--ro Bearer
+--ro URI
| +--ro MaxDepth string
| +--ro MaxTotLen string
| +--ro MaxSegLen string
+--ro DevType string
+--ro OEM string
+--ro FwV string
+--ro SwV string
+--ro HwV string
+--ro LrgObj boolean
+--ro SessionlessRpt boolean
+--ro UserInteraction
| +--ro UserInput boolean
| +--ro Display boolean
| +--ro Confirm boolean
| +--ro Choice boolean
| +--ro ProgressNotify boolean
+--ro Ext? boolean

## Slide 23: OMA DM Example: pyang
% pyang --format=tree DM-DevDetail.yang
module: DM-DevDetail
+--ro DevDetail
+--ro Bearer
+--ro URI
| +--ro MaxDepth string
| +--ro MaxTotLen string
| +--ro MaxSegLen string
+--ro DevType string
+--ro OEM string
+--ro FwV string
+--ro SwV string
+--ro HwV string
+--ro LrgObj boolean
+--ro SessionlessRpt boolean
+--ro UserInteraction
| +--ro UserInput boolean
| +--ro Display boolean
| +--ro Confirm boolean
| +--ro Choice boolean
| +--ro ProgressNotify boolean
+--ro Ext? boolean

## Slide 24: OMA LWM2M Example
<LWM2M …>
<Object ObjectType="MODefinition">
<Name>Device</Name>
<Description1>This LWM2M Object…</Description1>
<ObjectID>3</ObjectID>
<ObjectURN>TBD</ObjectURN>
<MultipleInstances>Single</MultipleInstances>
<Mandatory>Mandatory</Mandatory>
<Resources>
<Item ID="0">
<Name>Manufacturer</Name>
<Operations>R</Operations>
<MultipleInstances>Single</MultipleInstances>
<Mandatory>Optional</Mandatory>
<Type>String</Type>
<RangeEnumeration/>
<Units/>
<Description>Human readable manufacturer name</Description>
</Item>
<Item ID="1">
<Name>Model Number</Name>
<Operations>R</Operations>
<MultipleInstances>Single</MultipleInstances>
<Mandatory>Optional</Mandatory>
<Type>String</Type>
<RangeEnumeration/>
<Units/>
<Description>A model identifier…</Description>
</Item>
…
Notes: The translation was manual and is just to show roughly how OMA LWM2M objects and resources might map to YANG

## Slide 25: OMA LWM2M Example
<LWM2M …>
<Object ObjectType="MODefinition">
<Name>Device</Name>
<Description1>This LWM2M Object…</Description1>
<ObjectID>3</ObjectID>
<ObjectURN>TBD</ObjectURN>
<MultipleInstances>Single</MultipleInstances>
<Mandatory>Mandatory</Mandatory>
<Resources>
<Item ID="0">
<Name>Manufacturer</Name>
<Operations>R</Operations>
<MultipleInstances>Single</MultipleInstances>
<Mandatory>Optional</Mandatory>
<Type>String</Type>
<RangeEnumeration/>
<Units/>
<Description>Human readable manufacturer name</Description>
</Item>
<Item ID="1">
<Name>Model Number</Name>
<Operations>R</Operations>
<MultipleInstances>Single</MultipleInstances>
<Mandatory>Optional</Mandatory>
<Type>String</Type>
<RangeEnumeration/>
<Units/>
<Description>A model identifier…</Description>
</Item>
…
module LWM2M-Device {
namespace "urn:example:yang:lwm2m-device";
prefix l2m2m-device;
container Device {
config true;
action Reboot {
}
leaf-list AvailablePowerSources {
config false;
type uint32;
}
leaf BatteryLevel {
config false;
type uint32 {
range "0..100";
}
units "%";
}
Notes: The translation was manual and is just to show roughly how OMA LWM2M objects and resources might map to YANG

## Slide 26: OMA LWM2M Example: pyang
% pyang --format=tree LWM2M-Device.yang
module: LWM2M-Device
+--rw Device
+--ro Manufacturer? string
+--ro ModelNumber? string
+--ro SerialNumber? string
+--ro FirmwareVersion? string
+---x Reboot
+---x FactoryReset
+--ro AvailablePowerSources* uint32
+--ro AvailablePowerSourcesAsEnumeration* enumeration
+--ro AvailablePowerSourcesAsBits? bits
+--ro PowerSourceVoltage* uint32
+--ro PowerSourceCurrent* uint32
+--ro BatteryLevel? uint32
+--ro MemoryFree? uint32
+--ro ErrorCode* uint32
+---x ResetErrorCode
+--rw CurrentTime? yang:date-and-time
+--rw UTCOffset? string
+--rw Timezone? string
+--ro SupportedBindingAndModes? string
Notes: AvailablePowerSourcesAsEnumeration and AvailablePowerSourcesAsBits illustrate alternative approaches

## Slide 27: Thank you
Questions?

## Slide 28: YANG Resources
To find out more about YANG, useful resources include
  YANG Central: http://www.yang-central.org
  NETCONF Central: http://www.netconfcentral.org
  pyang tool: https://github.com/mbj4668/pyang
  YANG Models: https://github.com/YangModels/yang
Detailed NETCONF / YANG tutorial
  http://www.slideshare.net/tailfsystems/netconf-yang-tutorial (YANG starts at slide 68)
Also see the Wikipedia page
  https://en.wikipedia.org/wiki/YANG

## Slide 29: pyang Tree Format
% pyang --tree-help
Each node is printed as:
<status> <flags> <name> <opts> <type> <if-features>
<status> is one of:
+ for current
x for deprecated
o for obsolete
<flags> is one of:
rw for configuration data
ro for non-configuration data
-x for rpcs
-n for notifications
<name> is the name of the node
(<name>) means that the node is a choice node
:(<name>) means that the node is a case node
If the node is augmented into the tree from another module, its
name is printed as <prefix>:<name>.
<opts> is one of:
? for an optional leaf or choice
! for a presence container
* for a leaf-list or list
[<keys>] for a list's keys
<type> is the name of the type for leafs and leaf-lists
If the type is a leafref, the type is printed as "-> TARGET", where
TARGET is either the leafref path, with prefixed removed if possible.
<if-features> is the list of features this node depends on, printed
within curly brackets and a question mark "{...}?"