## Slide 1: Multiple Transports in LwM2M
Hannes Tschofenig

## Slide 2: Multiple Transports
LwM2M v1.1 supports a number of different transports, such as UDP, TCP, SMS, Lorawan, and NB-IOT. With LwM2M v1.2 we plan to add further transports.
A LwM2M Client may support multiple of these transports and each of them needs to be configured.
Each of these servers are identified through their own URI, even if they point to the same server.
Example:
  coaps://foo.example.com (for CoAP over DTLS over UDP)
  coaps+tcp://foo.example.com (for CoAP over TLS over TCP)
  coap+sms://0015105550101 (for CoAP over DTLS over SMS)
  https://foo.example.com (for HTTP over TLS over TCP)

## Slide 3: Example where the same data is provisioned twice
LwM2M Security Object | Instance #0
LWM2M Server URI | coaps://foo.example.com
Security Mode | 1 (“RPK”)
Public Key or Identity | 3059301306072a8648ce 3d020106082a8648ce3d 03010703420004a09dcb 1bc739e7f19afa9adcb1 944968bfba73efcec29b 50486eb44d1b29c19344 9970a3736830cb2bd5d7 ec05d2bd1fc07b6df5e4 8b54ce77a6a7229c3a91 c2
Server Public Key | 3059301306072a8648ce 3d020106082a8648ce3d 0301070342000482c773 f378d30c2783a48eb811 b96cf6a90694a8564f1e 7f6d366152f11698950f 6f7c40cda585334f8377 50a102f5bf25508ceb9e 55dfc0f12a455199a4c9 60
Secret Key | 307702010104209f352d a16495748e146fcb5370 b8e96d292ced5567a8fa e55a22bb67d91651b8a0 0a06082a8648ce3d0301 07a14403420004a09dcb 1bc739e7f19afa9adcb1 944968bfba73efcec29b 50486eb44d1b29c19344 9970a3736830cb2bd5d7 ec05d2bd1fc07b6df5e4 8b54ce77a6a7229c3a91 c2
Short Server ID | 102
LwM2M Security Object | Instance #1
LWM2M Server URI | coaps+tcp://foo.example.com
Security Mode | 1 (“RPK”)
Public Key or Identity | 3059301306072a8648ce 3d020106082a8648ce3d 03010703420004a09dcb 1bc739e7f19afa9adcb1 944968bfba73efcec29b 50486eb44d1b29c19344 9970a3736830cb2bd5d7 ec05d2bd1fc07b6df5e4 8b54ce77a6a7229c3a91 c2
Server Public Key | 3059301306072a8648ce 3d020106082a8648ce3d 0301070342000482c773 f378d30c2783a48eb811 b96cf6a90694a8564f1e 7f6d366152f11698950f 6f7c40cda585334f8377 50a102f5bf25508ceb9e 55dfc0f12a455199a4c9 60
Secret Key | 307702010104209f352d a16495748e146fcb5370 b8e96d292ced5567a8fa e55a22bb67d91651b8a0 0a06082a8648ce3d0301 07a14403420004a09dcb 1bc739e7f19afa9adcb1 944968bfba73efcec29b 50486eb44d1b29c19344 9970a3736830cb2bd5d7 ec05d2bd1fc07b6df5e4 8b54ce77a6a7229c3a91 c2
Short Server ID | 102
LwM2M Server Object | Instance #0
Short Server ID | 102
Lifetime | 86400
Default Minimum Period | 300
Default Maximum Period | 6000
DisableTimeout | 86400
Binding Preference | U

## Slide 4: Second example where additional message exchanges are needed.
LwM2M Security Object | Instance #0
LWM2M Server URI | coaps://foo.example.com
Security Mode | 1 (“EST”)
Public Key or Identity | N/A
Server Public Key | 3059301306072a8648ce 3d020106082a8648ce3d 0301070342000482c773 f378d30c2783a48eb811 b96cf6a90694a8564f1e 7f6d366152f11698950f 6f7c40cda585334f8377 50a102f5bf25508ceb9e 55dfc0f12a455199a4c9 60
Secret Key | N/A
Short Server ID | 102
LwM2M Security Object | Instance #1
LWM2M Server URI | coaps+tcp://foo.example.com
Security Mode | 1 (“EST”)
Public Key or Identity | N/A
Server Public Key | 3059301306072a8648ce 3d020106082a8648ce3d 0301070342000482c773 f378d30c2783a48eb811 b96cf6a90694a8564f1e 7f6d366152f11698950f 6f7c40cda585334f8377 50a102f5bf25508ceb9e 55dfc0f12a455199a4c9 60
Secret Key | N/A
Short Server ID | 102
LwM2M Server Object | Instance #0
Short Server ID | 102
Lifetime | 86400
Default Minimum Period | 300
Default Maximum Period | 6000
DisableTimeout | 86400
Binding Preference | U

## Slide 5: EST Message Exchanges
LwM2M
Client
LwM2M
Bootstrap-Server
Bootstrap-Request
Write, Read, Delete, Discover Bootstrap
Write, Read, Delete, Discover Bootstrap
…
EST Discover
URIs
EST Certificate Signing Request (CSR) Instance #0
Certificate #0
EST Certificate Signing Request (CSR) Instance #1
Certificate #1

## Slide 6: Single Security Object for use with multiple servers
LwM2M Security Object | Instance #0
Server Contact Information | 
Server Scheme | 
Server Property | 
Security Mode | 1 (“RPK”)
Public Key or Identity | 30593..c2
Server Public Key | 30593…90
Secret Key | 30935..c4
Short Server ID | 102
EST URIs | 
Server Contact Information
foo.example.com
bar.example.com:443
Server URI Scheme
coaps
coaps+tcp
Server Property (Bitmap)
Used as LwM2M Server? YES / NO Used as a fallback? YES / NO Used as Bootstrap Server? YES / NO
EST Discovery URIs
</est/crts>;rt="ace.est.crts";ct="281 287", </est/sen>;rt="ace.est.sen";ct="281 287", </est/sren>;rt="ace.est.sren";ct="281 287", </est/att>;rt="ace.est.att";ct=285, </est/skg>;rt="ace.est.skg";ct=62, </est/skc>;rt="ace.est.skc";ct=62

## Slide 7: Reduction of exchanges
LwM2M
Client
LwM2M
Bootstrap-Server
Bootstrap-Request
Write, Read, Delete, Discover Bootstrap
Write, Read, Delete, Discover Bootstrap
…
EST Discover
URIs
EST Certificate Signing Request (CSR) Instance #0
Certificate #0
EST Certificate Signing Request (CSR) Instance #1
Certificate #1