## Slide 1: OMA-DM-LightweightM2M-2016-0008-INP_LPWA_considerations LWM2M 1.1 LPWA considerations
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE
AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.
Date: 18 Jan 2016
Availability:
Public
OMA Confidential
Contact: Friedhelm Rodermund rodermund@vodafone.de
Source: Vodafone
X

## Slide 2: LWM2M 1.1 WID extract (1/2)
LWPAN (Low Power Wide Area Network) support
  LPWAN technologies such as 3GPP NB-IoT support low data rate, long range, low power consumption communications
  LWM2M would be well fitted as service enabler for LPWAN scenarios
  Possible optimizations and improvements of LWM2M towards LPWAN:
      Optimizations of LWM2M for usage over LPWAN to further reduce the amount of data carried across the radio interface  increasing battery life time
      Functional enhancements e.g. for LWPAN connectivity management
Dependencies : 3GPP C-IoT

## Slide 3: LWM2M 1.1 WID extract (2/2)
Follow impacts from 3GPP/GSMA enhancements on last mile like tunneling to reduce the burden on Client with respect to LWM2M TS
End-to-end Security need to be evaluated for LPWAN scenario, depending on the enhancements/recommendations provided by 3GPP/GSMA

## Slide 4: High level requirements
LPWA devices need remote device management and service enablement
Configuration settings to allow the device to connect to application servers
Updating firmware, software
Diagnostics to detect health of device, or repair in case it fails
Configuration settings to affect the behaviour of the device applications
Managing data from the applications
Device mgmt.
Service enabl.

## Slide 5: High level requirements
Which DM capabilities might be in scope?
Device Management (DM) and provisioning capabilities are highly relevant to LPWA e.g. NB-IoT devices and their applications:
DM capability | NB-IoT examples
Bootstrapping the device | Setting connectivity parameters, e.g. - type of data to send over NB-IoT (IP, non-IP, SMS) - frequency band selection ?
Managing application behaviour and device behaviour | Setting the communications pattern, e.g. - frequency of data readings - frequency of communicating with server (hourly, daily …) Setting the Power Save Mode parameters - how often will an idle device do an periodic update?

## Slide 6: High level requirements
Which DM capabilities might be in scope?
DM capability | NB-IoT examples
Firmware update | Likely in scope: - bug fix, security updates over active life of device Likely out of scope: - change in system technology (Rel-13 to 5G) Occasional ‘large file’ should be supported by NB-IoT RAN. Server needs to take into account device constraints (memory, storage). Likely we try to minimise the use of this.
Software component update | Capabilities to update a component of the device OS.
Diagnostics | A toolkit of capabilities to manage an uncommunicative or faulty device, e.g. - restart device Some diagnostics might be part of standard reporting, e.g. battery level.
Lock and wipe | Ability to remotely disable and protect data in the device.

## Slide 7: High level requirements
Furthermore, LPWA-specific use cases might require additional objects for service/asset management
Such LWM2M objects could be defined either by OMA or by IPSO Alliance

## Slide 8: Challenges
There are new constraints and challenges for an application layer solution running over LPWA e.g. NB-IoT:
Data rate - for battery constrained devices, we need to adapt to work using 200 bytes per day
Security - where is it most effective to apply this?
- e.g. customer may encrypt their data at source
- e.g. transport layer security (DTLS) could be applied UE and Application server?
varying characteristics - power: some will be constrained by battery; others will have mains
of NB-IoT device - mobility: some may highly physically mobile (tracking device); others static
- some may change their characteristics with time, e.g. a stolen television becomes mobile…
> might lead to configuration profiles for different device classes
integration into NB-IoT - opportunity to integrate DM components e.g. at SCEF? or PDN–GW? Or ?
architecture

## Slide 9: NB-IoT and LWM2M
LWM2M as the integrated solution for NB-IoT devices for
device management
extraction of application data from device
initiating control commands to the application.

## Slide 10: LWM2M optimizations and enhancements
  LWM2M meets the constraints of LPWA communications, however, further optimizations might be possible for e.g. NB-IoT. This work is part of LWM2M 1.1.
  LWM2M over non-IP transport needs to be defined
  LWM2M security concept to be reviewed and possibly enhanced looking at 3GPP SA3 and IETF work (e.g. DICE)
  LWM2M device management functionality to be enhanced (e.g. switching transport modes)
  Some considerations one these areas are given on the following slides.

## Slide 11: Work area 1: LWM2M over non-IP transport
  Considerations:
  We should consider work being done on SMS over CoAP, and DTLS over CoAP
  3GPP is discussing whether a new segmentation mechanism should be designed. How would this interwork with CoAP blockwise transfer?
  Are there any limitations for CoAP transport over IP for NB-IoT?

## Slide 12: Work area 2: LWM2M security improvements
  Considerations:
  LWM2M security concept needs to be reviewed and possibly enhanced looking at 3GPP SA3 and IETF work.
  For NB-IoT every byte counts, thus multiple encryption layers should be avoided where possible (e.g. network layer plus E2E security)
  IETF DICE to reduce the DTLS handshake overhead?
  Can IETF ACE play a role too?

## Slide 13: Work area 3: LWM2M device management enhancements
  Considerations – possible additional DM functions
  Switching NB-IoT transport modes (IP, non-IP, SMS)
  Frequency change
  File mgmt object e.g. to download simple configuration file
  What else do we need?

## Slide 14: Timeline for LPWA work in LWM2M 1.1
  Candidate Approval for LWM2M 1.1 is currently planned for March 2017
  market demands much earlier completion of NB-IoT related optimizations
  Target: aim at completion of LWM2M 1.1 LPWA work by June 2016
  This target could be supported by having either informal or formal interim meetings e.g. in March and June 2016

## Slide 15: Next steps
  Start discussion and work on the 3 work areas. Are there additional work areas?
  Find volunteers to support the work.
  Agree on formal/informal interim meeting in March

## Slide 16: backup

## Slide 17: LWM2M byte count example 1
Retrieving whole LWM2M „Device“ object (incl. manufacturer info, device type, model number, serial number, hardware version, firmware/software version, power status, memory status, ...):
- LWM2M payload 121 bytes (with TLV encoding)
- CoAP header 4 bytes
Note: For basic request/response interactions no Token field is required. For messages of the LWM2M Information Reporting Interface (with observe function) a Token field (+8 bytes) would be required.
- DTLS security (estimation): 29 bytes Assumption: 13 bytes (reference, RFC 6347) of header + 16 bytes of integrity check for CoAP in DTLS [RFC 6655] . Cipher suite mandated by CoAP (AES-128)
- UDP header: 8 bytes
- IP header: 4 bytes (with IP header compression)
Total: 166 bytes

## Slide 18
Retrieving battery level
LWM2M payload 3 bytes (TLV encoding)
CoAP header 4 bytes
Note: For basic request/response interactions no Token field is required. For messages of the LWM2M Information Reporting Interface (with observe function) a Token field (+8 bytes) would be required.
- DTLS security (estimation): 29 bytes Assumption: 13 bytes (reference, RFC 6347) of header + 16 bytes of integrity check for CoAP in DTLS [RFC 6655] . Cipher suite mandated by CoAP (AES-128)
- UDP header: 8 bytes
- IP header: 4 (with IP header compression)
Total: 48 bytes
LWM2M byte count example 2