## Slide 1: OMA-LWM2M-2016-0013R01-INP_LWM2M Object Versioning LWM2M Objects Versioning
Submitted To: OMA-DM
Date: 2016 February 25th
Availability: Public OMA Confidential
Contact: Thierry GARNIER, thierry.garnier@gemalto.com
Mohammed DADAS, mohammed.dadas@orange.com
Source: Gemalto N.V
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: LWM2M Objects Versioning
Scope
  This contribution aims at addressing questions to support the evolution & fixes of LWM2M Objects Specification in the LWM2M Life Cycle
Context
  Several categories of LWM2M objects are organized per IDs range (OMA registry)
      OMA Objects
          [0..7] Core Spec TS.10 Objects
          [8..1023] Extra Core Spec TS 1.0 Objects
      SDO Objects
          [2048-2099(?)] oneM2M Objects
          [3200-3399(?)] IPSO Objects
          [3400-10240] others Objects
      Vendor Objects
          [ 10241-32768 ] (1 allocated)
    Note : it should be natural of having rules for allocating range of objects IDs per organization (SDOs, Vendors)

## Slide 3: LWM2M Objects Versioning
Identified issues
  Once the LWM2M TS 1.0 Enabler was approved (target is mid 2016), any fix (including Objects in [0..7] range) will impact the LWM2M Enabler versioning (note : no rule for LWM2M versioning defined yet)
  LWM2M Objects evolution & fixes could be handled by creating/duplicating objects (so new IDs) but it’d raise up others issues :
        OMNA registration will contain (quasi-)redundant objects (duplicated functionality) without semantic links in between
        no answer for addressing Core Spec object fixes (ID change)
        Risk of IDs usage inflation
        SDOs / vendors prefer to allocate objects IDs within their own range (instead of having chaotic IDs registration)
  Still no way to link LWM2M Enabler version and Object specification (compatibility issue)

## Slide 4: LWM2M Objects Versioning
Luckily LWM2M provides mechanisms for easing Object evolution
  adding or removing an optional resource in an object specification is supported by design
    during registration, LWM2M Client is able to register an Object Instance to the Server in providing its optional Resources
    with Discover command, the Server can discover the optional resources of an Object Instance in a given Client
However there are cases for which enhancing/fixing a given object is impacting
    adding or to removing mandatory resources
    turning a resource from optional to mandatory one, or the reverse
    modifying a resource datatype
    modifying the multiple/single characteristic of an object or a resource
  => All theses modifications can lead to backward compatibility issues.
  (out-of-date LWM2M element - Server or Client - has no way to be aware of )

## Slide 5: LWM2M Objects Versioning
Use case I :
Context : Object X has been fixed according to one of the above conditions
    (e.g a mandatory resource has been added)
  Issue : only the LWM2M Client or the LWM2M Server is out-of-date regarding the Object X :
      the registration phase maybe performed without reporting any issue
      in the best case, Server operation related to Object X on a LWM2M Client, will be treated as a bad request (e.g. mismatch of mandatory resources when Creating Object Instance)
      in the worst case Client could badly misinterpret the command payload.
=> At least, the Client/Server relation must be aware that Object X has an issue

## Slide 6: LWM2M Objects Versioning
Use case II : LWM2M Enablers support backward compatibility : what about the Objects vs Enabler compatibility ?
  A new Client based on LWM2M 1.1 Enabler, is supposed to fully support LWM2M 1.0 protocol and then to be addressable by a LWM2M 1.0 based Server
  => a LWM2M 1.0 Server must be aware if a Client is using Objects with incompatible features (i.e. implementing pure LWM2M 1.1 features) or not.
  Note : it is realistic to imagine a LWM2M 1.1 based Client using LWM2M 1.0 based Objects only

## Slide 7: LWM2M Objects Versioning
Use case III : LWM2M Objects maintenance
Operation: fix of a given object (e.g. object 11 / APN) according to the policy rules defined previously (e.g. the data type of a resource has been changed / fixed).
Context : My customer is using LWM2M Cellular Connectivity capability in his LWM2M Client - objects ID 10 and 11 are used . This LWM2M Client can be addressed by 2 Servers (Short ID 100 & 101); in this multi-server context, an ACL Object (ID 2) must be instantiated to implement the customer Object Access Control Policy.
2 views :
    Explicit Object versioning: as depict in 2016-0013-INP & CR [2015-0066R04] )
    Implicit Object versioning: in using creation & registration of a new Object ID (e.g. ID:128) to replace Object ID:11

## Slide 8: LWM2M Objects Versioning
View 1 : Explicit Object versioning for fixing object ID:11 (CR [2015-0066R04])
  Connectivity Object specification update (Objects ID10,11,12,13) : new revision of that Object ID:11 is e.g. “1.0.a”. No impact elsewhere in the specification
  Customer Specifications Update : the documents has to refer Object ID:11 new revision
  LWM2M Client update : during registration phase the LWM2M Client must inform the Server of the new version of the fixed Object ID:11 (also for discover command)
    e.g. REGISTER ep=nodename, </10/0>, </10/1>, </11> ;over=”1.0.a”, </11/0> …..

## Slide 9: LWM2M Objects Versioning
View 2 : Implicit versioning for fixing object ID:11 (creation & registration of a new object e.g. ID:128)
According to the “no Object versioning” view, there is still a need to fix the data type change issue.
  a new Object – e.g. ID 128 – must be created to replace the to-be-fixed Object e.g. ID 11/APN.
Side-effect impact of a fix according to View 2
    ID usage inflation brings confusion : what is the relation between ID:11 & ID:128 ?
  Connectivity Object specification update (object 10, 11,12, 13) :
    => update related to object ID:11 need to introduce the replacement of ID:11 by ID:128
          => APN in the spec has now to be referenced by ID:128 instead of ID:11
  In the LWM2M Client, fixing Object ID:11 by Object ID:128, means modifying all the objects referencing this object ID:11 : i.e. ACL object instances and cellular Object Instances (see below)
  => all references to ID:11 must be changed into ID:128) (heavy process, source error ..)

## Slide 10: LWM2M Objects Versioning
View 2 : Side effects
AC OI | O ID | OI ID | R I ID | Def Val | ACO | Description
2/0 | 10 | 1 | 2/100 | 0x000F | 100 | Srv (100) has full rights. (R,W,E,D)
 |  |  | 2/101 | 0x000F | 100 | Srv (101) has full rights. (R,W,E,D)
2/1 | 11 128 | 0 | 2/100 |  | 100 | 
2/2 | 11128 | 1 | 2/100 |  | 100 | 
2/3 | 10 | 0 | 2/100 | 0x000F | 101 | Srv (101) has full rights. (R,W,E,D)
 |  |  | 2/101 |  | 101 | 
2/4 | 11128 | 2 | 2/101 |  | 101 | 
2/5 | 11128 | 3 | 2/101 |  | 101 | 
…… |  |  |  |  |  | 
….. |  |  |  |  |  | 
…… |  |  |  |  |  | 
Figure 1 : change in the Customer ACL Object content specification & LWM2M Client/Device
AC OI : Access Control Object Instance
O ID : Object ID
OI ID : Object Instance ID
R I ID : (ACOI) ACL Resource Instance ID
ACO : Access Control Owner (Short Server ID)

## Slide 11: LWM2M Objects Versioning
View 2 : Side effects
Resource Name | Resource ID | Resource Instance ID | Value | Notes
Activated Profile Names | 4000 | 0 | 12811:0 | Operator1 internet
 |  | 1 | 12811:1 | Operator1
SMSC address | 0 |  | +61415011501 | 
Module activation code | 2 |  | *98 | Application will prefix this to first AT command to module for activatin of module.
Resource Name | Resource ID | Resource Instance ID | Value | Notes
Activated Profile Names | 4000 | 0 | 12811:2 | Operator2 internet
 |  | 1 | 12811:3 | Operator2
SMSC address | 0 |  | +61415011520 | 
Module activation code | 2 |  | *85 | Application will prefix this to first AT command to module for activatin of module.
Figure 2 : change in Connectivity Object 10 Instance 0,1 referring instances of Object ID:11
Object Instance 10 Instance 1 : Cellular Network Connectivity
Object 10 Instance 0 : Cellular Network Connectivity

## Slide 12: LWM2M Objects Versioning
Conclusions
  Use Case I shows that not supporting Object versioning leads to issues
  Use Case II shows that LWM2M Objects and Enabler must be compatible to work together
  Use Case III shows that simply replacing one ID Object by a new one, is not a so light process
  Object versioning strategy must be present from LWM2M initial Enabler for preventing compatibility issues with Objects evolution (fixes , not supported features..)
Specification of LWM2M Objects Versioning within LWM2M Enabler
    definition of a set of rules governing Objects versioning
    definition of standard way to inform a LWM2M Server of Objects (specific) version
    definition of a way to correlate LWM2M Objects and Enabler versions
LWM2M Objects Versioning proposal : OMA-DM-LightweightM2M-2015-0066R04-CR_Object_Versioning
    Object version is indicated to Server during Object registration and in response to the Discover command as part of the usual CoRE Links Format list e.g : ep=nodename, <2/0>;over=”X”
    when Object is in initial version, no information has to be provided (current & default situation) e.g : ep=nodename, </3/0>
    Object version must also indicate the compatibility with the earliest LWM2M Enabler version supporting that object