## Slide 1: LWM2M Software/Firmware Updates
Hannes Tschofenig

## Slide 2: CoAP
CoAP, as defined in RFC 7252 was not designed for transmission of large payloads.
Since the CoAP header itself does not contain length information the UDP length header is used instead. The maximum UDP datagram size is limited to ~64 KB.
Transmitting data beyond the (path) MTU size will, however, lead to inefficiency because of IP fragmentation and fragmentation at the adaptation layer.
Selected references about IP fragmentation:
  Kent, Mogul, “Fragmentation Considered Harmful”
  Mathis, Heffner, Chandler, ”Fragmentation Considered Very Harmful”
Firmware images can, however, easily be larger than 64 KB.

## Slide 3: Proposal #1: Block-wise Transfer
Introduce Block-wise Transfer in LWM2M v1.0 for the use of large payloads.
https://tools.ietf.org/html/draft-ietf-core-block-19
Advantage:
  Document close to publication as an RFC
  Small implementation overhead
  Runs over UDP
Disadvantage:
  Less efficient than CoAP over TCP/TLS

## Slide 4: Proposal #2: CoAP over TCP/TLS
Introduce CoAP over TCP/TLS in LWM2M v1.0 for the use of large payloads.
Advantage:
  Supports larger payload sizes (up to 32-bits in length)
  Uses features of TCP for efficient transport
Disadvantage:
  Still a working group document and currently being re-written
  Larger implementation overhead than block-wise transfer