## Slide 1: OMA-DM-LightweightM2M-2016-0048-INP_data_model_extensions_for_LPWA LWM2M LPWA new objects/resources
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE
AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.
Date: 1 May 2016
Availability:
Public
OMA Confidential
Contact: Friedhelm Rodermund rodermund@vodafone.de
Source: Vodafone
X

## Slide 2: Introduction
LWPA is a new breed of networks dedicated to IoT
Given that LWPA networks and devices provide new kinds of radio interfaces, and given that LWPA will enable new use cases
-> additional management capabilities will be needed for device management and service enablement
Some initial suggestions on the following slides

## Slide 3: Possible enhancements (1/3)
Configure transport mode e.g. for Narrowband-IoT (NB-IoT): IP, non-IP, SMS
Configure frequency band of LPWA device (tbc)
Separate PLMN-list object incl. priorities – to enable PLMN-list management and update on the device for manual PLMN selection (vs. automatic PLMN selection)

## Slide 4: Possible enhancements (2/3)
Support for configuration of 3GPP timers for NB-IoT at the application layer:
  Periodic tracking area update
  Minimum periodic search timer
  Active timer (used with PSM – how long to stay in idle before going into PSM)
“kill switch” – to disable the device from attempting to connect to the network

## Slide 5: Possible enhancements (3/3)
Enhancements to the Security Object ?
MTU size configuration e.g. to avoid performance issues when NAS payload size > max payload size on IP tunnel
Identities object: SCEF identity, IMSI, MSISDN, SCEF IP address, SCS/AS IP address
Data rate and bytes consumed and quota enforcement
Enhanced power management

## Slide 6: Next steps
  Draft the required LWM2M Objects and Resources either as new Objects or enhancements to existing Objects