## Slide 1: OMA-DM-LightweightM2M-2016-0147R01-INP Bootstrap & Multi-Servers related & unrelated Issues
Submitted To: OMA-DM
Date: 2016 October 14th
Availability: Public OMA Confidential
Contact: Thierry GARNIER, thierry.garnier@gemalto.com
Source: Gemalto N.V
7
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: BootStrap & MultiServers issues
OMA-LWM2M
TS 1.0
(reserved)
4
Recap on Server Short ID usage in LwM2M 1.0
1
2
Bootstrap Sections
Single & Multi-Servers Context
3
5
Next Steps : provision for CRs

## Slide 3: Recap on Short Server ID usage in LwM2M TS 1.0
Definition : Short Server ID is one of the LWM2M Identifier (6.3) : it uniquely identifies each LWM2M Server configured for the LWM2M Client.
  Several features around
      The identifier is assigned during the Bootstrap procedure : TS doesn’t specify if it is allocated by the Bootstrap Server or the Client
        if determined by the Bootstrap Server : adding new LWM2M Server means the Bootstrap server keep trace of the allocated Short ID
        If determined by the Client : it’s more flexible to add a new Server without having to maintain history (Bootstrap Server Replacement, Server addition) but a way to pair a Security Object Instance and the Server Object Instance must be defined
      2 specific Server Short ID values are defined/reserved (Section 6.3)
        Default Short Server ID : 0 : which is definitively not an ID for a Default Server !!!!!!
        MAX_ID : which determines the Bootstrap Server as the Owner of an Access Control Instance
        => Both are definitively not real Server Short ID
      The Server Short ID is present in the Security Object (Res ID:10) and Server Object (Res ID:0) as a link between 2 instances of that objects (beware to bootstrap consistency)
      The Server Short ID is used as Instance ID of the ACL Multi-Instance Resource (Access Control Object)
      In Multi Server Context the Server Short ID is returned in ep attribute in the Discover Command (!!)

## Slide 4: Bootstrap Section : Questions & fixes
Single & Multi Server Contexts
  Simple Device/Client could decide to support a single Server configuration only, and refuse to enter into
  a Multi Server Context (support of Control Access Objects and specific processing around).
  At least the current spec should define a clean behaviour when a Multi-Server configuration is attempting
  to be pushed by a Bootstrap Server in such a Client. [CR150]
  During the Bootstrap Phase, the process to safety link the different entities together to reach a successful configuration (Security Object, Server Object, Access Control Object) is not addressed at all. [CR150]
  In multi-server context, a current functionality should be to simply add (or remove) a LwM2M Application Server Account to (from) the Client in using the Bootstrap Interface
      such functionality is potentially available from Smartcard through the proprietary channel between the SmartCard and Device, but maybe could be better explain (or not !!)
      in using the Bootstrap Server, it should be possible to do it, with as less (history) constraint as possible (Server Short ID & Control Access Management)

## Slide 5: Bootstrap Section : Questions & Fixes
  Bootstrap Modes
    Client & Server Modes : [CR148]
      (at least) 50% of the text is redundant (Client / Server Bootstrap) and must be communalized
      distinction between persistent & non-persistent keys (beyond the nebulous meaning) doesn’t bring too much : must be simplified to address Bootstrap Server Account Replacement & Purge functionality
    SmartCard : some points have to be improved / clarified
    Examples to be fixed [CR151]
      Pushing Security Object Instances (Object 0) – on Bootstrap interface flow– should appear

## Slide 6: Single & Multi-Servers Context
Access Control Object & Management [CR152]
  Short Server ID usage & wording has to be revisited for adding simplicity and clarity
  Process of allocating such Object Instances has to be revisited
  Some examples have still to be fixed (initial Access Control Object Instance missing)
  ………..

## Slide 7: Next Steps : TS 1.0
Decisions & List of CRs to address the previous points
  Few points addressed as proposal :
    CR 148 : : Bootstrap Process rationalization
    CR 150 : Bootstrap and Configuration Inconsistencies
    CR 151 : Bootstrap Flow fixes
    CR 152 : Access Control Fixes
  Question (slide 3) on Discover (Section 5.4.2)
    If a Resource, an Object Instance, or an Object has attributes for multiple LWM2M Servers, then one link is returned for each and the ep= attribute is used to indicate the Short Server ID of the LWM2M Server. For example: if Object ID is 3 and Object Instance ID is 0, and Resource ID is 7 with two Observe operations from two Servers, then
    </3/0/7>;ep=1;dim=8;gt=50;lt=42.2, </3/0/7>;ep=2;dim=8;pmax=300;gt=80;lt=75.5
    not suitable : as a server 1 has nothing to do with infos on Server 2
    only useful (but not in that configuration) for a Bootstrap Server IF it has such an available command
    => should be removed ?
  Other points …….
2016