## Slide 1: OMA-DM-LightweightM2M-2017-0033-INP Gemalto Proposal for LwM2M enhancement
Submitted To: OMA-DM
Date: 2017 February 07th
Availability: Public OMA Confidential
Contact: Thierry GARNIER, thierry.garnier@gemalto.com
Source: Gemalto N.V
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Gemalto Proposals for LwM2M enhancement
LwM2M
1.1
3
LwM2M Bootstrap Enhancement
1
LwM2M Extended Addressing
4
LwM2M Virtual Object for Notification
2
LwM2M Compact Media Type
5

## Slide 3: 1-LwM2M Extended Addressing (1/2)
Rational : LwM2M 1.0 addressing limitation
  LwM2M resources can have multiples instances but can only be addressed as a whole (array)
  The rational should to individually address a certain Instance of an (Object Instanc) Resource
  e.g. to get the value of an individual power source maintained in the Device Id:3 Object
Proposal : extending the Object path of some LwM2M commands up to the Resource Instance ID
Illustration : Getting the value (mV) of the external battery supported by the Device Object ID:3 of a LwM2M Client
  a) LwM2M 1.0 Getting resources 6 & 7 (e.g. external battery is the second power resource instance)
  tlv: READ /3/0/6 86 06 41 00 01 41 01 02
  tlv: READ /3/0/7 88 07 08 42 00 0E D8 42 01 13 88
  b) LwM2M 1.1 Getting the value (mV) of the external battery (if any)
    Same step as before READ /3/0/6 86 06 41 00 01 41 01 02
    Ext Bat Resource is directly addressed READ /3/0/7/1 0x1388

## Slide 4: 1-LwM2M Extended Addressing (2/2)
  Impact of the proposal vs current LwM2M TS 1.0
  Bootstrap Interface : none
  Notification Interface : none
  Device Management & Service Enablement
    Read Command : Extended path / Object/ Object Instance / Resource / Resource Instance
    Discover Command : no change
    Write Command : Extended path / Object/ Object Instance / Resource / Resource Instance
    Write-Attributes command : no change
    Execute Command : no change
    Create Command : no change
    Delete command : no change

## Slide 5: 2-LwM2M Compact Media Type (1/2)
Rational : LwM2M 1.0 supports application/vnd.oma.lwm2m+json media type
  data format is structured according to SENML semantics (easy to read / timestamp support ..)
  json still too verbose compared to application/vnd.oma.lwm2m+tlv media type
  e.g : example p23 : Read /3/0 457 Bytes are returned through json Content-Format
  while only 124 Bytes are needed in using tlv Content-Format
Proposal : LwM2M 1.1 could support CBOR (RFC 7049) as an additional Media Type
=> application/vnd.oma.lwm2m+cbor media type
  data format structured according to SENML semantics is maintained
  CBOR binary coding is used instead of JSON text format : compactness gain
  => e.g : same example p23 : Read /3/0 264 Bytes are returned in using CBOR format

## Slide 6: 2-LwM2M Compact Media Type (2/2)
  Illustration p23

## Slide 7: 3-LwM2M Bootstrap Enhancement (1/2)
Rational : LwM2M 1.0 supports incremental Bootstrap but with limitations
  In LwM2M 1.0 an initial LwM2M configuration can potentially be enriched through successive Bootstrap phases in using Bootstrap-Discover command.
  However, the action of a Bootstrap-Server is still limited because of the potential lack of visibility regarding the Access Control Right already set in a LwM2M Client.
Proposal : in LwM2M 1.1 the Bootstrap-Discover command should solve the above limitation
  Bootstrap-Discover 1.0 : allows the Bootstrap-Server to get a « map » of the Objects, Object Instances and Server Short IDs supported by a certain Client
  Bootstrap-Discover 1.0 : allows the Boostrap-Server to know if a Client can support a Multi-Server context (Object Access Control ID:2).
  Bootstrap-Discover 1.1 should allow the Bootstrap-Server to get the full Access Control Right picture implemented in the Client, and then to proceed to deep configuration modifications.

## Slide 8
Illustration (cf LwM2M TS 1.0 p59)
(LwM2M 1.0) Bootstrap-Discover /
=> lwm2m:”1.1”,</0/0>,</0/1>;ssid=127,</1/0/>;ssid=127, >,</0/2>;ssid=310,</1/1/>;ssid=310 , </2/0>,<2/1>, </3/0>,</5>,</4>,
(LwM2M 1.1) Bootstrap-Discover /2 (TLV encoding)
Other impacts : none
3-LwM2M Bootstrap Enhancement (2/2)