## Slide 1: OMA-DM-LightweightM2M-2017-0060R02-INP WG LwM2M 1.1 Proposals
Submitted To: OMA-DM
Date: 2017 February 15th
Availability: Public OMA Confidential
Contact: Thierry GARNIER, thierry.garnier@gemalto.com
Source: DM WG
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: WG LwM2M 1.1 Proposals
OMA-LwM2M
1.1
Extended Addressing (Gemalto)
Bootstrap Enhancement (Gemalto)
Compact Media Type (Gemalto)
Virtual Object for Notification (Gemalto)
LoRA-LTE-M Support (ORANGE)
Secure Element Support (Gemalto, Ericsson)
WG LwM2M 1.1 Proposals

## Slide 3: 1-LwM2M Extended Addressing (1/2 Gemalto)
Rationale : LwM2M 1.0 addressing limitation
  LwM2M resources can have multiples instances but can only be addressed as a whole (array)
  The rational should to individually address a certain Instance of an (Object Instanc) Resource
  e.g. to get the value of an individual power source maintained in the Device Id:3 Object
Proposal : extending the Object path of some LwM2M commands up to the Resource Instance ID
Illustration : Getting the value (mV) of the external battery supported by the Device Object ID:3 of a LwM2M Client
  a) LwM2M 1.0 Getting resources 6 & 7 (e.g. external battery is the second power resource instance)
  tlv: READ /3/0/6 86 06 41 00 01 41 01 02
  tlv: READ /3/0/7 88 07 08 42 00 0E D8 42 01 13 88
  b) LwM2M 1.1 Getting the value (mV) of the external battery (if any)
    Same step as before READ /3/0/6 86 06 41 00 01 41 01 02
    Ext Bat Resource is directly addressed READ /3/0/7/1 0x1388

## Slide 4: 1-LwM2M Extended Addressing (2/2 Gemalto)
  Impact of the proposal vs current LwM2M TS 1.0
  Bootstrap Interface : none
  Notification Interface : none
  Device Management & Service Enablement
    Read Command : Extended path / Object/ Object Instance / Resource / Resource Instance
    Discover Command : no change
    Write Command : Extended path / Object/ Object Instance / Resource / Resource Instance
    Write-Attributes command : no change
    Execute Command : no change
    Create Command : no change
    Delete command : no change
Supporters : Gemalto*, Sierra Wireless, ARM, ORANGE
* Submitter

## Slide 5: 2-LwM2M Compact Media Type (1/2 Gemalto)
Rationale : LwM2M 1.0 supports application/vnd.oma.lwm2m+json media type
  data format is structured according to SENML semantics (easy to read / timestamp support ..)
  json still too verbose compared to application/vnd.oma.lwm2m+tlv media type
  e.g : example p23 : Read /3/0 457 Bytes are returned through json Content-Format
  while only 124 Bytes are needed in using tlv Content-Format
Proposal : LwM2M 1.1 could support CBOR (RFC 7049) as an additional Media Type
=> application/vnd.oma.lwm2m+cbor media type
  data format structured according to SENML semantics is maintained
  CBOR binary coding is used instead of JSON text format : compactness gain
  => e.g : same example p23 : Read /3/0 264 Bytes are returned in using CBOR format

## Slide 6: 2-LwM2M Compact Media Type (2/2 Gemalto)
  Illustration p23
Impact : registering a new OMA media-type to IANA
Supporters : Gemalto*, Sierra Wireless, ARM, ORANGE, ERICSSON

## Slide 7: 3-LwM2M Bootstrap Enhancement (1/2 Gemalto)
Rationale : LwM2M 1.0 supports incremental Bootstrap but with limitations
  In LwM2M 1.0 an initial LwM2M configuration can potentially be enriched through successive Bootstrap phases in using Bootstrap-Discover command.
  However, the action of a Bootstrap-Server is still limited because of the potential lack of visibility regarding the Access Control Right already set in a LwM2M Client.
Proposal : in LwM2M 1.1 the Bootstrap-Discover command should solve the above limitation
  Bootstrap-Discover 1.0 : allows the Bootstrap-Server to get a « map » of the Objects, Object Instances and Server Short IDs supported by a certain Client
  Bootstrap-Discover 1.0 : allows the Boostrap-Server to know if a Client can support a Multi-Server context (Object Access Control ID:2).
  Bootstrap-Discover 1.1 should allow the Bootstrap-Server to get the full Access Control Right picture implemented in the Client, and then to proceed to deep configuration modifications.

## Slide 8
Illustration (cf LwM2M TS 1.0 p59)
(LwM2M 1.0) Bootstrap-Discover /
=> lwm2m:”1.1”,</0/0>,</0/1>;ssid=127,</1/0/>;ssid=127, >,</0/2>;ssid=310,</1/1/>;ssid=310 , </2/0>,<2/1>, </3/0>,</5>,</4>,
(LwM2M 1.1) Bootstrap-Discover /2 (TLV encoding)
Impacts : none
Supporters : Gemalto*, ORANGE
3-LwM2M Bootstrap Enhancement (2/2 Gemalto)

## Slide 9: 4-LwM2M Virtual Object (1/3 Gemalto)
Rationale : LwM2M 1.0 Limitation
  For Notifying information (Resource) owned by separate Objects and Object Instances, there are usually 2 ways to do that :
      either by creating a specific objects which gathers all the needed resources to be notified; drawback is that Object is a) specific b) resources of the new object are redundant with resources of already present in Client: so consistency issues regarding resources values must be addressed c) the specific object created is just a collection of information and has no specific meaning (container object)
      or in letting the system to be notified by multiple individual events with the strong drawback in constraint IoT domain of wasting communication power and bandwidth (current situation)

## Slide 10
  Proposal
  Introducing the concept of Virtual Object instead of container Object aims at matching the request of reporting various information, while minimizing traffic without facing identified drawbacks : a LwM2M Virtual Object collects only references of the needed Resources of various Objects Instances concerned by the Observation.
  Main rules: - the Observation is placed on the Resource of the original Object Instance
- the Resource to Observe is registered into an virtual Object Instance
- a new <NOTIFICATION> Attribute is defined which will contain a reference to the
virtual Object Instance initiator of the subscription ……(to be continued)
4-LwM2M Virtual Object (2/3 Gemalto)

## Slide 11
  Illustration
  Observation & Notification scenario using Virtual Object Approach
      A certain Resource (e.g. Res ID:1, Device Obj ID:3) is registered on a irtual Object Instance (e.g. 30:2). A <NOTIFICATION> Attribute is set on the original Resource (vref:30:2) accordingly.
      Above identified Resource is placed under Observation through the OBSERVE /3/0/1 command.
      When notification is triggered from Res 1 of the Device Object, the full Virtual Object Instance 2 is returned in structured format e.g. application/vnd.oma.lwm2m+cbor
          Impact : Notification reporting process, new <NOTIFICATION> Attribute support, …
          No change regarding the general OBSERVE setup mechanisms
          Supporters : Gemalto*, U-Blox, ORANGE
{ "bn":"/",
"e":[
{"n":"3/0/9", "v":25, ”t”:0 },
{"n":"3/0/10", "v”:100,”t”:-10},
{"n":"5/0/3", "v":1, ”t”:-20},
{"n":"15/2/3","bv":1, "t":-50}
],
“bt”: 25462634
}
4-LwM2M Virtual Object (3/3 Gemalto)

## Slide 12: 5-LoRA-LTE-M Support (1/2) (ORANGE)
Rationale :
  In field deployments, there are as much non-ip devices as ip devices and there is a need to address all of them in the same way.
  multiple options for LPWAN are today under deployment in the field
  LwM2M is planning to cover NB-IoT only
  It is needed to cover also LoRA and LTE cat M at this stage
Proposal : LwM2M 1.1
  Extend the coverage of LPWAN to cover also LoRA and LTE-M
  Use the 3GPP SCEF interfaces when making sense and available

## Slide 13: 5-LoRA-LTE Support(2/2 ORANGE)
  Illustration
Impact : transport bindings section
Supporters : ORANGE*, Gemalto

## Slide 14: 6-Secure Element Support (1/2 Gemalto)
Rationale : in LwM2M smartCard is only used for (initial) Bootstrap
  Secure Element Support :
      superseeds and enhances the smartcard / UICC capabilities present in LwM2M 1.0 Enabler
      authorizes the LwM2M Client to really secure sensitive operations and to update crypto services in the SE (Tamper Resistant Component)
Proposal : LwM2M 1.1
  LwM2M Security Object may be located in the SE for protecting sensitive information (Keys..)
  Flexible framework to extend LwM2M Security : e.g EST key pairs on-board generation in fully Secure environment
  Sensitive Objects located in the SE may still be transparently accessed by LwM2M Server as any other LwM2M Objects
  SE administration ( new Services deploiement, key storage .. ) is handled via a specific LwM2M Object implementing the Global Platform Secure Element Remote Application Management v1.0.1 specification
  A standard API (OMAPI 3.2) may be used by the LwM2M Client to access the SE in the Device
  Bootstrap from smartCard as specified in LwM2M 1.0 can still be used (same format) with the SE and could even be simplified (PKCs#15)
  eUICC-M2M support capability (TBC)

## Slide 15: 6-Secure Element Support(2/2 Gemalto)
  Illustration
Impact : SE is optional and LwM2M TS 1.0 backward compatibility is maintained
Supporters : Gemalto*, Ericssson, ORANGE