## Slide 1: OMA-DM-LightweightM2M-2017-0066-INP_virtual_object_and_Information_reporting Proposal for Virtual Object and Information Reporting Improvements in LwM2M 1.1
Submitted To: DM
Date: 27 Jan 2017
Availability: Public OMA Confidential
Contact: Mojan Mohajer, mojan.mohajer@u-blox.com
Source: u-blox
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Observing Multiple Resources Across Different Objects
Rationale : LwM2M 1.0 Limitation
  LwM2M v1.0 Information Reporting Interface does not adequately support means of consolidating notifications from client into a single message when multiple resources in different objects are observed and meet notify criteria.
    Client either has to generates multiple notify messages to the server which is not efficient for a power constrained device or
    Data model needs to be modified to group resources into a single object that can be observed as highlighted in Section 4.3.2 of GSMA White Paper, CLP.18-Device Management and Service Enablement for Mobile IoT Devices. This has the undesired effect of duplicating resources and unnatural grouping of them in arbitrary objects

## Slide 3: Observing Multiple Resources Across Different Objects
Proposal
  Define a generic virtual object type with resources that provide links to individual resources of instances of one or more concrete objects. This is similar in principle to Linked Batch collection of resources as defined in draft-ietf-core-interfaces-07 and will support
    Dynamic addition and removal of a resource link to the virtual object instance
    Resource links inherit observe parameters of the actual resources that they point at if already set up (TBD)
    In multi server environment a virtual object instance can only be accessed by the server that created it
    Virtual object instance will support FETCH method where LwM2M server can indicate
      Individual observe condition for each linked resource, gt, lt, st, etc.
      Notify Trigger Condition: All resources meeting observation criteria (AND operation), Any (OR operation)
      Scope of resources to include in Notify in case of OR operation: All resources within virtual object instance, Qualified resources (only resources that meet notify condition). If no condition is placed on the resource it will always be included
    Fetch on virtual object will take precedence over any existing observation on the resources pointed to by the virtual object instance that were previously set up by the same server, i.e. observing server should not be sent individual notifications from the resources if virtual object notification has already provided the information. (TBD)

## Slide 4: Observing Multiple Resources Across Different Objects
Proposed Object & Description
Proposed Resource Description
Name | ID | Instances | Mandatory | URN
Virtual | nn | Multi | Optional | urn:oma:lwm2m:oma:nn
ID | Name | Operation | Instances | Mandatory | Type | Description
0 | Add New | E | Single | Mandatory |  | Adds a new resource
1 | Remove | E | Single | Mandatory |  | Removes an existing resource
2 | Resource Count | R | Single | Mandatory | Integer | 
3 | Resource Reference | R | Multiple | Mandatory | Resource Link | List of resources pointed to by this instance of virtual object

## Slide 5: Observing Multiple Resources Across Different Objects
Example Use Case
  Client supporting Connectivity Monitoring Object (Object id=4) and IPSO Temperature Sensor ( Object id= 3303) as well as the mandatory OMA LwM2M objects.
  At the service layer, the server requires notification when
    Measured temperature value exceeds a set threshold, or once a day (gt=32.1; pmax=86400)
  At the DM level, the server requires the following information based on simple rules
    Signal strength included in every notify message from client
    Battery level to be reported based on st, lt, pmin and pmax observation parameters such as
      Notify the server when it drops below a certain level or
      Notify the server when there is a significant step change, e.g. st=3, that may indicate unusual activity/condition or security threat?
      Notify the server at least once a week and at most once a day; this assumes service layer notifications are generated at least once a week or more often

## Slide 6
Observing Multiple Resources Across Different Objects
Illustration
  Server messages to create virtual object and set up observe for the example use case on the previous slide
    Create (nn)
    Execute /nn/0/0 (/3303/0/5700, /3/0/9, /4/0/2)
    CompositeObserve /nn/0 ({“bn”:”/”,
    “e” [
    {“3303/0/5700”, “gt”:32.1, “pmax”:86400},
    {“3/0/9”, “st”:3, “lt”:30, “pmin”:86400, “pmax”:604800}
    {“4/0/2”}
    ]
    })
  .

## Slide 7: Observing Multiple Resources Across Different Objects
Impact
  New data type, resource link
  New Observe method to map to FETCH, draft-ietf-core-etch-04, which can potentially specify notification condition for each resource link in the virtual object
Supporters: u-blox, Gemalto, Orange, ….