## Slide 1: LwM2M v1.1 – Upgrading the client
Rationale : During the upgrade of the LwM2M client, several requests and conditions are being foreseen for ease of use, in order to increase the interoperability standards in this part of the feature, it needs to be more formal and possibly precise.
Proposal : Following requirements to be covered in the upgrade area
  Differntiate firmware vs software
  State preserved firmware upgrade
    for storing the state for surviving upgrade, Appendix E1, E2, E3, E5, E6 to be safeguarded
  reverting back to previous firmware, a recovery possibility
    Older states (of previous requirement) before firmware upgrade should be retained for reverting back to older firmware

## Slide 2: LwM2M v1.1 – Upgrading the client
Illustration :
  Section to elaborate on firmware vs software
  Earlier discussions yielded a object which is survived by firmware upgrade for providing the needed functionality of preserving the states on upgrade
  Reverting to the old firmware can be done using same object which survived the firmware upgrade procedure to store essentials for reverting back to older functionality
  Bootstrap mechanisms can access the object which survives the crash
  LwM2M server(s) could have access to the object though specific mechanisms to understand the presence of the object during starting handshake.

## Slide 3: LwM2M v1.1 – Upgrading the client
Impact :
  Bootstrap Interface :
  Notification Interface :
  Device Management & Service Enablement
Supporters for contribution : Nokia, Gemalto?, Ublox?, ARM?...