## Slide 1: OMA-DM-LightweightM2M-2017-0074R02-INP_Aggregation_of_DM_and_service_data Proposal for Aggregation of DM and service data for data synchronization in LwM2M 1.1
Submitted To: DM
Date: 21 March 2017
Availability: Public OMA Confidential
Contact: Ada, xiaoyang.xiao@Huawei.com
Source: Huawei
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Aggregation of DM and service data for data synchronization
Rationale : LwM2M 1.0 data synchronization limitation
  There’s a requirement for constrained devices to synchronize their data in a more efficient way especially when using the Cellular IoT bearers, e.g. NB-IoT, EC-MTC, LTE-M to save the battery power and the network bandwidth.
  The data synchronization mechanism from LwM2M Client to LwM2M Server is now using Get or Observe/Notify, which only support to synchronize a data within an Object or an Object Instance or a Resource, and can’t synchronize the resources that belong to different Objects.
  Usually the DM related resources and service data are defined in different objects. For example, for a smart water meter, the Battery Level resource is defined in Object Device by OMA and the Total Flow Value is defined in a 3rd-party Object. When the meter sync its Battery Level and Total Flow Value periodically, it needs at least 2 messages exchange. This is not efficient for the network bandwidth as well as the sleep cycle because of a longer wakeup.
  One way to resolve the issue mentioned above is to register a 3rd-party Object in OMNA which contain both DM and service data. However, there’s no dynamic configuration of the resources in an registered object in LwM2M 1.0 and all the changes have to go to OMNA. It brings a large amount of maintenance works.
Proposal : LwM2M 1.1 should solve the above limitation
  A new object should be registered for data sync.
  The resources to be synchronized can be configured in the data sync object dynamically.
  This Data Aggregation object should support multiple instances, each instance represents a single resource in an existing object that can contain device management resource or service resource.

## Slide 3: Aggregation of DM and service data for data synchronization
Illustration:
  The resource definition of the data sync object could be like this:
  1. Assume the Data Aggregation object ID is 100, and we create one Data
  Aggregation object instance
  2. Configure the DM data Battery Level from /3/0/9 to the first pair of name/value.
  3. Configure the service data Fill Level from /3000/0/1 to the second first pair of
  name/value.(assume the service object ID is 3000)
  4. Retrieve the Data Aggregation object using GET method, to get both DM and
  service data in a single message
ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description
0 | Name | RW | multiple | Mandatory | String |  |  | The resource defined in another object. For example, when it refers to the ‘Battery Level’ resource in the ‘Device’ Object, this data name should be /3/0/9
1 | Value | RW | multiple | Mandatory | Opaque |  |  | The data value relates to the data name. For example, if the value in /3/0/9 then this value maybe 30, which means 30%. And the sequence of the “value” resource instances is the same as the the sequence of the “name” resource instances which relate to the “value” resource instance.
Name | Object ID | Instances | Mandatory | Object URN
Data Aggregation | 100? | multiple | Optional | urn:oma:lwm2m:oma:100?

## Slide 4: Aggregation of DM and service data for data synchronization
Impact :
  A new object(Data Aggregation ) and its related resources should be added in LwM2M 1.1.
  The servers using this new object should obey the ACL rules.
Supporters: Huawei/Neul