## Slide 1: 1-LwM2M Extended Addressing (1/2)
Rationale : LwM2M 1.0 addressing limitation
  LwM2M resources can have multiples instances but can only be addressed as a whole (array)
  The rational should to individually address a certain Instance of an (Object Instanc) Resource
  e.g. to get the value of an individual power source maintained in the Device Id:3 Object
Proposal : extending the Object path of some LwM2M commands up to the Resource Instance ID
Illustration : Getting the value (mV) of the external battery supported by the Device Object ID:3 of a LwM2M Client
  a) LwM2M 1.0 Getting resources 6 & 7 (e.g. external battery is the second power resource instance)
  tlv: READ /3/0/6 86 06 41 00 01 41 01 02
  tlv: READ /3/0/7 88 07 08 42 00 0E D8 42 01 13 88
  b) LwM2M 1.1 Getting the value (mV) of the external battery (if any)
    Same step as before READ /3/0/6 86 06 41 00 01 41 01 02
    Ext Bat Resource is directly addressed READ /3/0/7/1 0x1388

## Slide 2: 1-LwM2M Extended Addressing (2/2)
  Impact of the proposal vs current LwM2M TS 1.0
  Bootstrap Interface : none
  Notification Interface : none
  Device Management & Service Enablement
    Read Command : Extended path / Object/ Object Instance / Resource / Resource Instance
    Discover Command : no change
    Write Command : Extended path / Object/ Object Instance / Resource / Resource Instance
    Write-Attributes command : no change
    Execute Command : no change
    Create Command : no change
    Delete command : no change
    ACL : Extended path / Object/ Object Instance / Resource / Resource Instance
Supporters : Gemalto*, Sierra Wireless, ARM, ORANGE
* Submitter