## Slide 1: OMA-DM-LightweightM2M-2017-0083-INP_Proposal_group_multicast_communication Proposal for group multicast communication in LwM2M 1.1
Submitted To: DM
Date: 21 March 2017
Availability: Public OMA Confidential
Contact: Ada, xiaoyang.xiao@Huawei.com
Source: Huawei
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Progress on group multicast communication
Rationale :
  LwM2M 1.0 cannot support group multicast communication for common management or control to multiple targets in groups,
    e.g. a LwM2M server needs to send multiple messages to get the value of the software version of one software installed on several devices, or to deliver the same firmware package to several devices, which will increase network traffic used in the constrained network;
  Such unicast communication mechanism would increase the communication cost for the constrained network
Proposal
LwM2M 1.1 supports group multicast communication based CoAP group communication which uses IP multicast as specified in [RFC7390]
  Support the ability to manage a set(group) of End-devices
  Support the ability to send command or data to the group of End-devices
  Defined a Group Multicast object to capture the mapping between the IP multicast address, local member object/resource and the fanOutPoint (virtual) of the multicast request.

## Slide 3: Progress on group multicast communication
Illustration:
  Example Use Case 1: member object don’t support multiple object instance.
  A firmware is installed on three lights in the same building , and the firmware Object (object id = 5) is created, i.e. /5/0 on light A, /5/0 on light B, /5/0 on light C;
  LwM2M server wants to get the firmware Version(resource id = 7) from the three lights before performing actual firmware update.
  LwM2M server creates a Group Multicast object on each lights to trigger this device to join an IP multicast group and to listen to the IP multicast message associated with the IP multicast address:
LwM2M server
LwM2M client 1(A)
LwM2M client 2（B）
LwM2M client 3（C）
R
R
R
R
  POST coap://50
  POST coap://50
  POST coap://50
  POST coap://50
Req: POST coap://50/
Payload:
{“bn”:” /50”,
“e”:[
{“n”:”0”,”sv”:” 224.0.1.3:24”}, ]
} Note: 224.0.1.3:24 is the IP multicast address

## Slide 4
LwM2M server
LwM2M client 1(A)
LwM2M client 2(B)
LwM2M client 3(C)
R
R
R
R
  Req: GET coap://5/0/7
  HOST URI : 224.0.1.3:24;
  Req: GET coap://5/0/7
  HOST URI : 224.0.1.3:24;
  Req: GET coap:///5/0/7
  HOST URI : 224.0.1.3:24;
  Req: GET coap:// 5/0/7
  HOST URI : 224.0.1.3:24;
  LwM2M Server reads firmware version by using one multicast GET message from all three lights in the multicast group.
Progress on group multicast communication
  Req: GET coap://5/0/7
  HOST URI : 224.0.1.3:24;

## Slide 5: Progress on group multicast communication
Illustration:
  Example Use Case 2: object supports multiple object instance.
  A control software is installed on three lights in the same building, and the Software Component Object associated with this control software (object id = 14) is created, i.e. /14/0 on light A, /14/2 on light B, /14/1 on light C;
  LwM2M server wants to get the software Component Version(resource id = 2) from the three lights before performing actual software update.

## Slide 6: Progress on group multicast communication
Req: POST coap://50/
Payload:
{“bn”:”/50/0”,
“e”:[
{“n”:”0”,},
{“n”:”1”,”sv”:”/14/0/5”}
(/14/2/5 or /14/1/5 if the receiver is light B or light C )
{“n”:”2”,”sv”:” 224.0.1.3:24”},]
} Note: the object instance id is assigned by LwM2M server.
LwM2M server
LwM2M client 1(A)
LwM2M client 2（B）
LwM2M client 3（C）
R
R
R
R
  POST coap://50
  POST coap://50
  POST coap://50
  POST coap://50
  LwM2M server creates a Group Multicast object on each lights to trigger this device to join a IP multicast group and to listen to the IP multicast message associated with the IP multicast address and to provide a fanOutPoint to LwM2M server:

## Slide 7
LwM2M server
LwM2M client 1(A)
LwM2M client 2(B)
LwM2M client 3(C)
R
R
R
R
  Req: GET coap://50/0/0
  HOST URI : 224.0.1.3:24;
  Req: GET coap://50/0/0
  HOST URI : 224.0.1.3:24;
  Req: GET coap:// 50/0/0
  HOST URI : 224.0.1.3:24;
  Req: GET coap:// 50/0/0
  HOST URI : 224.0.1.3:24;
  LwM2M Server reads the Component Version of the control softwares by using one multicast message from all three lights in the multicast group.
  LwM2M Server sends the multicast GET message:
  After LwM2M client receiving the multicast GET request, each light device (LwM2M client) find the localMemPath according the /50/0/0 and replaces the /50/0/0 with the localMemPath (e.g. /14/0/2), then gets the value (of /14/0/2) and returns to LwM2M Server
Progress on group multicast communication
  Replace 50/0/0 with /14/0/2
  Replace 50/0/0 with /14/2/2
  Replace 50/0/0 with /14/1/2
  Req: GET coap://50/0/0
  HOST URI : 224.0.1.3:24;

## Slide 8: Progress on group multicast communication
Proposed Object & Description:
ID | Name | Operations | Instances | Mandatory | Type | Description
0 | fanOutPoint | RWE | Single | optional | virtual | When this resource is accessed, the client shall replace the requested path with LocalMemPath, and then enhance the request
1 | LocalMemPath | RW | multiple | optional | string | path of the member on this client：objectID/objectInstanceID[/resourceID]
2 | multicastAddress | RW | Signle | Mandatory | string | IP multicast address : port associated with the multicast group, and when client create this object instance, this device shall join this IP multicast group
Name | Object ID | Instances | Mandatory | Object URN
Group Multicast | 50? | multiple | Optional | urn:oma:lwm2m:oma:50?
Note: When the object of the member supports multiple object instance, the Group Multicast object instance ID must be assigned by the server to make sure they are same on each device in the multicast group, to provide a same path to LwM2M server by the fanOutPoint resource.

## Slide 9: Progress on group multicast communication
  The relationship between the LwM2M Gateway group and the group multicast in this proposal
  The LwM2M Gateway group capability needs an intermediate device to get the message from the distance LwM2M server to the group and forward the message to the devices in the group. In the smart home, there is often a home gateway connected a few devices.
  The group multicast capability in this proposal can, based on IP multicast, make the LwM2M server directly send the message to the devices in the group without an intermediate device. In the 3GPP network, e.g. the LwM2M server communicates with NB-IoT devices without other LwM2M entity deployed between them.
  The two solution is complementary: the gateway group is suit for the scene LwM2M server accesses the device(LwM2M client) indirectly, and the group multicast is suit for the scene LwM2M server can only access the device(LwM2M client) directly.
Group message
Multicast message

## Slide 10: Progress on group multicast communication
Impact :
  LwM2M server needs to maintain the multicast group information locally
  a new resource type – virtual
  Both LwM2M server or LwM2M client need to support the CoAP group multicast as specified in [RFC7390]
  A mechanism is needed to make sure that LwM2M server can assign the same object instance id for Group Multicast object on the different device/client, for example,
  discover before the creation of the Group Multicast every time, and choose an available id or
  Divide the object instance id into two kinds, i.e. 0…3000 is reserved for object assigned by LwM2M client, 3001…6000 is reserved for object assigned by LwM2M server. When the LwM2M server wants to create Group Multicast object at first time, it can get the available number in the 30001…6000 from the set of devices, choose 3001…3050 for itself, and tell the client to record this information, the 3001…3050 shall not be used by other LwM2M servers, or
  Other method?
Supporters : HUAWEI