## Slide 1: OMA-DM-LightweightM2M-2017-0096-INP LwM2M Logging Event Framework
Submitted To: OMA-DM
Date: 2017 March 28th
Availability: Public OMA Confidential
Contact: Thierry GARNIER, thierry.garnier@gemalto.com
Source: Gemalto N.V
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: LwM2M Logging Event Framework
Rationale :
  Logging and retrieving diagnostics events is a must_to_have for any system, so namely for IoT Systems
  (OMA-DM has specific MOs, oneM2M defines specific resources …)
  In LwM2M no object implementing such capability has been defined yet (and certainly don’t need to be)
  Defining LwM2M Objects for supporting Logging Diagnostics Events Data & Mechanisms is at least questionable
Basic Proposal
  Instead of defining specific Object for answering to the Log Events problematic, a set of Re-Usable Resources could be specified for addressing such a functionality (Data type, Behaviour)
  Whatever LwM2M Object supporting that set of Reusable Resources, such an Object could potentially be turned into a specific logging events Object
  The specified Re-Usable Resources must respect in standard a mandatory behaviour, however such a behaviour may be extended to support additional functionalities specified in the definition of the Object hosting that set of Reusable resources.
  A White Paper, will explain usage of such an generic Interface (Re-usable Resources Set) for defining specific Diagnostics & Monitoring LwM2M Objects (no impact on any LwM2M Enabler release)

## Slide 3: LwM2M Logging Event Framework
  Detail proposal : OMNA (re-usable Resources) registration of a Log Event Set Interface
ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description
4010 | LogClass | R | Single | Optional | Integer | 0-255 |  | Log Event Set Interface : 1/5 Define the Log Event Class : 0:generic (default) 1:system 2:security 3:event 4:trace 5:panic [6-99]:rsv [100-255]:vendor specific
4011 | LogStart | E | Single | Mandatory |  |  |  | Log Event Set Interface 2/5 Actions: a) Start data collection(DC) b) LogStatus is set to "0"(running) c) DC is emptied(default) or extended according to arg'0' value d) DC Period is set according to arg'1' value Arguments: '0': DC emptied(=0)[default] or extended(=1) '1': set the DC Period (in sec): if=0 or absent[default] DC is stopped by LogStop action only.
4012 | LogStop | E | Single | Mandatory |  |  |  | Log Event Set Interface 3/5 Actions: a) Stop data collection(DC) b) LogStatus is set to "1"(stopped) c) DC is kept(default) or emptied according arg'0' value Argument: '0': DC kept(=0)[default]or emptied(=1)
4013 | LogStatus | R | Single | Optional | Integer | 0-255 |  | Log Event Set Interface 4/5 Data Collection process status: 0 : running 1 : stopped [2-99] : rsv [100-255] : vendor specific.
4014 | LogData | R | Multiple | Optional | Opaque |  |  | Log Event Set Interface 5/5 Read Access on that Resource returns a serialized information. Data format is given by the 1st byte of the opaque sequence: 0 : OMA-LwM2M TLV format 1 : OMA-LwM2M JSON format 2 : OMA-LwM2M CBOR format [3..99] reserved [100..255] vendor specific

## Slide 4: LwM2M Logging Event Framework
  Illustration : e.g. LwM2M Connectivity Statistics Object revisited (ID:7++)
ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description
4010 | LogClass | R | Single | Optional | Integer |  |  | Log Event Set Interface : 1/5 Define the Log Event Class : 0:generic (default) 1:system 2:security 3:event 4:trace 5:panic [6-99]:rsv [100-255]:vendor specific
4011 | LogStart | E | Single | Mandatory |  |  |  | Log Event Set Interface 2/5 Actions: a) Start data collection(DC) b) LogStatus is set to "0"(running) c) DC is emptied(default) Specific:Reset to 0 of resources 0-5 d) DC Period is set according to arg'1' value Arguments: '0': none [default] '1': set the DC Period (in sec): if=0 or absent[default] DC is stopped by LogStop action only.
4012 | LogStop | E | Single | Mandatory |  |  |  | Log Event Set Interface 3/5 Actions: a) Stop data collection(DC) b) LogStatus is set to "1"(stopped) c) DC is kept(default) Argument: '0': none [default]
4013 | LogStatus | R | Single | Mandatory | Integer |  |  | Log Event Set Interface 4/5 Data Collection process status: 0 : running 1 : stopped
4014 | LogData | R | Multiple | Optional | Opaque |  |  | Log Event Set Interface 5/5 Read Access on that Resource returns a serialized information of the Resources [0..5]. Data format is given by the 1st byte of the opaque sequence: 0 : OMA-LwM2M TLV format 1 : OMA-LwM2M JSON format

## Slide 5: LwM2M Logging Event Framework
Next Steps :
  OMA-WG DM Agreement for registering this set of re-usable resources(OMA endorsement)
  => much better than having other SDO or specific company proposing this Device Management feature
  There is no area on OMA-DM LwM2M portal for storing/consulting technical White Papers addressing LwM2M guide lines:
    CREATIOn of such an area : a) WP : Defining Diagnostics & Monitoring LwM2M Objects using the generic Logging Event Framework b) LwM2M & CoAP over TCP support ……
Supporters : Gemalto*, Huawei ..