Change Request

| Title: | Normative General Behaviour | Public OMA Confidential |
| --- | --- | --- |
| To: | LOC WG |
| Doc to Change: | OMA-LIF-ROAMPROT-V1_0_0-20031023-D |
| Classification: | 0: New Functionality 1: Major Change 2: Bug Fix 3: Clerical |
| Source: | Sebastian Kraufvelin, Nokia |
| Replaces: | n/a |

Reason for Change

In the interim meeting in Tokyo a new section for Normative General Behaviour were added to RLP. The purpose of this CR is to enhance this section further.

Impact on Backward Compatibility

None as this is a new specification.

Impact on Other Specifications

None

Intellectual Property Rights Considerations

None.

Recommendation

It is recommended that this CR is agreed and incorporated in the next revision of RLP.

Detailed Change Proposal

### <<first changed clause>>

### Quality of Position in Request Messages

Response time requirement:

TBC

Age of location information:

Location Servers may specify a requested maximum age using the max_loc_age element in a request message. This information SHOULD be used by the Location Server of the target's serving network to, for example, to determine whether a cached location estimate is sufficient. .

Accuracy of location information:

Location Servers may specify a requested accuracy using the eqop element in a request message. This information may be used by the Location Server of the target's serving network to, for example, select an appropriate location method.

Requested quality of position cannot be provided:

The behaviour of the Location Server of the target's serving network when a requested quality of position cannot be provided depends on the implementation. This Location Server MAY or MAY NOT return a location estimate even if the requested quality of position was not satisfied. Any other Location Server which only passes on the result MUST NOT change the result it received.

<<end of changed clause>>

<<next changed clause>>

## Target Identities

Location Servers MUST specify the identity of the target device in the msid element. This element allows that the target device is uniquely addressed in multiple ways including MSISDN, IMSI, IP address, etc.

All implementations deployed in a 3GPP environment MUST support the following identities:

- MSISDN

All implementations deployed in a 3GPP2 environment MUST support the following idenitities:

- TBD

All other identities allowed by the protocol MAY be supported.

<<end of changed clause>>