## Slide 1
Beyond traditional M2M to the IoT: Aggregating Disparate Data Protocols on the IoT
-Eshwar Pittampalli, Ph.D., Director, Market Development; OMA

## Slide 2: Outline
Introduction
OMA DM
OMA LWM2M
OMA GwMO
Collaboration with oneM2M
Notes: In the context of OMA device management, a Windows Mobile device can be viewed as a hierarchical tree structure where the interior nodes and leaf nodes of the tree are the device settings and the leaf node values are the device setting values. You configure the device by manipulating the nodes. You access a node by specifying a hierarchical path to the node, called the Universal Resource Identifier (URI), starting from the root.

## Slide 3
M2M to IoT- Connections:
Device to Device (D2D)
Device to Server (D2S)
Server to Server (S2S)
On top of this, if you add People (P), there are several more combinations
Disparate protocols - As a broad categorization of protocols, we see:
OMA-DM/MQTT/CoAP: a protocol for collecting device data and communicating it to servers (D2S)
XMPP: a protocol best for connecting devices to people, a special case of the D2S, since people are connected to the servers
DDS (Data Distribution Service): a fast bus for integrating intelligent machines (D2D)
AMQP (Advanced Message Queuing Protocol): a queuing system designed to connect servers to each other (S2S)
  Others: UPnP DM, TR069, ZigBee, KNX, OpenWebNet, & Bluetooth), etc.
Introduction
Beyond traditional M2M to the IoT: Aggregating Disparate Data Protocols on the IoT
Notes: DDS is a data-centric middleware standard with roots in high-performance defense, industrial, and embedded applications.
AMQP is message-centric middleware that arose from the banking industry.
MQTT: Message Queueing Telemetry Transport
XMPP: Extensible Messaging and Presence Protocol

## Slide 4: Aggregating Disparate Data Protocols on the IoT
End Devices
Smart Devices
Non OMA-DM
Resource Constrained Devices
OMA DM Protocol
OMA LWM2M Protocol

## Slide 5: OMA-DM and OMA-LWM2M
OMA DM
  Enables device customization and services configuration remotely
  Configuration and management is exposed in a Management Object(MO)within the Management Tree.
  MO can be modified by DM Commands triggering of functional behavior in the device,
  Examples include FUMO, SCOMO, etc.
OMA LWM2M
  Lightweight M2M is focused on constrained M2M devices, and is applicable to Cellular, 6LoWPAN, WiFi and ZigBee IP or any other IP based devices
  Can be combined with existing DM offerings
  OMA Lightweight M2M protocol supports both device management and service logic.
Notes: In the context of OMA device management, a Windows Mobile device can be viewed as a hierarchical tree structure where the interior nodes and leaf nodes of the tree are the device settings and the leaf node values are the device setting values. You configure the device by manipulating the nodes. You access a node by specifying a hierarchical path to the node, called the Universal Resource Identifier (URI), starting from the root.

## Slide 6: OMA DM Gateway Management Object (GwMO)-v1.1
Three different supported modes:
  Transparent Mode: The DM Gateway assists the DM Server in sending a DM Notification to the End Device(s) behind the DM Gateway
  Proxy Mode: The DM Gateway manages End Device(s) behind the DM Gateway on behalf of the DM Server over DM protocol
  Adaptation Mode: Similar to the Proxy Mode with the difference that the DM Gateway manages End Device(s) behind the DM Gateway on behalf of the DM Server over non-OMA-DM protocols (such as UPnP DM, TR069, etc.)
OMA DM GwMO (v1.0) provides a mechanism for OMA DM to manage devices indirectly, through a gateway, when:
  Direct interaction between server and client is not possible
  Device does not have a publicly routable address
  Device may be sitting behind a firewall
  Device supports a management protocol other than OMA-DM

## Slide 7: DM Gateway Adaptation Mode
Enables management of OMA DM and non-OMA DM devices behind a DM Gateway using OMA DM Server and DM Gateway pair.
Option to have adaptation functionality implemented in the management server or the Gateway.
Existing devices supporting OMA DM and new devices only supporting non-OMA DM protocol can be easily and cost-effectively managed and provisioned by the Service Provider.
Extend the use of OMA DM Server available in the Service Provider’s network without additional installations or support or cost.

## Slide 8: DM Gateway Adaptation Mode (Use case 1)
Management Authority
MNO/Energy Supplier
Home
Gateway
GSM/CDMA/3G/LTE
Zigbee
Home Area Network (HAN)
Device Management via DM Gateway
  A Zigbee Home Area Network (HAN) is composed of home appliances, e.g. Smart Meter, Air Conditioner, Programmable Communicating Thermostat (PCT)
  The Home Gateway with GSM/CDMA/3G/LTE connectivity acts as a DM Gateway. Note that many of GSM/CDMA/3G/LTE communication modules today implement OMA DM functionality.
  A Management Authority e.g. MNO or Energy Supplier configures remotely via DM protocols the HAN, then leverages that connection for demand-response, load-balancing, etc.

## Slide 9: DM Gateway Adaptation Mode (Use case 2)
Management Authority
MNO/Healthcare Service Provider
Smartphone (DM Gateway)
GSM/CDMA/3G/LTE
Weighing Scales
Bluetooth
Bluetooth
Blood Pressure Meter
Continua (CHA/PCHA)-compliant Device Management via DM Gateway
  Some weight scales, Blood-Pressure Gauges which are compliant with Continua, transfer the data over Bluetooth (or USB, NFC) but these devices don’t have GSM/CDMA /3G connectivity.
  A mobile handset with Bluetooth connectivity acts as a DM Gateway.
  A Management Authority (e.g. MNO or Health-care Service Provider) configures remotely via DM protocols the Bluetooth devices, then leverages that connection for diagnosis etc.

## Slide 10: DM Collaboration – OMA & BBF
Group Name: WG5 - MAS
Source: Tim Carey, ALU, timothy.carey@alcatel-lucent.com
Meeting Date: 2013-09-30
Agenda Item: TP#7 MAS
Slide borrowed from: http://member.openmobilealliance.org/ftp/Public_documents/DM/2013/OMA-DM-2013-0112-INP_oneM2M_OMA_BBF_collaboration.zip
Collaboration between OMA &oneM2M- Not to add any more to existing disparate protocols
Collaboration with oneM2M

## Slide 11: DM Collaboration – OMA & BBF
Discuss if we should begin to collaborate with OMA and BBF on DM Server Interaction
  -Define a framework and requirements for the interaction between the M2M Service Layer and the Device Management Layer via the ms interface
Slide borrowed from: http://member.openmobilealliance.org/ftp/Public_documents/DM/2013/OMA-DM-2013-0112-INP_oneM2M_OMA_BBF_collaboration.zip

## Slide 12: Some of the questions investigated………..
How is a M2M Service Layer Session Established?
How does the DM Server Initiate Events to the M2M Service Layer?
How are resources discovered by the M2M Service Layer?

## Slide 13: Summary
OMA is addressing:
Smart end devices with OMA-DM new revisions
  Gateway Management Object (GwMO) to support non OMA-DM protocol compliant devices
Resource constrained devices with LWM2M
Working in close cooperation with oneM2M to address evolving needs identified for various vertical applications
For more information, please visit:
RD: OMA-RD-GwMO-V1_1-20130226-C
AD: OMA-AD-GwMO-V1_1-20130625-C
TS: GwMO v1.1 main TS
OMA-TS-GwMO-V1_1-20140217-D
GwMO ZigBee MO v1.0 TS
OMA-TS-GwMO_ZigBeeMO-V1_0-20140217-D
GwMO v1.1RD:
  OMA-TP-2013-0005-INP_GwMO_V1_1_RD_presentation_for_information
GwMO v1.1 AD:
  OMA-TP-2013-0193-INP_GwMO_v1_1_AD_Presentation_for_Information

## Slide 14
Thank You!