## Slide 1: The role of standardization in m2m/iOT
London SDI, September 2014
Joaquin Prado
Director of Technical Program

## Slide 2: Who knows …
Open Mobile Alliance?
OMA Device Management?
OMA LightweightM2M?
OMA Device Management Gateway Management Object?
OMA Push?

## Slide 3: M2M / IOT Standards
Difference in standardizing M2M vs other mobile Enabler/Services
Current Standardization efforts in M2M/IoT
How the Industry will benefit from M2M Standardization
OMA Offering in M2M/IoT
Commercial DM Deployments a Global Scale

## Slide 4: Standardizing M2M VS other Mobile Services Differences
M2M/IoT characterized by Constrained Devices
  Low Cost
  Limited Processing Power
  Battery to last years
  Network variable availability
  Often low bitrate
M2M for Non-Constrained Devices
  Full IP Stack
  About limitations don’t apply
Whole M2M/IoT Ecosystem
  OneM2M (ETSI TC) is defining a Conceptual/Functional M2M/IoT Architecture Model
  OMA is collaborating with ETSI TC M2M
  Large % of billions of Devices are restricted to:
  10KB RAM, 100 KB Flash, 40 MHz

## Slide 5: M2M / IOT Standards
Difference in standardizing M2M vs other mobile Enabler/Services
Current Standardization efforts in M2M/IoT
How the Industry will benefit from M2M Standardization
OMA Offering in M2M/IoT
Commercial DM Deployments a Global Scale

## Slide 6: M2M/Iot Protocol WAR?
M2M/IoT
Internet Standards – IETF - CoAP
Small foot-print devices (10KB RAM, 100KB Flash,
8-bits microcontrollers, < 40MHz), Base on HTTP (UDP)
Mobile Standards – OMA – LWM2M
Based on CoAP
Applicable to Cellular, 6LoWPAN, WiFi, ZigBee
Data structure (Objects/Resources)
Industrial background – OASIS - MQTT
Small code foot-print
Transport layer agnostic
Mobile cross-platform
Consumer space – AllSeen Alliance - AllJoyn
Devices to discover, connect & Interact
Transport layer agnostic
Mobile cross-platform
M2M / IoT Standards – OneM2M (ETSI)
Internet Standards – IETF – 6LoWPAN
IPV6 over Low Power Personal Area Networks
Allow small foot-print sensors to communicate over IEEE 802.15.4
Other Standards efforts: oneM2M; IEEE 802.15.4 Low rate wireless personal area Network; BACNet – American Society of Heating; AMQP – Open source; DDS – Data Distributed Service – Open Source; RPL – Routing protocol low power devices; RESTful HTTP – Runs over HTTP; DASH7 – DASH7 Alliance; DTLS – IETF Security Protocol; UDP - IETF; ZigBee Pro – ZigBee Alliance; RFiD; Bluetooth

## Slide 7: M2M / IOT Standards
Difference in standardizing M2M vs other mobile Enabler/Services
Current Standardization efforts in M2M/IoT
How the Industry will benefit from M2M Standardization
OMA Offering in M2M/IoT
Commercial DM Deployments a Global Scale

## Slide 8: How the industry will benefit from standardization
IoT Ecosystems is complex & with large number of interested parties
Different type of economic & social drivers
Large number of interested parties: Private sector, Government, Standards Bodies, Academia, etc
Privacy, Data Security … of paramount importance
Currently large number of protocols covering different market needs
Standardization is NOT Innovation but creates a level-playing-field
Ensure interoperability among components
Promote proprietary deployments (Innovation) on top of standardized protocols
Allows deployment escalation

## Slide 9: … at the end
Markets will decide what standard to use …
M2M / IoT Standards consolidation and evolution & reused is already happening

## Slide 10: M2M / IOT Standards
Difference in standardizing M2M vs other mobile Enabler/Services
Current Standardization efforts in M2M/IoT
How the Industry will benefit from M2M Standardization
OMA Offering in M2M/IoT
Commercial DM Deployments a Global Scale

## Slide 11
OMA Device Management
Firmware Update
Diagnostic and Monitoring
Connectivity Management Objects
Device Capability Management Objects
  Install & update software
  Lock & Wipe Personal Data
OMA LightweightM2M
OMA Gateway Management Object
OMA Offering
in
M2M/IoT

## Slide 12: OMA Device Management (DM V2.0, V1.3)
Framework that enables remote device customization & service configuration
Two-way message protocol MO information can be modified by DM Commands
Data Model (Management Object, MO) exposes Client
configuration information to be manipulated by a Server
DM Protocol
DM Commands:
Add, Get, Replace, Delete, Exec, Alert, etc.
  DM Functions:
  Configure connectivity
  Update firmware
  Diagnose problems
  Monitor performance
  Install and update software
  Lock and wipe personal data
  Manage device capabilities
Transports
DM Protocol
DM Representation
Bindings to Transports
Application MO

## Slide 13: OMA LightweightM2M (LWM2M)
Framework for Constrained M2M IP based Devices & Networks
  6LoWPAN, WiFI, ZigBee, etc
Protocol Commands & Data Data Model
Supports Device Management & Service Logic
  Public registry of Objects & Resources
  Satisfy requirements for specific Service Logic

## Slide 14: OMA LightweightM2M (LWM2M)
Device-Server Protocol based on CoAP (IETF)
  CoAP and DTLS bound to UDP or SMS
Extensible Object & Resource Model for application semantics
  A Client has one or more Object Instances
  An Object is collection of Resources
  A Resource is an atomic piece of information
    Read, Written or Executed
  Resources can have multiple instances

## Slide 15: DM Gateway Management Object (GwMO v1.1)
OMA DM manages devices indirectly, through a gateway when:
Direct interaction between server and client is not possible
Device does not have a publicly routable address
Device may be sitting behind a firewall
Device supports a management protocol other
  than OMA-DM

## Slide 16: M2M / IOT Standards
Difference in standardizing M2M vs other mobile Enabler/Services
Current Standardization efforts in M2M/IoT
How the Industry will benefit from M2M Standardization
OMA Offering in M2M/IoT
Commercial DM Deployments a Global Scale

## Slide 17: Commercial DM Deployment on a Global Scale
OMA has achieved commercial deployment of 1.6 Billion devices implementing the Firmware Update Management Object enabler (February 2013)
Press release, May 21st 2012 – Sprint, Metrum, Tollgrade Make Smart Grid Smarter Enabling smart meters with wireless connectivity (link)
Sensinode Announces Commercial Support of OMA Lightweight M2M at Mobile World Congress, February 27th 2013 (link)
MediaTek Chooses Red Bend FOTA Software to Update #Wearables, July 1st 2014 (link)
The Connected Home Management (link)

## Slide 18: OMA LWm2M Test Event
Vodafone – OMA TestFest
Dusseldorf – Germany
8th to 11th December 2014
Free Event
Members & Non-Members

## Slide 19: Summary

## Slide 20: Summary II
M2M/IoT is characterized by Constrained Devices
  Low Cost
  Limited Processing
  Battery to last many years
  Network variable availability
  Often low bitrate
Current IoT standards emerge from different backgrounds
We are at the infancy of the IoT
More protocols to come, consolidate, merge & evolve
Markets needs will decide what to use
10KB RAM,
100 KB Flash,
40 MHz

## Slide 21: Summary II
Open Mobile Alliance has specifically designed Enablers in M2M/IoT space
  OMA Lightweight M2M (v1.0)
  OMA Device Management (v1.1.2, v1.2.1, v1.3, (v2.0 RESTful)
  OMA DM Gateway Management Object (v1.0, v1.1)
  OMA TestFest Event in collaboration with Vodafone
  Dusseldorf, 8th to 11th December – Free Event

## Slide 22: Thank You