## Slide 1: ETSI TCCE WG4 work
G. Marque-Pucheu (Airbus / ETSI TCCE WG4)
26-27/08/ 2014

## Slide 2: Schedule
First contribution on the use of LTE for TETRA evolution in December 2009
One umbrella WID ‘REN/TETRA-04180’ approuved 05/2010
Complemented by three detailled WID for three documents approved beginning of 2014
  DTR/TCCE-04186 for the architecture of the interfaces (published)
  DTR/TCCE-04187 stage 2 for the mobile to infrastructure interface (draft under discussion)
  DTR/TCCE-04188 stage 3 for the mobile to infrastructure interface (draft under discussion)
Up to now, more than 100 time-slots devoted to broadband drafting
2

## Slide 3: Status of stage 3 work
150 pages drafted
About 90% of work done for basic PTT voice services
Not started for supplementary services, dispatcher specific services, video services, IMS support and examples
Early draft due for 01/2015 – on track
3

## Slide 4: Technical assumptions
Mostly based on SIP with strict RFC compliance
  Additional broadcast messages for setup in very large group environment
Can work with and without IMS over any IP based network
  But using LTE capabilities (GCSE)
Designed to be NAT tolerant with no setup performance penalty (permanent connections)
Designed for interoperability with legacy networks – up to now digital only (TETRA, TETRAPOL, P25 phase 1 and 2)
Based on TCCE WG1 URS, but keeping track of TIA and 3GPP requirements
4

## Slide 5: Relation with OMA standards
Significant similarities with PoC but differences for some aspects related to:
  Performance
  NAT tolerance
  Native IMS independance
  Compliance with Public Safety oriented requirements
Should rely completly on OMA for Device Management and XML Document Management for service and profile management
Covers only the mobile to infrastructure interface and does not detail internal architecture
5

## Slide 6: Conclusion
Work done so far in ETSI TCCE is a signficant contribution to MCPTT work but is covering only part of the work to be done
Should be complemented by existing and to be updated OMA standards
If IMS operation is a requirement, interface compatibilty has to be verified
Work on off network operation is waiting 3GPP RAN progress, but may benefit from on network protocol architecture and from TCCE overall expertise on direct mode protocol design (TETRA DMO)
6