## Slide 1: OMA-COM-CPM-2015-00xx-INP_Interworking_and_CMS Interworking and Message Store
Submitted To: OMA-COM-CPM
Date: 05 10 2015
Availability: Public OMA Confidential
Contact: Tom Van Pelt, tvanpelt@gsma.com
Source: GSM Association
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Introduction
Presentation triggered by action point to provide solution for
  IWF-28: When a CPM Message is delivered via both CPM and non-CPM communication technologies to devices of the CPM User, the CPM Enabler SHALL ensure that each delivered message is only stored once in the network-based storage.
  IWF-29: The CPM Enabler SHALL provide the interworking information needed (e.g. the non-CPM technology used, correlation data) to support correlation of message objects stored in the CPM Message Store with the messages interworked to non-CPM technologies.
  USA-012: To avoid presenting duplicate messages to the CPM User, the CPM Enabler SHALL support the CPM User’s devices to correlate message duplicates, in case different technologies were used to deliver that message to the devices of the CPM User. Note: In some scenarios, a CPM Message can be delivered as CPM Standalone Message to a tablet and be interworked as SMS to a mobile device. When stored in the CPM Message Store, the message is stored as e.g. standalone message, so when the mobile device synchronizes with the CPM Message Store it should be able to identify that it’s the same message as the SMS and only show it to the user once.
Covers lots of other aspects as well since the use cases should be clear
Tries to cover this by going through the applicable scenarios at a high level

## Slide 3: Scenarios: introduction
Show flows for different cases
  Combination of states on originating and terminating side
Do not include direct delivery cases
  They are about interworking, not about multi-device
    Would be relevant in all scenarios where there is a primary device with special treatment
      Can potentially be reached through or send legacy messages when not having IP connectivity
      Is assumed to be the user’s main device (i.e. reaching it means reaching the user unlike on secondary devices)
  Make them more complex while not adding much value
Do not provide all detail e.g.
  No interactions with HLR
  No SIP/MSRP/MAP methods
Only include primary delivery path
  i.e. when device comes online it doesn’t gain IP connectivity and does therefore not sync with message store

## Slide 4: Scenarios: Involved Entities
The following entities are (potentially) involved when sending a message from User A to User B:
  A-Party
    Client A
    PF A
    CMS A
    IWF A
    xMS-C A
  B-Party
    Client(s) B
    PF B
    CMS B
    IWF B
    xMS-C B
Users can be in different states
  Online CPM users  Referred to as « Online user »
  CPM user that is offline, but with access to legacy messaging  Referred to as « reachable user » (short for offline, but reachable)
  CPM user that is completely offline  « Offline user » (short for offline and not reachable)
  Non-CPM user
Note: State could be different depending on device.
These different states lead to different message routing and different storage requirements

## Slide 5: Scenarios: Both Online
Primary Device A
Secondary Device A
SMS-C A
IWF A
PF A
CMS A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B

## Slide 6: Scenarios: A Online/B-Reachable
Primary Device A
Secondary Device A
SMS-C A
IWF A
PF A
CMS A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B
Notes:
All covered, except way to store information on SMS delivered to primary device B in CMS B.
  Proposal: include information in IMDN provided by IWF B to PF B (similar to info on successful result of SRI_for_SM)

## Slide 7: Scenarios: A Online/B-Primary Offline
Primary Device A
Secondary Device A
SMS-C A
IWF A
PF A
CMS A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B
Notes:
IWF-B needs to provide information on SMS to PF B/CMS B (same issue as for case where B is reachable)
Message object in CMS needs to be updated/replaced with object that contains info on SMS after delivery to primary device. No idea how that can be done with current standards…

## Slide 8: Scenarios: A online/B non-CPM
Primary Device A
Secondary Device A
SMS-C A
IWF A
PF A
CMS A
Primary Device B
Notes:
Why involve the SMS-C? With the proposed procedures for SRI_for_SM, the IWF may send directly to device B as well
No need to store anything SMS related in CMS

## Slide 9: Scenarios: A-Reachable/B-online (alt 1)
Primary Device A
Secondary Device A
SMS-C A
IWF A
PF A
CMS A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B
Notes:
IWF A needs to provide information on SMS to PF A (with headers to be stored in CMS)
  Can be part of request sent to PF (e.g. an additional body)
PF needs to route IMDN back to the IWF A which needs to convert it into an SMS delivery response
  IMDN record route might be used for the routing, but not clear how to match to open SMS transaction

## Slide 10: Scenarios: A-Reachable/B-online (alt 2)
Primary Device A
Secondary Device A
SMS-C A
CMS A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B
Notes:
Needs proprietary way to store SMSs on the A-Party side (could involve CPM infrastructure, but wouldn’t be used for routing)
Otherwise, no different from case where user A is non-CPM user

## Slide 11: Scenarios: A-Reachable/B-Reachable (1)
Primary Device A
Secondary Device A
SMS-C A
IWF A
PF A
CMS A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B
Notes:
Not really significant differences from case where B was online

## Slide 12: Scenarios: A-Reachable/B-Reachable (2)
Primary Device A
Secondary Device A
SMS-C A
CMS A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B
Notes:
SMS/IWF involved twice with different behaviour expected which may be a routing issue
  SMS from originating to terminating needs to be routed to PF (for storage, but also for delivery to secondary device)
  SMS to primary needs to be routed to device

## Slide 13: Scenarios: A-Reachable/B-Primary offline (1)
Primary Device A
Secondary Device A
SMS-C A
IWF A
PF A
CMS A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B
Notes:
Only new difficulty to A-online/B-Offline and A-Reachable/B-Reachable is the SMS deliver transaction between SMS-C A and IWF A
  If all clients would be offline that transaction still needs a response (to avoid timeouts and retries)
  A positive response because of S&F in PF B would lead to an incorrect delivery report to primary device A
  A negative response would require S&F in PF-B to be disabled
   not straightforward. Easiest would be if SMS-C A and IWF A were integrated since that avoids the transaction

## Slide 14: Scenarios: A-Reachable/B-Primary offline (2)
Primary Device A
Secondary Device A
SMS-C A
CMS A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B
Notes:
A similar issue between SMS-C A and IWF B could exist as in alternative 1 if the message cannot be delivered right away
  Here merging the IWF and SMS-C is not possible though as they might be in different networks
  Since terminating PF and IWF are in the same network it might be easier to disable S&F though and leave that to the originating SMS-C

## Slide 15: Scenarios: A-Reachable/B-non-CPM (alt 1)
Primary Device A
Secondary Device A
SMS-C A
IWF A
PF A
CMS A
Primary Device B
Notes:
SMS-C A needs to route incoming requests and responses to IWF A somehow
  Again easiest if IWF and SMS-C are integrated
  Re-routing the SMS deliver might be harder as it would require to differentiate between those messages that have passed via the CPM infrastructure and those that haven’t
  Also the routing of the responses seems hard since the SMS-C has to keep track of the source of the message

## Slide 16: Scenarios: A-Reachable/B-non-CPM (alt 2)
Primary Device A
Secondary Device A
SMS-C A
CMS A
Primary Device B
Notes:
Seems easier than alternative 1 for this use case

## Slide 17: Scenarios: A-offline
No set of scenarios since A cannot initiate sending the message
What can happen though is A going offline and changing connectivity between sending the message and the generation of delivery and/or display report
For that scenario a few generic rules are sufficient
  The delivery report has to follow the path of the original message
    A delivery report for an IP message cannot be sent over SMS/MMS
    A delivery report for legacy messaging technology might involve a legacy xMS-C depending on it
    Exceptions may be if the legacy xMS-C function is integrated with the PF/IWF and the originating client has synced with CMS already
      In that case a delivery report for a message that was sent as legacy could be delivered over IP without creating issues in the network
      Might be more complex though
  The delivery report should be stored in the CMS even if the client is offline

## Slide 18: Scenarios: A-non-CPM/B-online
Primary Device A
SMS-C A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B

## Slide 19: Scenarios: A non-CPM/B-Reachable
Primary Device A
SMS-C A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B
Notes:
No specific new difficulties for this use case
Still complex SMS routing

## Slide 20: Scenarios: A non-CPM/B-Primary Offline
Primary Device A
SMS-C A
SMS-C B
IWF B
PF B
CMS B
Primary Device B
Secondary Device B
Notes:
No specific added difficulties, but really complex SMS routing

## Slide 21: Scenarios: A Non-CPM/B Non-CPM
Out of scope 

## Slide 22: Proposals for IWF-28/IWF-29
Storage of SMS data needs an information channel between IWF and PF
  Also needed for GC use cases (hence link to IWF-26/IWF-27)
    E.g. always assigning same identity and restart by non-CPM user
  Since messaging data is interworked technology dependent, proposal is to use XML passed by IWF to PF
    Containing specific MIME and CPIM headers with the appropriate values that need to be stored for the client to be able to do the matching
    These could be included by PF when creating message object
    Additional information could be ignored by parties with only IP connectivity which could thus use the same MIME object (stored only once as per the requirement
  For messaging the channel could potentially rely on IMDN
    Only common technology between the different message delivery methods (MSRP, MESSAGE)
    Not really appropriate for other use cases
    To be aligned between the use cases
  Channel could maybe be useful to steer routing of legacy messaging
    Seems really complex which might require the IWF to have insight in the PF’s routing logic
Main issue remaining:
  What if xMS delivery happens later because primary device was offline
  In that case CMS object might have been created already upon delivery to secondary devices and IMAP does not allow to alter existing objects

## Slide 23: General conclusions
Several issues to be solved still
Legacy message routing is getting complex in some of the use cases
  Would require analysis on how the use cases can be realised
  Solution could be to leave some network internal aspects out of scope in this release of CPM
    Assumes the availability of proprietary approaches
  Would not solve everything though
The role of the SMS-C is getting quite minimal for serving CPM users
  Would it be an option to group SMS-C and IWF?