## Slide 1: OMA-DM-LightweightM2M-2015-0036R01-INP_CoAP_firewall_traversal CoAP firewall traversal
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE
AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.
Date: 17 Jun 2015
Availability:
Public
OMA Confidential
Contact: Friedhelm Rodermund
rodermund@vodafone.de
Padmakumar Subramani Padmakumar.subramani@alcatel-lucent.com
Source: Vodafone, Alcatel-Lucent
X

## Slide 2: CoAP firewall traversal - introduction
During the OMA Test Fest for LWM2M in January 2015 it was confirmed that there are limitations regarding the usage of UDP in certain scenarios.
E.g. firewalls might be configured to close the connection if no traffic is received after a short time.
There are several scenarios where this problem does’t occur, and existing measures to avoid these limitations.
Further measures and optimizations could be added to the LWM2M TS.
This documents aims at:
1) analysing the cause of these limitations
2) listing options for avoiding these limitations

## Slide 3: CoAP firewall traversal – problem description
In certain scenarios – depending on network architecture and firewall settings - it may happen that a CoAP over UDP the connection is timed out after x seconds when there is no traffic (at the Jan 2015 test fest x was 45-90 sec).
Reason is that firewalls often have a more restricitve configuration wrt UDP traffic compared with TCP
The problem may occur in the example scenarios showing different architecture options on the next slides.
There are use cases where a 45 sec connection is sufficient e.g. to transmit sensor values, and/or, because keeping the connection open could cause scalbility issues on the server side (depends on server)
However, there are also use cases where a longer or even permanent connection is desired.

## Slide 4: CoAP firewall traversal – architecture example 1
LWM2M Server
L W M 2 M / C o A P
F L O W
L W M 2 M / C o A P F L O W
L W M 2 M / C o A P
F L O W

## Slide 5: CoAP firewall traversal – architecture example 2
Gateway
Broker
LWM2M
Client
LWM2M
Client
LWM2M
Client
LWM2M
Client
LWM2M Server
PUBLIC NETWORK
P U B
S U B
P U B S U B
P U B
S U B
P U B S U B
L W M 2 M / C o A P
F L O W
L W M 2 M / C o A P
F L O W
OPERATORS NETWORK
UTILITY NETWORKS
FIREWALL @ OPERATOR NWK
FIREWALL @ UTILITY NWK
FIREWALL @ UTILITY NWK

## Slide 6: CoAP firewall traversal – Options
On the following slides various options how to avoid LWM2M firewall traversal problems are provided for discussion, enhancement and refinement within OMA DM WG

## Slide 7: CoAP firewall traversal – Option 1 recommended firewall settings for UDP incl. Queue mode
• Recommended firewall configuration for UDP …. From LWM2M TS:
• For a firewall to support LWM2M, it should be configured to allow outgoing UDP packets to destination port 5683 (other ports can be configured), and allow incoming UDP packets back to the source address/port of the outgoing UDP packet for a period of at least 240 seconds. These UDP packets may contain DTLS or CoAP payloads. When a firewall is configured as such any LWM2M Clients behind it should use Queue Mode.
• For a firewall to support LWM2M it can be configured to allow both outgoing and incoming UDP packets to destination port 5683 (other ports can be configured). These UDP packets may contain DTLS or CoAP payloads. When a firewall is configured as such any LWM2M Clients behind it are not required to use Queued Mode, but may use it for other reasons (e.g. a battery powered sleeping device).
• Any LWM2M Clients behind a NAT can use Queued Mode. There are other mechanisms to transverse a NAT, however they are out of scope for the LWM2M Enabler.

## Slide 8: CoAP firewall traversal – Option 2 LWM2M registration update
• It is possible avoiding the UDP connection time-out by setting the LWM2M registration update timer < firewall UDP time out
• Drawback: this may cause unwanted traffic

## Slide 9: CoAP firewall traversal– Option 3 IPv6
• Although CoAP does not require IPv6, it is easiest used in IP environments where devices are directly routable
• Only solves NATting but not the UDP connection time out

## Slide 10: CoAP firewall traversal– Option 4 CoAP over TCP
• CoAP over TCP support would help avoiding unfriendly firewall settings for UDP
• Dependencies : IETF drafts conclusion, CoAP over TCP
• IETF has two RFCs for this and plans to merge them:
https://tools.ietf.org/html/draft-bormann-core-coap-tcp-00
https://tools.ietf.org/html/draft-tschofenig-core-coap-tcp-tls-01
• Plan is to finalize work at the ITEF meeting this July in Praha

## Slide 11: CoAP firewall traversal– Option 5 CoAP PubSub
CoAP PubSub, in which one can create a reachable endpoint for a sensor client to push updates to, using CoAP PUT or POST; sleeping actuator clients can use GET on wakeup; would be more efficient than queue mode
(further elaboration would be useful)
Dependencies : IETF drafts conclusion, CoAP PubSub

## Slide 12
CoAP firewall traversal – Option 6 private APN
Many operators use private APNs for their enterprise customers
This is often combined with a VPN connection
In such scenarious there should not be a limitation regarding CoAP traffic, and if there is, the configuration can be done accordingly

## Slide 13
CoAP firewall traversal – Option 7 using TCP before and UDP behind gateway
Gateway scenarios are very likely in IoT – one of the advantages is the reduction of traffic over the WAN
In such scenarious an option would be using:
CoAP over TCP for gateway-server connection
CoAP over UDP for gateway-client connections
See example architecture on next slide

## Slide 14
CoAP firewall traversal – Option 7 using TCP before and UDP behind gateway
Gateway
Gateway
LWM2M
Client
LWM2M
Client
LWM2M
Client
LWM2M
Client
LWM2M Server
PUBLIC NETWORK
OPERATORS NETWORK
UTILITY NETWORKS
FIREWALL @ OPERATOR NWK
FIREWALL @ UTILITY NWK
FIREWALL @ UTILITY NWK
CoAP over TCP
CoAP over TCP
CoAP over UDP
CoAP over UDP
CoAP over UDP
CoAP over UDP

## Slide 15
CoAP firewall traversal – Option 8
• More options ?

## Slide 16: Firewall Traversal – Next steps
1) Refine findings and options
2) Add support for TCP binding to LWM2M TS (CoAP over TCP)
3) Identify and fill gaps in the TS regarding the other options