## Slide 1: OMA-DM-LightweightM2M-2015-0036RR02-INP_CoAP_firewall_traversal LWM2M firewall traversal
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE
AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.
Date: 27 Aug 2015
Availability:
Public
OMA Confidential
Contact: Friedhelm Rodermund rodermund@vodafone.de Padmakumar Subramani Padmakumar.subramani@alcatel-lucent.com
Source: Vodafone, Alcatel-Lucent
X

## Slide 2: CoAP firewall traversal - introduction
During the OMA Test Fest for LWM2M in January 2015 it was confirmed that there are limitations regarding the usage of UDP in certain scenarios.
E.g. firewalls might be configured to close the connection if no traffic is received after a short time.
There are several scenarios where this problem does’t occur, and existing measures to avoid these limitations.
Further measures and optimizations should be added to the LWM2M TS.
This documents aims at:
1) analysing the cause of these limitations
2) proposing several solutions for avoiding these limitations

## Slide 3: CoAP firewall traversal – problem description
In certain scenarios – depending on network architecture and firewall settings - it may happen that a CoAP over UDP the connection is timed out after x seconds when there is no traffic (at the Jan 2015 test fest x was 45-90 sec).
Reason is that firewalls often have a more restricitve configuration wrt UDP traffic compared with TCP. This has mainly two reasons:
UDP is a connectionless protocol and as there is no connection information the common way to close it is to idle out. Would disabling the timeout at the firewall solve the problem? No, that could cause issues as increasing these timeouts increases the number of connections which the firewall has to keep track of which e.g. increases RAM usage but could also lead to no more ports available because connnection/state table could fill up when none of the connections is being closed. -> Disabling time-out no solution but expanding the timeout could be an option

## Slide 4: CoAP firewall traversal – problem description (cont.)
Furthermore there is a potential security issue as UDP can suffer from spoofing and DOS attacks. This is another reason for not keeping the connection open infinitly.
Typical timeout values for UDP is 30 secs. Important to note that also TCP has a time-out which is often around 3600 sec.

## Slide 5: CoAP firewall traversal – problem description (cont.)
There are use cases where a 45 sec connection is sufficient e.g. to transmit sensor values, and/or, because keeping the connection open could cause scalbility issues on the server side (depends on server)
However, there are also use cases where a longer or even permanent connection is desired.
The problem may occur with „unfriendly firewalls“ as shown in example scenarios on the following slides.

## Slide 6: „unfriendly firewall“ scenario 1
LWM2M Server
L W M 2 M / C o A P
F L O W
L W M 2 M / C o A P F L O W
L W M 2 M / C o A P
F L O W

## Slide 7: „unfriendly firewalls“ scenario 2
Gateway
Broker
LWM2M
Client
LWM2M
Client
LWM2M
Client
LWM2M
Client
LWM2M Server
PUBLIC NETWORK
LWM2M/CoAP
P U B
S U B
P U B S U B
L W M 2 M / C o A P
F L O W
L W M 2 M / C o A P
F L O W
OPERATORS NETWORK
UTILITY NETWORKS
FIREWALL @ OPERATOR NWK
FIREWALL @ UTILITY NWK
FIREWALL @ UTILITY NWK
LWM2M/CoAP

## Slide 8: CoAP firewall traversal – solutions
On the following slides various options how to avoid LWM2M firewall traversal problems are provided for discussion, enhancement and refinement within OMA DM WG

## Slide 9: CoAP firewall traversal – Solution 1 recommended firewall settings for UDP incl. Queue mode
• Recommended firewall configuration for UDP …. From LWM2M TS:
• For a firewall to support LWM2M, it should be configured to allow outgoing UDP packets to destination port 5683 (other ports can be configured), and allow incoming UDP packets back to the source address/port of the outgoing UDP packet for a period of at least 240 seconds. These UDP packets may contain DTLS or CoAP payloads. When a firewall is configured as such any LWM2M Clients behind it should use Queue Mode.
• For a firewall to support LWM2M it can be configured to allow both outgoing and incoming UDP packets to destination port 5683 (other ports can be configured). These UDP packets may contain DTLS or CoAP payloads. When a firewall is configured as such any LWM2M Clients behind it are not required to use Queued Mode, but may use it for other reasons (e.g. a battery powered sleeping device).
• Any LWM2M Clients behind a NAT can use Queued Mode. There are other mechanisms to transverse a NAT, however they are out of scope for the LWM2M Enabler.
In certain scenarios the M2M/IoT service provider cannot apply the recommended firewall settings because he has not control over the firewall.

## Slide 10: CoAP firewall traversal – Solution 2 LWM2M registration update
• It is possible avoiding the UDP connection time-out by setting the LWM2M registration update timer < firewall UDP time out
• This solution works fine ... but may cause unwanted traffic

## Slide 11: CoAP firewall traversal– Solution 3 IPv6
• Although CoAP does not require IPv6, it is easiest used in IP environments where devices are directly routable
• Only solves NATting but not the UDP connection time out

## Slide 12: CoAP firewall traversal– Solution 4 CoAP over TCP
• CoAP over TCP support would help avoiding unfriendly firewall settings for UDP
• Dependencies : IETF drafts conclusion, CoAP over TCP
• IETF has two RFCs for this:
https://tools.ietf.org/html/draft-bormann-core-coap-tcp-00
https://tools.ietf.org/html/draft-tschofenig-core-coap-tcp-tls-01
• At the ITEF meeting this July in Praha it was decided to base the solution on the latter draft, however, there are still a few points under disussion (e.g. con/non mode)
In many cases this solution solves the problem, however, it has to be noted that also TCP connections have a time out which is minutes - instead of seconds with UDP. Also TCP keep-alive packets are a similar size to LWM2M UPDATE packets.

## Slide 13: CoAP firewall traversal– Solution 5 CoAP PubSub
CoAP PubSub, in which one can create a reachable endpoint for a sensor client to push updates to, using CoAP PUT or POST; sleeping actuator clients can use GET on wakeup; would be more efficient than queue mode
Dependencies : IETF drafts conclusion, CoAP PubSub
draft-koster-core-coap-pubsub
specifies the means for nodes with limited reachability to communicate using simple extensions to CoAP.
The extensions enable publish-subscribe communication using a broker node that
enables store-and-forward messaging between two or more nodes.

## Slide 14: CoAP firewall traversal– Solution 5 CoAP PubSub
The CoAP pub/sub Broker performs a store-and-forward function of state updates between certain CoAP pub/sub Clients. Clients Subscribe to state updates which are Published by other Clients, and which are forwarded by the Broker to the subscribing clients.
The clients and broker use topics to identify a particular resource or object in a publish-subscribe system. Topics are conventionally formed as a hierarchy, e.g. "/sensors/weather/barometer/pressure" or "EP-33543/sen/3303/0/5700".
The topics are hosted at the broker and all the clients using the broker share the same namespace for topics.
CoAP pub/sub Clients subscribe to topics on the Broker using the CoAP Observe operation.
Further elaboration would be needed implementation details of CoAP PubSub with firewalls.

## Slide 15
CoAP firewall traversal – Solution 6 private APN
Many operators use private/corporate APNs for their enterprise customers.
In such scenarious there shouldn‘t be a limitation regarding CoAP traffic as the APN configuration can be done individually for each customer (e.g. at GGSN/PDN-GW)

## Slide 16
CoAP firewall traversal – Solution 7 using TCP before and UDP behind gateway
Gateway scenarios are very likely in IoT – one of the advantages is the reduction of traffic over the WAN
In such scenarious an option would be using:
CoAP over TCP for gateway-server connection
CoAP over UDP for gateway-client connections
See example architecture on next slide

## Slide 17
CoAP firewall traversal – Solution 7 using TCP before and UDP behind gateway
Gateway
Gateway
LWM2M
Client
LWM2M
Client
LWM2M
Client
LWM2M
Client
LWM2M Server
PUBLIC NETWORK
OPERATORS NETWORK
UTILITY NETWORKS
FIREWALL @ OPERATOR NWK
FIREWALL @ UTILITY NWK
FIREWALL @ UTILITY NWK
CoAP over TCP
CoAP over TCP
CoAP over UDP
CoAP over UDP
CoAP over UDP
CoAP over UDP

## Slide 18
LWM2M over HTTP2 – Solution 8
Running LWM2M over HTTP2 would also solve the issue of short connection time-out as HTTP2 typically uses TCP as transport protocol
However, HTTP2-over-QUIC is also possible which then again uses UDP as transport (QUIC uses UDP)

## Slide 19
Similar limitations with MQTT?
MQTT was originally designed for usage with TCP, however, it was noted that it has two drawbacks for constrained devices:
Every MQTT client must support TCP and will typically hold a connection open to the broker at all times
MQTT topic names are often long strings which make them impractical for 802.15.4
Thus, MQTT-SN was developed to address these shortcomings which defines a UDP mapping and allows indexing topic names.
Since MQTT-SN uses UDP it is expected to run into similar limitations regarding firewall traversal (further study would be required).

## Slide 20: Firewall Traversal – recommended next steps
Add support for TCP binding to LWM2M TS (CoAP over TCP)
Add pubsub to LWM2M TS
Add new appendix to LWM2M TS explaining the UDP limitations and existing solutions