## Slide 1: OMA-DM-LightweightM2M-2015-0053R01-INP Dev Mgnt & Serv Enablement Interface Discussion for Addressing Ambiguities
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE
AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.
Date: 31 Aug 2015
Availability:
Public
OMA Confidential
Contact: Thierry GARNIER thierry.garnier@gemalto.com
Source: Gemalto N.V
X

## Slide 2: Dev Mgt & Serv Enablement Interface
Outline
LWM2M Operations in conflict
      WRITE vs EXECUTE
      READ vs DISCOVER
      WRITE vs CREATE
LWM2M WRITE : CoAP PUT and POST usage clarification
Discussion for decision !!

## Slide 3: LWM2M Operations in conflict (1/3)
LWM2M WRITE vs EXECUTE operations
(issue raised on on GitHub #29)
WRITE : POST Object ID/ Object Instance ID/Resource ID
EXECUTE : POST Object ID/ Object Instance ID/Resource ID
Answer : LWM2M Client is aware which operation is supported by a Resource : E and RW must be exclusive
So POST on a executable Resource => LWM2M EXECUTE

## Slide 4: LWM2M Operations in conflict (2/3)
READ & DISCOVER Operations
READ : Object ID[/Object Instance ID/Resource ID]
DISCOVER : Object ID[/Object Instance ID/Resource ID]
Answer : The Content-Format (which must be specified) is different for these 2 commands :
For READ Content Format will be (in short) text/opaque/tlv/json
For DISCOVER Content Format will be application/link-format
So the 2 commands READ and DISCOVER can be distinguished

## Slide 5: LWM2M Operations in conflict (3/3)
WRITE & CREATE Operations (issue raised on GitHub #29)
  WRITE POST Object ID /Object Instance ID
  CREATE POST Object ID /Object Instance ID
Same CoAP syntax for 2 LWM2M functionalities
      Critical Bug to fix ASAP
But : CREATE : POST Object ID /Object Instance ID is not really REST compatible
    the URI target should exist
Proposal :
  WRITE POST Object ID /Object Instance ID : both ID are mandatory (no modif)
  CREATE POST Object ID /Object Instance ID : The ID is allocated by the Client only
  Safe : never any conflict / Server is informed of the new ID (reponse / registration update)
Discussion / Decision ?

## Slide 6: LWM2M WRITE : CoAP PUT and POST usage clarification
WRITE : POST & PUT : common understanding required !!
        (Device & Service Enablement Interface)
TS 1.0 mentions 2 capabilities for Write :
  a) Replace: replaces the Object Instance or the Resource with new value provided in the “Write” operation.
  Partial Update: adds or updates Resources or Resource Instances provided in the new value and leaves other existing Resources or Resource Instances unchanged.
Postulats : a) and b) are related on an already instantiated Object only
Assumptions :
A1 : a) is referring to PUT operation and b) is referring to POST operation : TRUE ?
A2 : replacement in a) means : “through a TLV/JSON payload, new Resources (i.e. optional ones) could be added or removed & new resource values can be set” TRUE ?
A3 : partial update in b) means : “existing Resources/Resources Instances are kept (none can be removed), and their values may be updated ; also new Resources, & Resource instances can be added” TRUE ?
Any addition ? Limitation to add ?

## Slide 7: Conclusions/Decisions