## Slide 1: OMA-DM-LightweightM2M-2018-2018-0024-INP_extended_scenarios_for_IR001_requirement Proposal to supplement some scenarios to consummate IR001 requirement
Submitted To: DM
Date: 16 Mar. 2018
Availability: Public OMA Confidential
Contact: changhongna@Huawei.com
Source: Huawei
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Background
Requirement LightweightM2M-IR-001 provides for single observe/notify across multiple resources of the same or different objects.
Two mechanisms, both the virtual_notify_object and FETCH/PATCH methods, for reporting of resources across different objects in a single notification message had been discussed.
This contribution supplements several scenarios to consummate the LightweightM2M-IR-001 requirement, and provides some methods based the virtual_notify_object mechanism proposed in OMA-DM-LightweightM2M-2018-0018R01-INP_virtual_observe_notify_object. The other methods based the FETCH/PATCH methods will be discussed at later conference meeting.

## Slide 3: Scenario 1: Using resources as only the condition for Observation
Client with Objects
1. A LwM2M Server wish to requests notifications from the LwM2M Client to obtain the client’s location when the state of the lock is switched-off and the speed of the client exceeds a set threshold.
2. The state of switch and speed of the LwM2M Client only as a subscription condition, and do not need to be included in the notification message.
Object Name | Object ID | Number of Instances
Location | 6 | 1
IPSO On/Off Switch | 3342 | 1

## Slide 4: Implementation of Scenario 1
Client with Objects
Observe condition
  Digital Input State < 1
  Speed > 1 meter/second
Notification message
  Latitude
  Longitude
  Altitude
  Timestamp
Object Name | Object ID | Number of Instances
Location | 6 | 1
IPSO On/Off Switch | 3342 | 1
Virtual Observe Notify | 99 | 1
ObserveLinks Instances | content
/99/0/1/0 | “/3342/0/5500; lt=“1””
/99/0/1/1 | “/6/0/6; gt=“1””
ReportLinks Instances | content
/99/0/2/0 | “/6/0/0”
/99/0/2/1 | “/6/0/1”
/99/0/2/2 | “/6/0/2”
/99/0/2/3 | “/6/0/5”

## Slide 5: Scenario 2: Support AND conditions for Observation
Client with Objects
1. A LwM2M Server wish to requests notifications from the LwM2M Client to obtain the client’s location when the state of the lock is switched-off and the speed of the client exceeds a set threshold.
2. The state of switch and speed of the LwM2M Client only as a subscription condition, and do not need to be included in the notification message.
Object Name | Object ID | Number of Instances
Location | 6 | 1
IPSO On/Off Switch | 3342 | 1

## Slide 6: Implementation of Scenario 2
Client with Objects
Virtual Observe Notify Object
ObserveRelation
Used by the server to indicate the AND relationship between or among instances of ObserveLinks.
Object Name | Object ID | Number of Instances
Location | 6 | 1
IPSO On/Off Switch | 3342 | 1
Virtual Observe Notify | 99 | 1
ID | Resource Name | Operations | Instances | Type | Mandatory
0 | ObservationEnabled | W | Single | Boolean | Mandatory
1 | ObserveLinks | RW | Multiple | Corelnk | Mandatory
2 | ObserveRelation | RW | Single | String | Optional
3 | ReportLinks | RW | Multiple | Corelnk | Optional
4 | Report | R | Single | Opaque | Mandatory

## Slide 7: Implementation of Scenario 2
Observe condition
  (Digital Input State < 1) and (Speed > 1 meter/second)
Notification message
  Latitude
  Longitude
  Altitude
  Timestamp
ObserveLinks Instances | content
/99/0/1/0 | “/3342/0/5500; lt=“1””
/99/0/1/1 | “/6/0/6; gt=“1””
ReportLinks Instances | content
/99/0/2/0 | “/6/0/0”
/99/0/2/1 | “/6/0/1”
/99/0/2/2 | “/6/0/2”
/99/0/2/3 | “/6/0/5”
ObserveRelation content: “/99/0/1/0, /99/0/1/1” ---including some or all instances of ObserveLinks; or “1,2”---”1” represents the first instance of ObserveLinks.

## Slide 8: Scenario 3: Reduce redundant information of the notification message
Client with Objects
1. A LwM2M Server monitor the status of LwM2M Clients, the LwM2M Client need to report the information of the device and the status of the network connectivity to the LwM2M Server.
2. The notification includes all Resources of all Instances of Device Object and Connectivity Monitoring Object. Some Resources, such as Manufacturer (/3/0/0), Serial Number (/3/0/2), IP Addresses (/4/0/4), and so on, may not be changed, or some Resources are not changed when the notification is sent to the LwM2M Server. In other words, this notification message contains a lot of redundant information which make the cost of the message transmission increase.
Object Name | Object ID | Number of Instances
Device | 3 | 1
Connectivity Monitoring | 4 | 1

## Slide 9: Implementation of Scenario 3
Client with Objects
Virtual Observe Notify Object
ResourceFiltering
Used by the server to indicate the client whether report all instances of ReportLinks or ObserveLinks or changed instances of ReportLinks or ObserveLinks. 0 represents reporting all resources, 1 represents reporting only changed resources compared with last notification.
Object Name | Object ID | Number of Instances
Device | 3 | 1
Connectivity Monitoring | 4 | 1
Virtual Observe Notify | 99 | 1
ID | Resource Name | Operations | Instances | Type | Mandatory
0 | ObservationEnabled | W | Single | Boolean | Mandatory
1 | ObserveLinks | RW | Multiple | Corelnk | Mandatory
2 | ObserveRelation | RW | Single | String | Optional
3 | ReportLinks | RW | Multiple | Corelnk | Optional
4 | ResourceFiltering | RW | Single | Boolean | Optional
5 | Report | R | Single | Opaque | Mandatory

## Slide 10: Implementation of Scenario 3
ResourceFiltering
Used by the server to indicate the client whether report all instances of ReportLinks or ObserveLinks or changed instances of ReportLinks or ObserveLinks. 0 represents reporting all resources, 1 represents reporting only changed resources compared with last notification.