## Slide 1: OMA-DM-LightweightM2M-2018-0031-INP_vNEXT_Topics
Submitted To: OMA-DM
Date: 2018 Oct 4th
Availability: Public OMA Confidential
Contact: Padmakumar.Subramani@nokia.com
Source: DMSE WG
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Software and firmware upgrade (E&C)

## Slide 3: Usage patterns
Retail cases needs specific wait for inputs where the devices have small entry display for certain user inputs
Mission critical devices like medical applications needs device to be in ready condition before the FOTA push
Agricultural use cases like remote not-so-available

## Slide 4: Proposal in LwM2M
Device Host Identity to work with Software Management enabler for upgradation
  User input for triggering updates
  Wait for certain period and upgrade
  Device should be able to inform its readiness for SW/FW upgrade
  Indication for the downloaded SW/FW package is for the Device Host what is downloaded and should interact with points a, b and c as well
Split of automatic upgrade and present step by step approach in the states of updates
  Today it is chatty towards the server, it should be possible to know only the end result for the server not the intermediary results or status of the FOTA/SOTA

## Slide 5: Problem Description – IETF SUIT
Integrate IETF SUIT work in LwM2M SW/FW upgrade

## Slide 6: Problem Description – Multi Component
Partial download of software component and resume for that partial download to complete
Priority of the software component updates
  Optional
  Mandatory
  Immediate
Key performance indicators for the software/firmware upgrade

## Slide 7: Problem Statements
2 different objects creating confusion in the market
  Merge Firmware Update and Software Management objects in next release.
  Expect to retire Software Management and reuse Firmware Update as single object along with Software component
  Update Software Component to interact with Firmware Update
Introduction of standardization and improvements in the functioning of SwMgmt
  To add Manifest from IETF SUIT work
  Initiate single state view from server for upgrades (non-chatty mode)
Market expects more clarity on the existing software mgmt. enabler
  Enhance resource definitions to give more clarity
  Add Examples for different models to enhance the adaptation of the SwMGMT
Key Performance indicators are unavailable for SwMgmt
  Create KPIs for SwMgmt enabler

## Slide 8: Requirements - SwMgmt
The LwM2M Enabler & SwMgmt Enabler MUST create single software management/firmware upgrade ability for the market.
The SwMgmt Enabler MUST create standardized mechanisms for manifest of the upgrade process
The SwMgmt Enabler MUST provide abilities to indicate the performance of the upgrade procedures

## Slide 9: SMS Wake UP Security – T & C?

## Slide 10: Problem Description
Device can be woken up and asked to communicate to server through a SMS
  Device can be flooded with SMS’s by any one who is aware of the identity of the device, like a hacker

## Slide 11: Requirements – SMS wake up
The LwM2M Enabler MUST provide a security mechanism for LwM2M enabler messages over SMS initiated by LwM2M Server.

## Slide 12: LwM2M gateway – e restart the work from 1.1 RD

## Slide 13: Improvements to RD v1.1
LwM2M Gateway can act in the following modes (similar to OMA-DM Gateway )
Transparent: The LwM2M Gateway assists the LwM2M Server in sending a LwM2M Notification to the End Device(s) behind the DM Gateway
Proxy: The LwM2M Gateway manages End Device(s) behind the LwM2M Gateway on behalf of the LwM2M Server over LwM2M protocol
Adaptation: Similar to the Proxy Mode with the difference that the LwM2M Gateway manages End Device(s) behind the LwM2M Gateway on behalf of the DM Server over non-LwM2M protocols (such as UPnP, TR069, USP, Zigbee, Bluetooth, OMA-DM etc.)
  OMA-DM: In this mode the intention is to replace OMA-DM interface through LwM2M gateway. In order to create the commands of OMA-DM flow through LwM2M. In certain configuration cases, LwM2M could straight replace XML file configurations.

## Slide 14: Why convergence on OMA-DM – Problem Description
It is difficult to operate with 2 clients in same device, OMA-DM and OMA-LwM2M
From bootstrapping to configurations 2 different device mgmt. server need to interface to the same device
Increased certificate handling at the device
Increased certificates in the server
Different port and other operational issues with multiple application protocols
Increased vulnerabilities and security monitoring

## Slide 15: Requirements – LwM2M Gateway
The LwM2M Enabler and LwM2M Gateway Enabler MUST provide abilities to manage the end device through transparent mode, whereby LwM2M Gateway is pass through for commands on either direction
The LwM2M Enabler and LwM2M Gateway Enabler MUST provide abilities to manage the end device through proxy mode, whereby LwM2M Gateway is acting as a LwM2M server on behalf of LwM2M server
The LwM2M Enabler and LwM2M Gateway Enabler MUST provide abilities to manage the end device through adaptation mode, whereby LwM2M Gateway translates the different end device protocol as LwM2M towards the server and vice versa
The LwM2M Enabler and LwM2M Gateway Enabler MUST provide abilities to work with OMA-DM MO’s on the device side with LwM2M client

## Slide 16: MeSsage identity –C&T

## Slide 17: Problem Description
Multicast needs would make LwM2M server connection to that message gets lost in the response
The following problems are considered by the DM&SE WG as to be solved by hop by hop interactivity and may not need message ID
    LwM2M message flows might get complex moving forward with various new transports are being aimed at addition
    It could be necessary to see both beyond LwM2M Client and Application space for necessary handshakes
      Application A inside device talking through LwM2M client & server into a Entity X sitting beyond the LwM2M server.
      API translations and data model/semantic model complexities could be avoided for simple scenarios
    New initiatives like Resource Directory, LwM2M Gateway can take help of the message identity for e2e handshake

## Slide 18: Requirements – Message Identity
The LwM2M Enabler MUST provide message identity as a unique way of identifying the commands and responses.

## Slide 19: FIRMWARE UPGRADE THROUGH MBMS GROUP FOR NB-IOT through SCEF

## Slide 20
See attached FWupdate_GroupWise_for_NB-IoT-SCEF_path.pdf

## Slide 21: Requirements – FW upgrade through Group for NB-IoT through SCEF
The LwM2M Enabler MUST provide ability to manage the firmware upgrade to a group of devices through SCEF path
The LwM2M Enabler MUST support blob delivery for a group of LwM2M clients
LwM2M Enabler MUST support blob delivery for a group over unicast
LwM2M Enabler MUST support blob delivery for a group over multicast

## Slide 22: Move OBJECTS out of Core TS

## Slide 23: Requirements – Move OBJECTS out of Core TS
The LwM2M Enabler MUST only carry real essential Objects which are mandatory for functioning between LwM2M server and LwM2M client.
The LwM2M Support Enabler SHALL contain all non-core objects