## Slide 1: OMA-DM-LightweightM2M-2019-0017-INP_High_efficiency_Link_Encoding High-efficiency Object Link Encoding for LwM2M
Submitted To: DMSE
Date: 2 April 2019
Availability: Public OMA Confidential
Contact: Ari Keränen
Source: Ericsson
X
NO REPRESENTATIONS OR WARRANTIES (WHETHER EXPRESS OR IMPLIED) ARE MADE BY THE OPEN MOBILE ALLIANCE OR ANY OPEN MOBILE ALLIANCE MEMBER OR ITS AFFILIATES REGARDING ANY OF THE IPR’S REPRESENTED ON THE “OMA IPR DECLARATIONS” LIST, INCLUDING, BUT NOT LIMITED TO THE ACCURACY, COMPLETENESS, VALIDITY OR RELEVANCE OF THE INFORMATION OR WHETHER OR NOT SUCH RIGHTS ARE ESSENTIAL OR NON-ESSENTIAL.
THE OPEN MOBILE ALLIANCE IS NOT LIABLE FOR AND HEREBY DISCLAIMS ANY DIRECT, INDIRECT, PUNITIVE, SPECIAL, INCIDENTAL, CONSEQUENTIAL, OR EXEMPLARY DAMAGES ARISING OUT OF OR IN CONNECTION WITH THE USE OF DOCUMENTS AND THE INFORMATION CONTAINED IN THE DOCUMENTS.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at https://www.omaspecworks.org.

## Slide 2: Introduction
LwM2M client registration & discovery use CoRE link format to express which objects and instances client implements
Messages (list of links) can grow substantially large when device has complex functionality
Example: a device registers two instances of temperature sensors, three power meter instances, and one set point with: </3303/1></3303/2></3305/0></3305/1></3305/3></3308/1>
The "dimension" ("dim") attribute can reduce the load
  still easily dozens of bytes of registration payload
  also breaks the original CoRE link model and only works with continuous instance IDs
Discovery operations have even higher bandwidth use

## Slide 3: Proposal: Efficient Binary Link Encoding
When optimal bandwidth use is required, schema information can be used to compress link format representations highly efficiently
  Object IDs are encoded in binary and using delta-encoding
  Object instances are encoded with bit-maps
  Optional resources are given positions in bitmap based on their order; bitmap is used to indicate which optional resources are present

## Slide 4: Example
</3303/1/5700></3303/1/5601></3303/1/5602></3303/1/5605></3303/1/5701>
</3303/2/5700></3303/2/5601></3303/2/5602></3303/2/5605></3303/2/5701>
</3305/0/5800></3305/0/5801>
</3305/1/5800></3305/1/5801>
</3305/3/5800></3305/3/5801>
</3308/1/5900></3308/1/5701>
0C E7 06 33 33 02 0B 01 01 01 03 02 01
~250 bytes
13 bytes