## Slide 1: OMA-LOC-2013-0099R01-LPPe_2.0_CrowdSourcingData LPPe 2.0 Crowd Sourced Data
Submitted To: LOC
Date: 13 Sep 2013
Availability: Public OMA Confidential
Contact: Ian Blair, ian.blair@csr.com
Source: CSR
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Crowd Sourcing in LPPe 2.0
Summary
  LPPe 2.0 will support Crowd Sourced data
  Following the discussion of OMA-LOC-2013-0088, it was determined that Crowd Sourced data should use Provide Location Information messages to transfer Crowd Sourced data to the Location Server
The purpose of this presentation is to discuss the further requirements for the messaging that is used to implement the feature

## Slide 3: Crowd Sourced Data collection
  Data is collected at points in time and space, (with an estimated uncertainty). Typically these will be points at intervals (distance or time based) along a route taken by a user.
  In the following, these locations are referred to as Measurement Points
  Each Measurement Point is associated with a set of measurements of nearby positioning nodes which we will refer to as observations. An individual observation includes set of measurement values, the identity of the measured node, and any fine correction that may be required to the timing (i.e. the difference between the time of the actual measurement and the nominal time of the Measurement Point).
  Measurement points are then referenced to a location. If the absolute location is known (e.g. from a GNSS measurement) it will be an Absolute reference.
  If the location can only be inferred in relation to other Measurement Points (e.g. from MEMS) then it provides a Relative reference.
  Note that the Location of an Measurement Point may also be inferred both relative to another Measurement point AND an Absolute location.

## Slide 4: Crowd Sourced Data collection

## Slide 5: Crowd sourcing – Absolute references
Absolute references:
  An Absolute Location references a specific location in terms of real-world coordinates, together with any estimation of the uncertainty (or, a set of UE Assisted measurements of non-crowd sourced nodes, since these can also be used to derive a location and uncertainty).
  References may be locations that have been calculated by means such as GNSS, they may be explicitly surveyed points, or they may even be sets of UE Assisted Data that could be used to derive a location.
  Note that whilst it is preferable for references to be known accurately, a server can extract information from poorer references by averaging across measurements from many Ues.

## Slide 6: Crowd Sourcing - Absolute References

## Slide 7: Crowd sourcing – Relative references
Relative references:
  A Measurement Point’s location may also be estimated using a Relative reference.
  A Relative reference is represented as a displacement vector (with uncertainty) relative to another Measurement Point
  Chains of Relative references can be collected, but they can only be converted into Absolute location estimates when one or more Measurement Points in the chain can also be associated with an Absolute reference.
  As with Absolute references, Relative references don’t necessarily have to be known accurately, but higher accuracy improves performance.
Composite references
  Also, and Anchor point Location may be known relative to other Measurement points when an absolute reference becomes known. In this case a Measurement Point will be linked to both a Relative references AND a new Absolute reference.

## Slide 8: Crowd Sourcing - Relative References

## Slide 9: LPPe Procedure Mapping
LPPe procedures applicable to Crowd Sourced Data collection are:
Capability exchange
  Existing LPP / LPPe capability signalling can be extended for Crowd Sourcing by adding relevant capability parameters. (However, it should be noted that Crowd source capabilities are separate from positioning capabilities).
Configuration
  Crowd Sourced Data collection will fit the Initiation (Control Transaction) aspects of a Periodic/Triggered Location Information Transfer (see [OMA-TS-LPPe...] 5.2.2).
CS Data Collection
  Crowd Sourced Data collection will fit the data transfer (Data Transaction) and Termination aspects of a Periodic/Triggered Location Information Transfer (see [OMA-TS-LPPe...] 5.2.2).

## Slide 10: LPPe Procedure Mapping
E.g. Configuration and Data transfers

## Slide 11: LPPe Procedure Mapping
Large data sets:
  Where large amounts of data need to be transferred, Segmented Location Information Transfer ([OMA-TS-LPPe...] 5.2.4) will be required.
  Note that the resume capability in this feature permits Crowd Sourced data to be saved and sent later (when a connection has been resumed). This is highly desirable for Crowd Sourced data collection.

## Slide 12: Location Capability
  Request Location capability
    Additional Parameters
      Request capabilities for each location technology that the Server can use for Crowd Sourcing
  Provide Location capability
    Additional Parameters
      Provision of capabilities for each location technology that will provide Crowd Sourced data from the Target

## Slide 13: Request Location Information
  Additional Parameters
    List of Crowd Sourced data technologies required
    Periodicity/trigger conditions for CS data collection and reporting

## Slide 14: Provide Location Information
    Additional Parameters Required
      Extension to add multiple Crowd Sourced Measurement Point data sets to message
      Each Measurement point requires::
        Distance offset vector from reference point(s), uncertainty, time
        Optional Velocity/uncertainty wrt. reference point(s)
        Node List (Cell Ids, AP Ids, BT MAC Addresses)
        Set of observations of nearby nodes (Identities + measurements + time offsets)
        Measurements consist of signal strength measurements, and (optionally) timing (depending on positioning technology).
        With one of:
          UE Based Absolute reference:
            Reference location expressed as an absolute location
          UE Assisted Absolute reference:
            Reference location given by implication from a set of measurements (independent of Crowd Sourced measurements) that can be used by the Server to derive a Reference Position
        Or
          Relative reference
            Reference to a further Crowd Sourced data set (which can chain to others...)

## Slide 15: Separation of LI procedures
  Positioning & CS Location Information procedures
    Existing LI procedures are for positioning
    CS LI procedures are for Crowd Sourcing
  Proposal:
    To maintain separation bit is proposed that CS and Positioning LI procedure sessions should be kept separate by using their own (i.e. not mixed) transactions.
    CS options within Location Information messages can then be maintained as alternatives to existing positioning options – they are not expected to be used simultaneously within the same message.

## Slide 16: Summary and conclusion
LPPe Location Information procedures can be used to manage and transfer Crowd Sourced data
The high level changes required to permit this are summarised in the slides above.