# Change Request

| Title: | ETS of Event Log | Public OMA Confidential |
| --- | --- | --- |
| To: | DM LightweightM2M WG |
| Doc to Change: | OMA-ETS-LightweightM2M-V1_0_1-20170830-D |
| Submission Date: | 22,Sep, 2017 |
| Classification: | 0: New Functionality 1: Major Change 2: Bug Fix 3: Editorial |
| Source: | Bei(Echo) Xu, Huawei echo.xubei@huawei.com |
| Replaces: | n/a |

Reason for Change

Add new test cases to support Event Log (ObjectID: 20)

Impact on Backward Compatibility

None

Impact on Other Specifications

None

Intellectual Property Rights

Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification.  This obligation does not imply an obligation on Members to conduct IPR searches.  This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn.  Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration.  These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

Recommendation

DM WG to review and Agree this CR.

Detailed Change Proposal

Add new test case

### 6.3.7	Event Log Object (ID 20) [2000-2099]

#### 6.3.7.1 LightweightM2M-1.0-int-2000 –Control the Log Function

| Test Case Id | LightweightM2M-1.0-int-2000 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Setting the writable Resource LogStart (ID:4011) of Event Log and verifying the triggered actions produce the expected results |
| Preconditions | The Client supports the Configuration C.16 as defined in Appendix C The Client is registered with the Server in indicating the Object ID:20 |
| Test Procedure | A WRITE operation is performed by the Server to update a valid value in the Client in setting the LogStart Resource. The various Resources of this Event Log Objects must be set as expected by the Client. Normal flow: A WRITE (CoAP PUT) operation with a valid value is performed by the Server on the LogStart Resource (/20/0/4011) of the Event Log Object The Server READs (CoAP GET) the Event Log Object to get the values of the LogStart (/20/0/4011) |
| Pass-Criteria | In test step 1, the Server receives the success message “2.04” associated with the WRITE request. In test step 2, the Server receives the success message “2.05” along with the LogStart Resources values. In test step2, the queried value of LogStart resource is the same with that in Step1. |

#### 6.3.7.2 LightweightM2M-1.0-int-2001 – Querying the readable resources

| Test Case Id | LightweightM2M-1.0-int-2001 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Querying Information on the Firmware Update Object Instance for determining the current states and supported characteristics of the Client for such capability. |
| Preconditions | The Client supports the Configuration C.16 as defined in Annex C The Client is registered with the Server in indicating the Object ID:20 |
| Test Procedure | A READ operation from the Server on the EventLog Object Instance requesting TLV format has been received by the client. Normal flow: READ (CoAP GET) operation is performed on the EventLog Object Instance |
| Pass-Criteria | In test step 1 :the Server receives the success message (2.05 Content) associated to its READ request In step 1: the values returned by the Client in TLV format are consistent with the Configuration C 16 used for that test (LogStatus (ID:4013), LogClass (ID:4010), and LogData(4014)) |

Add new Appendix C.15 Binary AppData Container Configuration

C.16 Event Log Configuration

This configuration is a superset of Configuration C.1 and can be used instead; it implements the Event Log Object ID: 20 (Identity Resource with 4 Instances)

# Text boxes

{“bn”:“/”,

“e”:[

{"n":"0/0/0","sv": <LwM2M Server URI>},

{"n":"0/0/1","bv":false},

{"n":"0/0/2","v":0},

{"n":"0/0/3","sv":<PSK Identity>},  // opaque in Base64

{"n":"0/0/4","sv": <n/a>},

{"n":"0/0/5","sv": <Secret Key>},    // opaque in Base64

{"n":"0/0/10","v":1},

{"n":"1/0/0","v":1},

{"n":"1/0/1","v":86400},

{"n":"1/0/2","v":1},

{"n":"1/0/3","v":10},

{"n":"1/0/5","v":86400},

{"n":"1/0/6","bv": false},

{"n":"1/0/7","sv":"U"},

{"n":"3/0/0","sv":<Manufacturer Name>},

{"n":"3/0/1","sv":<Model Name>},

{"n":"3/0/2","sv":<Serial Number>},

{"n":"3/0/3","sv":<Firmware Version>},

{"n":"3/0/11","v":0},  {"n":"3/0/16","sv":"U"},

{"n":"20/0/4010","v":0 },

{"n":"20/0/4011","sv":"0,100" },

{"n":"20/0/4013","v":3 }

{"n":"20/0/4014","sv":”61-7C-E3-01-C1-11-00-00-05-00-60-18-18-18-0C-00-01-41-06-00-02-00-40-0C-00-00-00-00”},  // opaque in Base64

]

}

Server Object ID: 1 implements the mandatory Executable Resource ID: 8   - Registration  Update Trigger

Device Object ID: 3 implements the mandatory Executable Resource ID: 4 - Reboot