## Slide 1
OMA LwM2M in Open Hardware:
Arduino Yun
Joaquin Prado (OMA)
David Fernandez (HOPU)
Antonio Jara (HOPU)
Public | © HOP Ubiquitous S.L. 2016

## Slide 2: Why Arduino Yun?
Arduino Yun hardware: Possibilities
  WiFi and Ethernet Connectivity to interact with Internet
  (OMA Server)
  Double System (OpenWrt – Linux / LininoIO and Arduino)
    Linux for networking support (OMA Client)
    Arduino for sensing / actuation support (OMA Objects)
  Compatible with a wide range of sensor shields from Arduino
    Special edition from SeedStudio for Grove support
  Support from Arduino to Hackathons and Workshops

## Slide 3: Arduino Yun hardware: Double System
ATmega
32u4
Linino AR 9331
BRIDGE
Tx
Rx
Tx
Rx
USB
Prog.
I/O
WiFi
Eth
USB
HOST
SD
CARD
Comunicated through a “bridge” to share their resources:
  From ATmega side: Arduino ‘Bridge’ library provides several classes to use AR9331 resources (WiFi, Ethernet, SD Card, …)
  From AR9331 side: LininoIO provides access to use the ATmega resources (GPIO/ADC/PWM/I2C ports).
Two different processors available:
  ATmega: Runs Arduino Sketchs.
  AR9331: Runs Linino OS, a Linux OS based on OpenWRT.

## Slide 4: Arduino Yun hardware: Possibilities
Two possibilities to work with wakaama in Arduino Yun:
Use an Arduino LwM2M library in the ATmega which manages a wakaama client executed in the AR9331.
  wakaama client example is managed through a command line prompt.
wakaama LwM2M Client in the AR9331 using LininoIO to manage the peripherals.
  GPIO/ADC/PWM/I2C ports are connected directly to the ATmega.
All the code and guidelines availables in: https://github.com/HOP-Ubiquitous/OMA-ArduinoYun
ATmega
32u4
Linino AR 9331
BRIDGE
Tx
Rx
Tx
Rx
USB
Prog.
I/O
WiFi
Eth
USB
HOST
SD
CARD

## Slide 5: Agenda
Arduino Yun hardware: Possibilities
Arduino Yun LwM2M library (wakaama based)
Cross-compiled wakaama + LininoIO
What’s in the new OMA-ArduinoYun repository?

## Slide 6: Arduino Yun LwM2M library (wakaama based)
Library features
Oriented to common Arduino users
  Programming environment is Arduino IDE.
  They have lot of tools, library's and knowledge about manage peripherals
  Most of them have a low programming profile.
The library internally use the ‘Process’ class provided by the Arduino Yun Bridge library to manage a wakaama process executed in the AR9331.
  The ‘Process’ class provides methods to write in the process stdin and read from the process stdout.
  Library uses the command line provided by wakaama.
The users will download an Arduino library (.zip) which is imported in the Arduino IDE.
  Users will manage the peripherals and will write/read resources in/from the LwM2M Client using library functions such as ‘changeResource’ and ‘readResource’.

## Slide 7: Arduino Yun LwM2M library (wakaama based)
Library features
  The library will download and install automatically a compiled wakaama LwM2M Client in the AR9331.
    This auto-download can be disabled, so users could compile their own wakaama LwM2M Client with new/personalized objects.
Users are limited to the objects already defined/included in the wakaama client from Eclipse Foundation (https://github.com/eclipse/wakaama ).
  Users will use the ‘enableObject’ to enable specific objects they want to use.

## Slide 8: Arduino Yun LwM2M library (wakaama based)
Library state
  The development just started.
    Available at http://github.com/HOP-Ubiquitous/OMA-ArduinoYun
  Library is capable to download and execute the process successfully.
  There are problems in the communications with the current wakaama shell implementation (Slow communications through the bridge?).
  Library future work
  Fix the comunications with the wakaama shell.
  Include all posible objects (IPSO) in wakaama (disabled by default).
  Add new functions to the library:
    enableObject
    readResource
  Provide a secured wakaama client.

## Slide 9: Arduino Yun LwM2M library (wakaama based)
  Library inconvenients
  Users which desire work with personalized objects must develop them for wakaama using the cross-compiler.
    Shell scripts to improve the experience with the cross-compiler are also provided in the repository.

## Slide 10: Agenda
Arduino Yun hardware: Possibilities
Arduino Yun LwM2M library (wakaama based)
Cross-compiled wakaama + LininoIO
What’s in the new OMA-ArduinoYun repository?

## Slide 11: Cross-compiled wakaama + LininoIO
Features
Nowadays is the common way to work with wakaama client and peripherals.
Programming environment is your favorite IDE and compile the client with OpenWRT cross-compiler.
More oriented to medium and advanced Arduino users, but facilited for common users.
Inconvenients
Common users could find difficulties to work in this way.
GPIO/ADC/PWM/I2C ports are directly connected to the ATmega MCU. So it’s necessary install LininoIO into the Arduino Yun to manage GPIO/ADC/PWM/I2C from the AR9331.
  Linino wiki provides the instructions to install LininoIO (link)
Alternatives to wakaama for Arduino Yun
Why not use the Java based Leshan client?
  Lack of enough memory 

## Slide 12: Cross-compiled wakaama + LininoIO
Wakaama cross-compiling art state
Wakaama runs without problems in the Arduino Yun AR9331 processor.
LininoIO is required to manage GPIO/ADC/PWM/I2C ports
OpenWRT cross-compiler is required.
  Manel Sangoi have a wiki with the instructions to compile wakaama for Arduino Yun. (link)
    This same instructions are collected into the http://github.com/OpenMobileAlliance/ArduinoYunOMA repository.
    The repository above includes shell scripts which follow the instructions of Manel Sangoi to help users to start with this way or accelerate the work in hackathons.

## Slide 13: Agenda
Arduino Yun hardware: Possibilities
Arduino Yun LwM2M library (wakaama based)
Cross-compiled wakaama + LininoIO
What's inside of the OMA-ArduinoYun repository?

## Slide 14: What's inside of the OMA-ArduinoYun repository?
What’s inside
Collect information and tools to work with Arduino Yun and OMA LwM2M.
  ArduinoLwM2MLib: The purposed library project to introduce a wakaama based LwM2M client in the sketches.
  wakaamaCCTools: Four scripts to automatize the wakaama compilation using the OpenWRT cross compiler. Aims help to hackathon participants by accelerating their working environment preparation.
  tools: A script for fast update Arduino Yun firmware and a sketch to provide network info (Access Point name and IP) to facilitate the identification of devices in hackathon environments.
All the information regarding the tools and more can be found in the repository README.md
Repository link: http://github.com/HOP-Ubiquitous/OMA-ArduinoYun