## Slide 1: OMA-WID-0334-Enhanced Call Notification NetAPI_V1_02018014-A Work Item Document WI 0334 - Enhanced Call Notification NetAPI_V1_0
Submitted To: ARC WG
Date: 14 May 2018
Availability: Public OMA Confidential
Contact: Mohammed Dadas, mohammed.dadas@orange.com
Source: Orange
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Work Item Title and Registration Name
Work Item Title | Working Group | Registration Name | Version number
Enhanced Call Notification Network API | ARC | REST_NetAPI_EnhancedCallNotification | V1.0
Testing to be conducted
N
Notes: The Work Item Title is the formal name of the WI. The Work Item Title SHOULD be chosen so that readers can quickly grasp the general idea of the WID and easily associate it with the corresponding WID name. The Work Item Title and Registration Name SHALL NOT include version numbers. Abbreviations SHOULD be avoided. The Version refers to the version of the Enabler Release or Reference Release to be specified by the Work Item.
An example of correct WI naming:
Work Item Title Working Group Registration Name Version Name
Device Management DM DM 3.0
An example of incorrect WI naming:
Work Item Title Working Group Registration Name Version Name
Device Management 3.0 DM DM 3.0

## Slide 3: General information about the Work Item
WID Information
  WID0334 – REST_NetAPI_EnhancedCallNotification
  Link to WID
    <URL>
  Short description
    The WID will provide Enhancements to the Call Notification API adding new features and improvements
WG Handling Proposal
  ARC WG
  Use FastTrack
Status of WID socialisation:
  ARC

## Slide 4: Opportunity Statement
Voice services Architecture
  Service session & user’s services are no more anchored in one specific network domain/technology (e.g. in HSS/HLR) but managed at service level independently from underlying network technologies
  Service Logic is decoupled from network domains thanks to service oriented unitary communication functions provided over network APIs
  Service Logic may interact with devices (native function or dedicated app) through application level API over data connection. The application in device interacts with device native functions through device APIs.
  All the communication session management remains at network level (e.g. call establishment) which is handled through network signaling protocols (e.g. SIP, ISUP…)
  APIs offered by networks to the service layer are stable (not impacted by network evolutions), self-service (Web based REST APIs) and rely as much as possible on standards (e.g. OMA/GSMA network APIs)
Notes: HSS: Home Subscriber Server
HLR: Home Location Register
SIP: Session Initiation Protocol
ISUP: ISDN User Part
ISDN: Integrated Services Digital Network
OMA: Open Mobile Alliance
GSMA: GSM Association

## Slide 5: Opportunity Statement
Voice services main components/layers
  The voice service architecture relies on 2 main functional components: the Service Logic and the Service Gateway
    Note: Service Gateway relates to SCEF (Service Capability Exposure Function) as standardized by 3GPP in its Release 15 (TS 23.682) but currently limited to IOT and PCC
Notes: SCEF: Service Capability Exposure Function
3GPP: 3rd Generation Partnership Project
IOT: Internet Of Things
PCC: Policy and Charging Control

## Slide 6: Main Use Case(s)
Adding two use cases not covered in the current Call Notification API:
  UC#1: one number in multiple devices
  UC#2: multiple numbers in one device

## Slide 7: UC#1: one number in multiple devices
The Service Logic is notified of an incoming call through a "call notification" network API (e.g. OMA Call Notification NetAPI)
The establishment of the parallel call sessions to reach multiple devices is triggered by Service Logic through a "ForkCall" action response to the call direction API
The ForkCall action asks network to fork the call towards the list of devices selected by Service Logic  it is the Service Gateway (e.g. the TAS) responsibility to handle the fork itself, but the list of devices to reach is given by the Service Logic layer
The device activation and deactivation mechanisms are fully handled at Service Logic level
      Note: The action “ForkCall” isn’t part of OMA Call Notification standardized API
Call flow example: incoming voice call
IMS domain
d1
d3
A
Service Logic
service database
Service Gateway
(e.g. TAS)
NotifyCallDirection (AB)
d2
ForkCall (forkDestination= d1, d3)
(AB)
(AB(d1))
(AB(d3))
Notes: TAS: Telephony Application Server

## Slide 8: UC#1: one number in multiple devices
By using the appropriate profile settings on L2 line of user A, the call initialization is routed to the Service Gateway
The Service Logic is notified of an outgoing call through a "call notification" network API (e.g. OMA Call Notification NetAPI)
The Service Logic commands to continue the call establishment to B and sets the parameter “useIdentity” to L1 in order to force the change of displayed calling line ID towards the distant user
      Note: The parameter “useIdentity” isn’t part of OMA Call Notification standardized API
Call flow example: outgoing voice call
IMS domain
A on d2
Service Logic
service database
Service Gateway
(e.g. TAS)
NotifyCallDirection
(L2B)
Continue (useIdentity (L1))
B
(L2B)
(L1B)

## Slide 9: UC#2: multiple numbers in one device
The user B is called by user A on virtual number VB on his smartphone having the line number LB
The Service Gateway notifies the Service Logic of an incoming call addressed to VB through the "call notification" network API (e.g. OMA Call Notification NetAPI)
The Service Logic
  retrieves the association of VB and the native line number LB of user B in its Service database
  informs the application in the device that holds VB number of an incoming call from A addressed to VB using data connection
  answers with action to route the call to the line number LB
The call is routed towards LB line number in the network
The application and the device must handle the user’s experience in order to present the call as being addressed to VB instead of LB
Call flow example: Incoming voice call
addressed to second number VB
IMS domain
A
Service Logic
Service database
Service Gateway
(e.g. TAS)
NotifyCallDirection (AVB)
B
RouteCall (LB)
B called on Virtual Number VB
Incoming call from A to VB
(AVB)
(ALB)

## Slide 10: UC#2: multiple numbers in one device
The user A wants to call B using virtual number VA instead of his native line LA
The app in Device A notifies the Service Logic that the user wants to call B from VA number
The Service Logic retains the call details that the user wants to place (basically numbers of B and VA, location, …)
The call is routed towards the Service Gateway thanks to appropriate settings in user A’s profile
The Service gateway notifies the Service Logic through the "call notification" network API that an outgoing call has been placed from LA, addressed to B
The Service Logic commands to continue the call establishment to B and sets the parameter “useIdentity” to VA in order to force the change of displayed calling line ID towards the distant user
      Note: The parameter “useIdentity” isn’t part of OMA Call Notification standardized API
Call flow example: Outgoing voice call placed
using VA (LA belongs to Origin Operator)
IMS domain
B
A
Service Logic
service database
Service Gateway
(e.g. TAS)
NotifyCallDirection (LAB)
Continue (useIdentity (VA))
Outgoing call from VA to B
Call is presented to B using VA Identity
(LAB)
(VAB)

## Slide 11: UC#2: multiple numbers in one device
The user A wants to call B using virtual number VA instead of his native line LA
The app in Device A notifies the Service Logic that the user wants to call B from VA number
The Service Logic retains the call details that the user wants to place (basically numbers of B and VA, location, …) and sends back a Routing Number (RN) to the application
The call is routed towards the Service Gateway thanks to the Routing Number
The Service gateway notifies the Service Logic through the "call notification" network API that an outgoing call has been placed from LA, addressed to RN
The Service Logic changes the destination address to B and sets the parameter “useIdentity” to VA in order to force the change of displayed calling line ID towards the distant user
      Note: The parameter “useIdentity” isn’t part of OMA Call Notification standardized API
Call flow example: Outgoing voice call placed
using VA (with routing number)
A
IMS domain
B
Service Logic
service database
Service Gateway
(e.g. TAS)
NotifyCallDirection (LARN)
Route (B, useIdentity (VA))
use RN
Outgoing call from VA to B
Call is presented to B using VA Identity
(LARN)
(VAB)

## Slide 12: Problem Statement
The current Call Notification API shows some limitations and missing elements to cover the identified UCs (Cf. Annex 1: Call Notification API current version coverage).
The following enhancements and additions are needed to fulfill the requirements:
  4 new Call events to notify:
    Alerted: the called user has been alerted.
    Blocked: the call has been blocked due to user’s service settings.
    Forwarded: the call has been forwarded toward a new destination (e.g. Voice Mail).
    Transferred: an ongoing call has been transferred from a device to another device of the same user.
  1 new action to respond to Call Direction notifications:
    ForkCall: request to fork the call towards multiple devices. The list of devices to reach is passed through the forkDestination parameter
  New parameter available within Continue and Route actions:
    UseIdentity: change the Calling Line Identifier sent to the called user. The Service Logic can decide to hide the given Identity if the caller subscriber has the OIR service activated.
  New parameter available within Call Event Notification:
    DeviceID: identify the Device that has performed the Event which is reported. It could be interesting for the events Busy, NotReachable, Answer, Disconnect, CalledNumber with Calling direction and new events Alerted and Transferred.
Notes: OIR: Origin Identity Restriction

## Slide 13: How OMA can help
OMA should drive the development of the technical specification to take into account the enhancements of the OMA Call Notification API.

## Slide 14: Impacts, relationships and dependencies
State (potentially) related/impacted:
  This WID concerns an evolution of the Call Notification API adding new features ; there are no impacts on the architecture of the specification.
State potential and identified dependencies:
  Internally: OMA ARC
  Externally: <GSMA? 3GPP?>
Describe impacts on different system elements:
  None

## Slide 15: Proposed Timeline

## Slide 16: Supporting Companies
The companies supporting this work item are:
Company name | Membership type
AT&T | Sponsor
T-Mobile | Sponsor
Ericsson | Full
Nokia | Full

## Slide 17: Proposed Resources
The companies supporting this work item are proposing the following resources:
Deliverable/Role | Proposed volunteer editor/champion
Requirements Document (RD) | NA
Requirements Document Review Report (RDRR) | NA
Architecture Document (AD) | NA
Architecture Document Review Report (ADRR) | NA
Technical Specification (TS) | Mohammed Dadas, Orange
Enabler Test Requirements (ETR) | IOP WG (TBC)
Enabler Test Requirements Review Report (ETRRR) | IOP WG (TBC)
Enabler Release Definition (ERELD) | TBD
Consistency Review Report (CONRR) | TBD
WID/WISPR Champion | Mohammed Dadas, Orange
ARC Champion | NA
IOP Champion | TBD

## Slide 18: Document History
Approved Version 1.0
Date | Changes
14 May 2018 | OMA-TP-2018-0002-INP_WID_0334_Enhanced_Call_Notification_NetAPI_V1_0_for_approval
Notes: This slide records the change history of the document. Please record each Approved version and its approval date. For each Draft version, indicate the main changes made with each change request.
This slide does not need to be presented to TP.

## Slide 19: Annex 1: OMA Call Notification API current version coverage
The current OMA Call Notification API (OMA-TS-REST_NetAPI_CallNotification-V1_0-20130212-C) describe the following items:
  2 types of notifications:
    CallEvent: when the event which satisfies the specified criteria occurs, the Server notifies the Application by using POST to the specified endpoint
    CallDirection: when the event which satisfies the specified criteria occurs, the Server notifies the Application by using POST to the specified endpoint. The Application needs to respond with a decision which action to be performed
  6 Call events to notify:
    Busy: called party is busy. This value is allowed for both Call Direction and Call Notification
    NotReachable: called party is not reachable. This value is allowed for both Call Direction and Call Notification
    NoAnswer: called party doesn’t answer. This value is allowed for both Call Direction and Call Notification
    CalledNumber: a call session between two parties, a calling participant and a called participant (called number) is being attempted. This value is allowed for both Call Direction and Call Notification
    Answer: called Participant has confirmed (answered) the call. This value is only allowed for Call Notification but not for Call Direction
    Disconnected: called (or calling) party disconnected. This value is allowed for both Call Direction and Call Notification
  4 actions available to respond to Call Direction notifications:
    Route: request to (re-)route the call to the address indicated with routingAddress
    Continue: request to continue the call without any changes. This will result in normal handling of the event in the network
    EndCall: request to end the call. This will result in termination of the call. The callingParty will receive a tone or announcement
    Deferred: indicates that the action can not be determined immediately, and the decision will be communicated in a later request from the Client to the Server