## Slide 1: OMA-CD-CPNS-2010-0005-INP_Service Group Management CPNS Service Group Management
Submitted To: CD-CPNS
Date: 4th Jan. 2010
Availability: Public OMA Confidential
Contact: Sungjin Park, sungjin43.park@samsung.com
Source: Samsung
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Goal
This Input contribution provides
  The explanation on what the issue is
  The example of a group establishment in PoC
    Ad-hoc Group
    Pre-defined Group
    Ad-hoc Group with multiple groups
  Proposal on establishment of CPNS Service Group
    CPNS Requirements on Service group
    Proposed flow
  Conclusion

## Slide 3: Issues
Using XDMS in case of the establishment of CPNS Service group
  Does XDMS cover all cases in CPNS;
    Creating a service group arbitrarily?
    Creating a service group pre-defined?
  How does other Enabler uses XDMS?
  What is the ideal flow in order to satisfy CPNS Requirements on Service group?

## Slide 4: Group establishment in PoC
Ad-hoc Group (Arbitrary)
PoC Client A
PoC Server
PoC Client B
INVITE
Conf-factory-URI,
Invited members: B, C, D
Checking Invited members in INVITE
INVITE (conference URI)
INVITE (conference URI)
PoC Client C,D
OK
OK
OK (conference URI)
NOTE: INVITE is PoC Command, not XDMS.

## Slide 5: Group establishment in PoC
Pre-defined Group
PoC Client A
PoC Server
PoC Client B
INVITE
Group URI: friend
Checking Group URI in INVITE
INVITE (friend)
INVITE C, D (friend)
PoC Client C,D
OK
OK
OK
NOTE: INVITE is PoC Command, not XDMS.
GET & OK are provided by XDMS.
Group URI: friend
Member list: B, C, D
Shared XDMS
GET (friend)
OK (B, C, D)

## Slide 6: Group establishment in PoC
Ad-hoc Group with Multiple groups
PoC Client A
PoC Server
PoC Client B
INVITE
Conf-factory-URI
Invited members: B, friend (as Group URI)
Checking Invited members in INVITE & finding Group URI
INVITE (conference URI)
INVITE C, D (conference URI)
PoC Client C,D
OK
OK
OK (conference URI)
Group URI: friend
Member list: C, D
Shared XDMS
GET (friend)
OK (C, D)

## Slide 7: Remove PoC Group
PoC Client A
PoC Server
PoC Client B
BYE
PoC Session URI
Forwarding
BYE
PoC Client C,D
OK
NOTE: REFER & BYE are PoC Commands, not XDMS.
A is authorized to remove the group. (E.g., A is the originator of the group.)
BYE
OK
OK

## Slide 8: Remove member in PoC Group
PoC Client A
PoC Server
PoC Client B
REFER
REFER-To: PoC Client B; method BYE
Checking REFER-To Header in REFER
BYE
PoC Client C,D
OK
OK
NOTE: REFER & BYE are PoC Commands, not XDMS.
A,B,C,D are one group. A is authorized to remove members from the group.

## Slide 9: Analysis
Based on PoC specification,
  XDMS is used for providing group member information on the group corresponding the group uri.
  PoC uses its own commands for creating group, Inviting members, removing group and member. (e.g., INVITE, BYE)
  XDMS only provides commands regarding providing information in PoC Enabler perspectives.
  PoC Group URI
    is allocated by PoC Server, in case of Ad-hoc group
    is used as Group URI, in case of Pre-defined group

## Slide 10: CPNS Requirements on Service Group
Req. No | Requirements
CPNS-HLF-011 | The CPNS Enabler SHALL be able to create a Service Group for the PNE(s).
CPNS-HLF-012 | The CPNS Enabler SHALL be able to invite the PNE(s) for a Service Group.
CPNS- HLF-031 | The CPNS Enabler SHALL be able to remove a PNE from a Service Group.
CPNS- HLF-032 | The CPNS Enabler SHALL be able to remove a Service Group.
CPNS-HLF-036 | The CPNS Enabler SHALL be able to identify CPNS entities, PN(s) and Service Group(s).

## Slide 11: Proposed flows
Creating a Service Group & Inviting PNEs (Arbitrary) with Service Group Identity
PNE A
CPNS Server
PNE B
CREATE
Group-factory-URI,
Invited PNEs: B, C
Checking Invited PNEs in CREATE command
INVITE (Group URI)
INVITE (Group URI)
PNE C
OK
OK
OK (Group URI)
NOTE 1. This flow covers HLF-011, 012, 036.
NOTE 2. PN GW is not shown in the flow, because it only performs forwarding commands.

## Slide 12: Proposed flows
Removing a Service Group
PNE A
CPNS Server
PNE B
TEAR DOWN
Group URI
Checking Group URI in TEAR DOWN command
TEAR DOWN
TEAR DOWN
PNE C
OK
OK
OK
NOTE 1. This flow covers HLF-032.
NOTE 2. PN GW is not shown in the flow, because it only performs forwarding commands.

## Slide 13: Proposed flows
Removing a PNE from a Service Group
PNE A
CPNS Server
PNE B
EXPEL
Group URI,
To be expelled PNE: B
Checking PNE in EXPEL command
EXPEL
PNE C
OK
OK
NOTE 1. This flow covers HLF-031.
NOTE 2. PN GW is not shown in the flow, because it only performs forwarding commands.

## Slide 14: Conclusion
The CPNS Enabler needs its own commands such as CREATE, INVITE, TEAR DOWN, EXPEL.
  The command name can be changeable.
The CPNS Enabler can create a service group in a way of arbitrary.
  In addition, it is possible to create a service group with the information provided by shared group XDMS.
  However, it seems redundant to use XDMS in CPNS requirements perspective.
The proposed flow is discussed and agreed in order to incoporated into AD.