## Slide 1: OMA-CD-CPNS-2010-0016R01-INP_Service Group and Personal Network Management Introduction to PAG CPNS Service Group Management and Personal Network Introduction to PAG
Submitted To: CD-CPNS
Date: 27th Jan. 2010
Availability: Public OMA Confidential
Contact: Johan Hjelm, johan.hjelm@ericsson.com
Takayuki Warabino, ta-warabino@kddi.com
Takashi Matsunaka, ta-matsunaka@kddi.com
Yuichi Ishikawa, yi-ishikawa@kddi.com
Tet Chiba, chiba@kddi.com
Source: Ericsson, KDDI
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: What is CPNS about?
Provides application-layer support for ubiquitous access to Services in a converged network,
  which is a collection of individual networks that are interconnected by means of PN Gateway (PN GW) devices (in the example above, the cell phone assumes the role of a PN GW that converges Personal Network and WAN/cellular networks to enable video to be streamed to the PMP from a network server).
Facilitates access by devices in a PN to application or content Services that are available either locally in one or more other PNE(s), or residing in other networks, including other PNs or network elements accessed via a cellular or other WAN technology.
Allows the PNE(s) that are part of the PN to access Services outside of the PN and for those PNE(s) to offer Services to PNE(s) in other networks.
The main CPNS Enabler entities are:
  CPNS Server
  Personal Network (PN) Gateway (GW)
  PNE (Personal Network Element)
Unique features of CPNS (compared e.g. To DLNA and UPnP)
  Manages service groups – including secure distribution of data in groups
PNE
PN GW
CPNS Server

## Slide 3: Components of CPNS
PNE
PN GW
PN
Service Group
CPNS Server
XDMS
XDM-3i
XDM-1,2i
XDMC
*Note:
Whether to use XDM or not is under internal discussion in CPNS
Deployment scenario shown here is one of possible alternatives, best of which is to be advised by PAG experts.
*Note

## Slide 4: Use Case: Service Group
1. John and Steve want to play the same mobile network-game as a team using their own device respectively. So John creates a game and using his mobile as a PN GW.
2. It sends messages to invite the Steve’s game device. And Steve executes the same game connecting to the PN gateway using WPAN techniques.
Here, Johns mobile phone and Steves games device form a service group
3. PN gateway connects to the CPNS Server to make up a group to start. The CPNS Server connects to the game server to provide proper group game Service.
4. The PN device transmits its game data to the PN gateway. And the PN gateway adds on its own data together and transmits to the CPNS Server at the same time.
5. The PN gateway receives the game data of a group from the CPNS Server, and takes the data designated to itself and forwards the data designated to the PN device to its destination.
6. During the game, Steve and John can use several charging options with the help of the CPNS Server.

## Slide 5: CPNS Requirements on Service Group
Req. No | Requirements
CPNS-HLF-011 | The CPNS Enabler SHALL be able to create a Service Group for the PNE(s).
CPNS-HLF-012 | The CPNS Enabler SHALL be able to invite the PNE(s) for a Service Group.
CPNS- HLF-031 | The CPNS Enabler SHALL be able to remove a PNE from a Service Group.
CPNS- HLF-032 | The CPNS Enabler SHALL be able to remove a Service Group.
CPNS-HLF-036 | The CPNS Enabler SHALL be able to identify CPNS entities, PN(s) and Service Group(s).

## Slide 6: Two types of group management
Service Group (SG) Management can be of two types, or a combination:
List-based group membership management
  Membership in the group may be decided from the start by the SG Owner, and stored as a list of the group membership
  SG Manager has the list where all member PNEs and PN GWs are registered. Membership is restricted to the PNE and PN GW which are listed.
  Realizes strict membership management
Policy-based group membership management
  SG Owner may decide that the group has an open membership (perhaps with conditions), and create a policy for the membership.
  SG Manager has the policy and distributes to Policy Enforcement Points (PEPs). The membership in the group is managed according to the policy by the PEPs locally.
  Realizes flexile membership management and alleviates load of SG Owner.
  (i.e. What SG Owner has to do is only create a policy. It doesn’t need to create a list of all member entities)

## Slide 7: Components of CPNS Group Management
PNE
PN GW
CPNS Server
CPNS User
PN or SG Owner
Policy Enforcement Point
PN and SG Manager, Policy Decision Point
Interface to XDMS (out of scope)
Policy or Member List
Provisioning Interface (out of scope)

## Slide 8: List-based and Policy-based Membership Management
Scenario
  For gaming application, Alice wants to create a Service Group with Bob, Charlie and Dave. Only game devices can join the Service Group.
CPNS Server
Alice
(SG Owner)
1. Alice manually identitifes the game devices of Bob, Charlie and Dave
3. Access and modify membership list
Creation of member list for list-based group
2. Create a list
Creation of policy for policy-based group
CPNS Server
2. Access and modify policy
1. Alice creates a policy
Alice
(SG Owner)
Game-A
Game-B
Game-C
(User = Bob OR Charlie
OR Dave) AND (Device = Game)
Bob
Charlie
Dave
Game-A
PMP
Game-B
Game-C
PMP
Bob
Charlie
Dave
Game-A
PMP
Game-B
Game-C
PMP
* Policy based management can be used for ad-hoc group

## Slide 9: Use of XDMS
The SG Owner can access the group membership list and policies in the XDMS by
  using the XDMC in the CPNS Server (i.e. updating the membership and policies in the XDMS, then synchronizing it with the CPNS Server)
  using a user interface on an authorized PNE to create updates of the membership list or policy, which are then synchronized with the XDMS through the XDMC.
The SG Owner can also access the Membership Database and the Policy Database in the CPNS Server.

## Slide 10: Issues for discussion with PAG
Use of XDMS
  Is it appropriate to use as a back end for the group management in CPNS?
  If not, what should we use to provision membership lists and policies to the CPNS Server?
Policies
  Can we use XDM Enabler to for policy management?
  If PEEM is used for policy management, can the policies be stored in XDMS and updated from there to the CPNS Server?