## Slide 1: OMA-CD-CPNS-2010-0032-CR_PN_Establishment_and_Registration Secure Session Establishment in PN Establishment and Registration
Submitted To: CD-CPNS
Date: 25th Jan. 2010
Availability: Public OMA Confidential
Contact: Takayuki Warabino, ta-warabino@kddi.com
Takashi Matsunaka, ta-matsunaka@kddi.com
Yuichi Ishikawa, yi-ishikawa@kddi.com
Tet Chiba, chiba@kddi.com
Source: KDDI
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Overview
Background:
  Sequence of “PN Establishment & Registration” is being discussed in CPNS.
  Authentication, authorization and secure session establishment for PNE should be done during “PN Est & Reg” phase.
  CPNS SWG has already agreed KDDI’s contribution regarding “Entity-User Key (EUKey)”, which can be used for the above purposes.
This INP clarifies:
  Sequence of EUKey assignment
  Sequence of authentication, authorization & secure session establishment by EUKey
  during “PN Establishment & Registration”

## Slide 3: Overview of the sequence in PN Est & Reg phase
PNE-1
PN GW-A
CPNS Server
e. (If ID & EUKey are not assigned) Assign ID & EUKey to PNE
a. CPNS Server authenticate & authorize PN GW
g. CPNS Server authenticates and authorize PNE by its ID & EUKey
f. Connection Setup Request
1
2
3
4
1. Secure Session Est between
PN GW and CPNS Server
3. ID & EUKey Assignment
4. Secure Session Est between PNE and PN GW
c. Physical pairing & entity discovery
d. Check if ID & EUKey assigned
h. Establish Secure Session
b. Establish Secure Session
i.
j.
k. Connection Setup Response
5. PN Inventory update
5
2. Entity Discovery in PN
Notes: 3

## Slide 4: 1. Secure Session Establishment between PN GW & CPNS Server
When?
  Secure session should be established before PN GW and CPNS Server start communication with each other
  Secure session establishment is triggered by either of two events
    When user manually triggers via PN GW’s UI (previous slide shows this case)
    When PN GW sends message to CPNS Server triggered by message from PNE
How?
  If PN GW connects to non-secure WAN:
    AUTH, AUZ and Secure Session establishment are done by SEC_CF
      EUKey can be used as password, PSK or certificate for AUTH and session establishment
      Since SEC_CF 1.0/1.1 supports only TLS, TLS session is established as secure session
  If PN GW connects to secure WAN (e.g. IMS):
    AUTH, AUZ and Secure Session establishment are done by underlying network mechanisms

## Slide 5: 1. Secure Session Establishment between PN GW & CPNS Server (cont.)
PN GW-A
CPNS Server
Manual
operation
PNE
A certain message
Triggered to send message to CPNS Server
SECA*
OSG*
TLS session setup
a.
b.
Either a. or b. triggers TLS session setup
* SECA (security agent) and OSG(OMA security gateway) are SEC_CF module
Non-secure WAN
According to SEC_CF AD,
  when http is used as transport protocol, PNGW MUST be authenticated by “Digest authentication”
  when transport is not http, PNGW can be authenticated by PSK or Certificate
For the above client authentication, EUKey can be used as password, PSK or certificate
  EUKey can be either of “PSK” or “Certificate”

## Slide 6: 2. Physical pairing & Entity Discovery in PN
In this step, PNE establishes a physical connection (e.g. bluetooth, WiFi) to PN GW device and discovers PN GW entity.
KDDI expects that other members come up with specific flow

## Slide 7: 3. ID & EUKey assignment to PNE
When?
  After physical pairing and entity discovery, and before PNE sends Connection Request
How ?
PNE checks if it already has ID & EUKey
If not, it requests ID & EUKey assignment to PN GW (ref. Appendix)
  Support shared-secret and certificate (public/private key) as Entity-User Key
    In case of Shared Secret Key, EUKey is shared between PNE & CPNS Server
    In case of Certificate, EUKey is signed by CPNS Server’s certificate
      PNE’s certificate can be validated by CPNS Server
  Key assignment can be performed in either of two ways
    Intermediate PN GW Initiated: Intermediate PN GW creates shared secret/certificate for PNE
      To create shared secret/certificate for PNE, Intermediate PN GW acquires “seed”/its own certificate from CPNS Server
    CPNS Server Initiated: CPNS Server creates shared secret/certificate for PNE
      Intermediate PN GW just forwards shared secret/certificate from CPNS Server to PNE
Notes: 7

## Slide 8: 3. ID & EUKey assignment to PNE (PN GW initiated EUKey assignment)
PNE-1
PN GW-A
CPNS Server
ID assignment request
Generate PNE’s ID
Seed/PN GW’s certificate request
Seed/PN GW’s certificate response
EUKey assignment response
Generate seed/certificate for PN GW
Checks if it can assign EUKey for PNE
If not
generate shared secret/certificate
If ID&EUKey are not assigned
EUKey assignment request
ID assignment response
ID
EUKey
PN GW initiated EUKey assignment
Notes: 8

## Slide 9: 3. ID & EUKey assignment to PNE (CPNS Server initiated EUKey assignment)
Sequences in grey are as same as previous slide
EUKey assignment request
EUKey assignment response
EUKey assignment response
Generate Shared Secret/Certificate for PNE
PNE-1
PN GW-A
CPNS Server
If ID&EUKey are not assigned
ID assignment request
Generate PNE’s ID
ID assignment response
EUKey assignment request
ID
EUKey
CPNS Server initiated EUKey assignment
Notes: 9

## Slide 10: 4. Secure Session Establishment between PNE & PN GW
When?
  PNE sends “Connection Setup Request” to PN GW
How?
  Before establishing secure session, PNE should be authenticated and authorized
  Authentication and authorization are done by the similar way to “Policy-based network management (e.g. IEEE802.1x (802.11i))”
    Authentication and authorization are done by PNE’s ID and EUKey
    Detailed sequence (appendix) differs depending on the form of EUKey (i.e. PSK or Certificate)
CPNS Server
(PDP)
PN GW
(PEP)
PNE
Policy
DB
1.Connection Request
3. Authentication and authorization request
6. Response with session key for secure session between PNE & PN GW
g. Secure session establishment
Authenticate PNE by its ID and EUKey,
Authorize connection request based on policy (checking msg sender and msg contents),
Create session key
4. Check policy
2. PN GW asks CPNS Server:
who is requesting to connect to my PN?
Is he allowed to connect to my PN?
5.
Notes: 10

## Slide 11: 5. PN Inventory update
Message for PN inventory update are exchanged on secure sessions established between PNE & PNGW, and PN GW & CPNS Server
KDDI expects that other members come up with specific flow
Notes: 11

## Slide 12: Recommendation
Recommend CPNS SWG to agree with the contents of the accompanied CR;
  “PN Establishment & Registration” can be divided into 5 steps:
    Secure Session Est between PN GW and CPNS Server
    Physical pairing and entity discovery in PN
    ID & EUKey assignment to PNE
    Secure Session Est between PNE and PN GW
    PN Inventory update
  Regarding 1,3 and 4, the flow described in this INP should be added in Appendix section of AD as a baseline for specific flow to be studied in TS phase.
    As for 2 and 5, KDDI expects contributions from other companies.

## Slide 13: Appendix
Quick recap of EUKey assignment
Detailed sequence of secure session establishment between PNE&PNGW (PSK based and Certificate based)

## Slide 14: Quick Recap: Entity-User Key Assignment Function
Assigns PN GW/PNE with Entity-User Key used for communication security between CPNS Server and the PN GW/PNE
  Assignment of Entity-User Key to Target PN GW/PNE is intermediated by Intermediate PN GW to ensure secure key assignment
CPNS Server
Target
PN GW
Target
PNE
Secure WAN
PNE
PN
Non-secure
WAN
PN
Secure PN
Intermediate
PN GW
Non-secure
WAN
PN
Public
PN GW
Key assignment signaling
Secure Communication Path
Intermediates
key assignment

## Slide 15: Detailed sequence of Secure Session Establishment between PNE & PN GW (PSK based)
PNE-1
PN GW-A
CPNS Server
When EUKey is in form of shared secret (Tentative. Will be studied further in TS phase…)
6-a. Challenge (N_gw)
6-b. Response (MIC p), Challenge (N_p)
6-c. Response (MIC_gw)
6-d. Finish
Share PMK between PNE-1 and PN GW-A
6-e. Derive PTK from PMK, N_p and N_gw
PMK: Pairwise Master Key
PTK: Pairwise Transient Key
MAC: Message Authentication Code
MIC: Message Integrity Code
1. Connection Request
3-a. Challenge (R_s)
3-b. Response (MAC_p) and Challenge (R_p)
3-d. Response (MAC_s)
5. Authentication and Authorization Response with PMK
3-f. Finish
2. Authentication and Authorization Request
3-g. Derive PMK from EUKey and R_p
3-g. Derive PMK from EUKey and R_p
4. Check policy
7. Secure session establishment with PTK
3-c. Authenticate PNE-1 with MAC_p
3-e. Authenticate CPNS Server with MAC_s
3. Authentication between PNE-A and CPNS Server
6. Authentication between PNE-A and PN GW-A
Notes: 15

## Slide 16: Detailed sequence of Secure Session Establishment between PNE & PN GW (cert based)
PNE-1
PN GW-A
CPNS Server
When EUKey is in form of certificate (Tentative. Will be studied further in TS phase…)
3-c. Server Nonce (R_s), Server Certificate (Cert_s)
3-d. PNE Certificate (Cert_p), Encrypted random number (E(pk_s, PMS)), PNE’s Signature (Sign_c)
3-f. Authentication Finished Message with Server’s Signature (Sign_s)
3-b. PNE Nonce (R_p)
3-e. Derive PMK from R_p, R_s , and PMS
1. Connection Request
2. Authentication and Authorization Request
3-a. Authentication Request
3-e. Derive PMK from R_p, R_s , and PMS
3. Authentication between PNE-A and CPNS Server
6-a. Challenge (N_gw)
6-b. Response (MIC p), Challenge (N_p)
6-c. Response (MIC_gw)
6-d. Finish
Share PMK between PNE-1 and PN GW-A
6-e. Derive PTK from PMK, N_p and N_gw
PMK: Pairwise Master Key
PTK: Pairwise Transient Key
PMS: Pre-shared Master Secret
Cert_p: PNE’s certificate
Cert_s: CPNS Server’s certificate
pk_p, sk_p: PNE’s public/private key
pk_s, sk_s: CPNS Server’s public/private key
5. Authentication and Authorization Response with PMK
4. Check policy
7. Secure session establishment with PTK
6. Authentication between PNE-A and PN GW-A
Notes: 16