## Slide 1: OMA-CD-CPNS-2010-0203-INP_PN_GW_Disconnection_Cases
Submitted To: OMA CD CPNS AHG
Date: 24 June 2010
Availability: Public OMA Confidential
Contact: Jean-François Deprun, jf.deprun@lge.com
Christophe Ochem, christophe.ochem@lge.com
Source: LG Electronics
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.
PN GW Disconnection Cases

## Slide 2: Preamble
This input contribution describes the PN GateWay disconnection cases from the CPNS server.
It is aimed to distinguish the accidental disconnection versus the requested disconnection cases.
This INP describes also the becoming of the PN:
  Either a new PN-GW is elected amongst the PNEs
  Either the PN shuts down
Through this contribution, LG suggests to standardizes the disconnection protocol between the CPNS server and the PN-GW.

## Slide 3: Disconnection Cases
Accidental disconnection with new PN-GW election
  The PN-GW has lost the connection with the CPNS server,
    Either the CPNS Server gets no answer from the PN-GW upon its requests
    Either the PN-GW sends messages to the CPNS Server, without response
  The connection of PN-GW with a non empty subset of PNE remains available
      Note: the connection is stated as lost on the base of criteria to be determined.
  The PN-GW enters an election procedure to select a PNE which can establish a connection to the CPNS Server
  We assume the CPNS Server is responsible for initiating the Switch procedure , which will attributes the gateway role to a new PNE: PNE#1
  PNE#1 is the new PN-GW and informs the other PNE on its role

## Slide 4: Disconnection Cases
Accidental disconnection - PN-GW shut down
  The PN-GW has lost the connection with the CPNS server
  In this case, we suppose:
    Either no PNE can be connected to the PN-GW
    Either the new PN-GW election procedure failed: no PNE owns the capabilities to become a new PN-GW
  The PN-GW requests a PN shut down

## Slide 5: Disconnection Cases
Disconnection request from PN-GW with PN-GW election
  The PN-GW initiates a disconnection request to the server,
  The CPNS server retrieves the status and the capabilities of the PNE to enter the new PN-GW election process
      Note: the Status and Statistics collection function is used.
  Based upon the statistics reports, the CPNS Server elects PNE#1 (e.g.)
  The CPNS Server initiates the switch procedure between the current PN-GW and PNE#1
  The CPNS Server disconnects the former PN-GW

## Slide 6: Disconnection Cases
Disconnection request from PN-GW: PN shut down
  The PN-GW initiates a disconnection request to the server
  In this case we have to distinguish:
    The PN-GW initiates a disconnection whilst it is disconnected from all the PNE: The PN-GW requests a PN shut down
    The PN-GW has connections with a non empty subset of PNEs, but none has the required capability to be elected as a new PN-GW: The CPNS Server states the PN shut down and erases the PN inventory.

## Slide 7: Conclusion
This Input Contribution is a base for the Disconnection cases to be accurately described in the TS.
It is also a base document to discuss on all the cases for which the Disconnection protocol has to be standardized.