## Slide 1: OMA-CD-DWAPI-2015-0043R01 Context of measurement sent from APIs For Discussion
Submitted To: CD (DWAPI)
Date: 9 November 2015
Availability: Public OMA Confidential
Contact: Max Hata, masato.hata.uf@s1.nttdocomo.com
Takafumi Yamazoe, yamazoet@nttdocomo.com
Source: NTT DOCOMO
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Current Status
We have been developing 6 TS for PCH:
  Weight Scale Body Composition Analyzer API
  Blood Pressure Monitor API
  Glucometer API
  Heart Rate Monitor API
  Pulse Oximeter API
  Thermometer API
All specs are designed based on the same architecture:
  One-shot measuring API
  Asynchronous messaging API

## Slide 3: Issues
Lack of context of data provided from API
  Some healthcare devices show progress of measurement until the final data is provided; some healthcare devices have several levels representing the accuracy of measurements
  Applications need to know which data is for intermediate progress and the final result
  But current TS drafts do not have any mechanisms to notify such context
Ambiguity of the purpose of the One-shot measuring API
  When should Plug-Ins return measurement results to the GotAPI Server for One-shot measuring requests?
  For what is the results of the One-shot measuring API used? (What are the use cases?)
The features to address these issues are not defined in the RD.
We understand these are not in the scope of IEEE specs and left for implementation of each device vendors
However, OMA DWAPI APIs should address these issues to enable good user friendly applications

## Slide 4: Levels of measurement accuracy (Example)
Temperature
Time
Prediction
20 sec
3 min
10 min
36.6℃
36.7℃
36.8℃
Actual measurement value
Pip!
Pip!
Pip!
Level
1
Level
2
Level
3
An example of thermometer (thermistor type)
Some devices have multiple reporting timing with different accuracies per single measurement

## Slide 5: Issues
All PCH APIs have the same issues:
  The current TS drafts don't specify:
    Framework to convey the context of data from APIs
    Timing when the One-shot API should return a result
  To enable user friendly user interfaces, apps should know:
    Which level of accuracy the result is
    Whether the measurement has finished or not
Solution:
  A) For one-shot and asynchronous, add new properties in the data set to each API to represent the context of the data
  B) For one-shot API (only), specify the timing to return the result for each API
    No need to specify the timing for asynchronous as it provides data whenever data becomes available

## Slide 6: A) Adding data set
thermometer: {
temperature: {
value: 36.8,
accuracy: 2,
maxAccuracy: 3,
state: 1,
...
},
...
}
Example of JSON
Add ‘accuracy’, ‘maxAccuracy’, ‘state’ to the messages of both one-shot and asynchronous
accuracy
  The type of this value is integer started from 0. The bigger value means higher accuracy.
maxAccuracy
  the type of this value is integer. This value depends on the type of the targeted device.
  0 is a special value, it means the targeted device doesn't have any timing meaning any accuracy levels (e.g., Heart Rate Monitor)
state
  This value is 0 or a positive integer.
  The value is 0, (i) when the device is in a standby mode (before measuring), or (ii) when the device is powered off
  The value is 1 when the device is measuring
  The value is 2 when the device has finished the measuring

## Slide 7: Principle of definitions of new values for data set
For devices which have multiple levels of accuracy
  e.g., Thermistor-based Thermometer
  "maxAccuracy" is greater than 1
  "accuracy" represents the accuracy level of the data that has been measured
For devices which don't have multiple levels of accuracy
  e.g., Glucometer, Blood Pressure Monitor, Weight Scale and BCA, Infrared-based Thermometer
  "maxAccuracy" is always 1
  When the measurement is in progress, "accuracy" is 0
  When the measurement has completed, "accuracy" is 1
For devices which don't have the state that the measurement has completed
  e.g., Heart Rate Monitor, Pulse Oximeter
  "maxAccuracy" and "accuracy" are always 0
  "state" never becomes 2

## Slide 8: B) Specifying the timing to return the result for One-shot messaging
When the one-shot request has been sent to a Plug-In from an application:
  If the measurement has completed and the device has the latest measurement value, the Plug-In SHALL return the latest value immediately.
  Otherwise, if the measurement is in progress:
    If the Plug-In expects that the next measurement value with a new accuracy level will come in a few seconds, the Plug-In SHALL wait until it gets the value of the next accuracy level, then return the value.
      e.g., Glucometer, Blood Pressure Monitor, Weight Scale and BCA, Infrared-based Thermometer, Thermistor-based Thermometer (when "accuracy" is still 0),
    If the Plug-In does not expect that the next measurement value with a new accuracy level will come in a few seconds or the device does not have the state that the measurement has completed, the Plug-In SHALL return the latest measurement value to the app immediately
      e.g., Thermistor-based Thermometer (when "accuracy" is greater than 1), Heart Rate Monitor, Pulse Oximeter

## Slide 9
Examples of messages for
one-shot
asynchronous

## Slide 10: 1. Thermistor-based Thermometers
3 min
20 sec
10 min
36.6℃
36.8℃
37.0℃
Pip!
Pip!
Pip!
temperature: {
value:36.6,
accuracy:1,
maxAccuracy:3,
state:1
}
temperature: {
value:36.6,
accuracy:1,
maxAccuracy:3,
state:1
}
36.7℃
36.9℃
wait
immediate
temperature: {
value:36.7,
accuracy:1,
maxAccuracy:3,
state:1
}
immediate
temperature: {
value:36.8,
accuracy:2,
maxAccuracy:3,
state:1
}
immediate
temperature: {
value:36.9,
accuracy:2,
maxAccuracy:3,
state:1
}
immediate
temperature: {
value:37.0,
accuracy:3,
maxAccuracy:3,
state:2
}
immediate
Indicator
on device
One-shot
Messaging
Asynchronous
Messaging
temperature: {
value:36.6,
accuracy:1,
maxAccuracy:3,
state:1
}
temperature: {
value:36.7,
accuracy:1,
maxAccuracy:3,
state:1
}
temperature: {
value:36.8,
accuracy:2,
maxAccuracy:3,
state:1
}
temperature: {
value:36.9,
accuracy:2,
maxAccuracy:3,
state:1
}
temperature: {
value:37.0,
accuracy:3,
maxAccuracy:3,
state:2
}
36.5℃
temperature: {
value:36.5,
accuracy:0,
maxAccuracy:3,
state:1
}
----
temperature: {
value:0,
accuracy:0,
maxAccuracy:3,
state:1
}
start
temperature: {
value:0,
accuracy:0,
maxAccuracy:3,
state:0
}
immediate
request
response
For one-shot
For asynchronous
message
Notations

## Slide 11: 2. Infrared-based Thermometers
5 sec
36.6℃
36.8℃
37.0℃
Pip!
temperature: {
value:37.0,
accuracy:1,
maxAccuracy:1,
state:2
}
36.7℃
36.9℃
wait
Indicator
on device
One-shot
Messaging
Asynchronous
Messaging
temperature: {
value:36.6,
accuracy:0,
maxAccuracy:1,
state:1
}
temperature: {
value:36.7,
accuracy:0,
maxAccuracy:1,
state:1
}
temperature: {
value:36.8,
accuracy:0,
maxAccuracy:1,
state:1
}
temperature: {
value:36.9,
accuracy:0,
maxAccuracy:1,
state:1
}
temperature: {
value:37.0,
accuracy:1,
maxAccuracy:1,
state:2
}
36.5℃
temperature: {
value:36.5,
accuracy:0,
maxAccuracy:1,
state:1
}
----
temperature: {
value:0,
accuracy:0,
maxAccuracy:1,
state:1
}
start
temperature: {
value:0,
accuracy:0,
maxAccuracy:1,
state:0
}
immediate
temperature: {
value:37.0,
accuracy:1,
maxAccuracy:1,
state:2
}
immediate
If any
(This intermediate reporting may not be present?)
request
response
For one-shot
For asynchronous
message
Notations

## Slide 12: 3. Glucometers
5 sec
355 mg/dl
357 mg/dl
359 mg/dl
Pip!
concentration: {
value:359,
accuracy:1,
maxAccuracy:1,
state:2
}
356 mg/dl
358 mg/dl
wait
Indicator
on device
One-shot
Messaging
Asynchronous
Messaging
concentration: {
value:355,
accuracy:0,
maxAccuracy:1,
state:1
}
concentration: {
value:356,
accuracy:0,
maxAccuracy:1,
state:1
}
concentration: {
value:357,
accuracy:0,
maxAccuracy:1,
state:1
}
concentration: {
value:358,
accuracy:0,
maxAccuracy:1,
state:1
}
concentration: {
value:359,
accuracy:1,
maxAccuracy:1,
state:2
}
354 mg/dl
concentration: {
value:354,
accuracy:0,
maxAccuracy:1,
state:1
}
----
concentration: {
value:0,
accuracy:0,
maxAccuracy:1,
state:1
}
start
concentration: {
value:0,
accuracy:0,
maxAccuracy:1,
state:0
}
immediate
concentration: {
value:359,
accuracy:1,
maxAccuracy:1,
state:2
}
immediate
If any
(This intermediate reporting may not be present?)
request
response
For one-shot
For asynchronous
message
Notations

## Slide 13: 4. Weight Scale Body Composition Analyzers
5 sec
69.2 kg
70.8 kg
71.3 kg
Pip!
bodyMass: {
value:71.3,
accuracy:1,
maxAccuracy:1,
state:2
}
69.9 kg
71.0 kg
wait
Indicator
on device
One-shot
Messaging
Asynchronous
Messaging
bodyMass: {
value:69.2,
accuracy:0,
maxAccuracy:1,
state:1
}
bodyMass: {
value:69.9,
accuracy:0,
maxAccuracy:1,
state:1
}
bodyMass: {
value:70.8,
accuracy:0,
maxAccuracy:1,
state:1
}
bodyMass: {
value:71.0,
accuracy:0,
maxAccuracy:1,
state:1
}
bodyMass: {
value:71.3,
accuracy:1,
maxAccuracy:1,
state:2
}
68.3 kg
bodyMass: {
value:68.3,
accuracy:0,
maxAccuracy:1,
state:1
}
----
bodyMass: {
value:0,
accuracy:0,
maxAccuracy:1,
state:1
}
start
bodyMass: {
value:0,
accuracy:0,
maxAccuracy:1,
state:0
}
immediate
bodyMass: {
value:71.3,
accuracy:1,
maxAccuracy:1,
state:2
}
immediate
If any
(This intermediate reporting may not be present?)
request
response
For one-shot
For asynchronous
message
Notations

## Slide 14: 5. Pulse Oximeters
98 %
98 %
98 %
98 %
98 %
Indicator
on device
One-shot
Messaging
Asynchronous
Messaging
spo2: {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
spo2: {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
spo2: {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
spo2: {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
spo2: {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
98 %
spo2: {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
----
spo2: {
value:0,
accuracy:0,
maxAccuracy:1,
state:1
}
start
spo2: {
value:0,
accuracy:0,
maxAccuracy:1,
state:0
}
immediate
5 sec
spo2 : {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
spo2 : {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
wait
immediate
spo2 : {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
immediate
spo2 : {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
immediate
spo2 : {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
immediate
spo2 : {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
immediate
spo2 : {
value:98,
accuracy:1,
maxAccuracy:1,
state:1
}
Pip!
6 sec
7 sec
8 sec
9 sec
10 sec
immediate
request
response
For one-shot
For asynchronous
message
Notations

## Slide 15: 6. Heart Rate Monitors
76 bpm
75 bpm
77 bpm
76 bpm
75 bpm
Indicator
on device
One-shot
Messaging
Asynchronous
Messaging
rate : {
value:76,
accuracy:1,
maxAccuracy:1,
state:1
}
rate : {
value:76,
accuracy:1,
maxAccuracy:1,
state:1
}
rate : {
value:75,
accuracy:1,
maxAccuracy:1,
state:1
}
rate : {
value:75,
accuracy:1,
maxAccuracy:1,
state:1
}
rate : {
value:77,
accuracy:1,
maxAccuracy:1,
state:1
}
75 bpm
rate : {
value:75,
accuracy:1,
maxAccuracy:1,
state:1
}
----
rate : {
value:0,
accuracy:0,
maxAccuracy:1,
state:1
}
start
rate: {
value:0,
accuracy:0,
maxAccuracy:1,
state:0
}
immediate
5 sec
rate : {
value:75,
accuracy:1,
maxAccuracy:1,
state:1
}
rate : {
value:76,
accuracy:1,
maxAccuracy:1,
state:1
}
wait
immediate
rate : {
value:76,
accuracy:1,
maxAccuracy:1,
state:1
}
immediate
rate : {
value:75,
accuracy:1,
maxAccuracy:1,
state:1
}
immediate
rate : {
value:75,
accuracy:1,
maxAccuracy:1,
state:1
}
immediate
rate : {
value:77,
accuracy:1,
maxAccuracy:1,
state:1
}
immediate
rate : {
value:75,
accuracy:1,
maxAccuracy:1,
state:1
}
Pip!
6 sec
7 sec
8 sec
9 sec
10 sec
immediate
request
response
For one-shot
For asynchronous
message
Notations

## Slide 16: 7. Blood Pressure Monitors
10 sec
100 mmHg
100 mmHg
146 mmHg
Pip!
systolic: {
value:146,
accuracy:1,
maxAccuracy:1,
state:2
}
160 mmHg
40 mmHg
wait
Indicator
on device
One-shot
Messaging
Asynchronous
Messaging
systolic: {
value:0,
accuracy:0,
maxAccuracy:1,
state:1
}
systolic: {
value:0,
accuracy:0,
maxAccuracy:1,
state:1
}
systolic: {
value:0,
accuracy:0,
maxAccuracy:1,
state:1
}
systolic: {
value:0,
accuracy:0,
maxAccuracy:1,
state:1
}
systolic: {
value:37.0,
accuracy:1,
maxAccuracy:1,
state:2
}
40 mmHg
systolic: {
value:0,
accuracy:0,
maxAccuracy:1,
state:1
}
----
systolic: {
value:0,
accuracy:0,
maxAccuracy:1,
state:1
}
start
systolic: {
value:0,
accuracy:0,
maxAccuracy:1,
state:0
}
immediate
systolic: {
value:146,
accuracy:1,
maxAccuracy:1,
state:2
}
immediate
if any
(This intermediate reporting may not be present?)
Blood Pressure Monitor shows the pressure of cuff during measuring.
The display of cuff pressure is only for user interface and it has nothing to do with the final blood pressure value.
Watch https://youtu.be/fsRFXgoOsW4
The current TS draft does not specify the pressure of cuff. Is it needed?
The device shows the pressure of cuff while measuring

## Slide 17: Conclusion
Shall we implement the solution to the TS?
Messages | Property | Timing
One-shot | Add properties; accuracy, maxAccuracy and state | Specify the timing to return the result for each API
Asynchronous |  | No specification
For the problem of lacking the context of the data from the APIs and ambiguity of one-shot responses, a solution is proposed:
One-shot and Asynchronous:
  Add properties in the messages: accuracy, maxAccuracy and state
One-shot (only)
  Specify timing to return the results