## Slide 1: OMA-COM-CPM-2017-0121-INP_discussion_on_pager_mode Discussion on Pager Mode Standalone Message
Submitted To: COM-CPM
Date: 25 Oct 2017
Availability: Public OMA Confidential
Contact: Jianping Zheng, Yue Liu, Yingjie Hong, Hao Dong
Source: China Mobile, ZTE Corporation
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Outline
Standalone Message vs. Chat for 1-1 Messaging
Analysis on Limitation of Pager Mode Standalone Message
Proposal: Amendment of Pager Mode Standalone Message

## Slide 3: 1-1 Messaging Mechanisms
Considering the large scale connections of CPM clients and high concurrency of message traffic, we need a low cost mechanism for 1-1 Messaging
Option 1: Chat
Option 2: Standalone Message
  Pager Mode
  Large Message Mode

## Slide 4: Network Resource Consumption : Standalone Message vs. Chat
Memory: see Table 2.
IP Address: Chat needs much more IP/Port resource for MSRP sessions
 |  | Traffic Mode (A) | Traffic Mode (B) | Traffic Mode (C) | Traffic Mode (D)
Standalone message |  | 128.59 | 128.59 | 128.59 | 128.59
Session mode(Note 1) | overall | 146.05 | 164.10 | 308.50 | 489.00
 | SIP stack | 132.05 | 136.10 | 168.50 | 209.00
 | MSRP stack | 1.20 | 2.40 | 12.00 | 24.00
 | MSRP k-alive | 12.80 | 25.60 | 128.00 | 256.00
 | Traffic Mode (A) | Traffic Mode (B) | Traffic Mode (C) | Traffic Mode (D)
Online users | 1000000 | 1000000 | 1000000 | 1000000
Average conversation per user | 0.10 | 0.20 | 1.00 | 2.00
Average messages per conversation | 20 | 10 | 2 | 1
Note 1:session timer = 300s
Table 1: User traffic mode
Table 2: Memory consumption in network equipments (GB)

## Slide 5: Client Resource Consumption: Standalone Message vs. Chat
Testing Environment
  User traffic mode: see Table 1.
  Network condition: low packet loss (L), high packet loss (H)
User activity | 1-to-1 text | 1-to-1 multimedia | Active Groups
low | 23.5 | 4.5 | 3
medium | 38.8 | 12.9 | 11
high | 64.4 | 16.2 | 14
Table 1: User traffic mode

## Slide 6: Client Resource Consumption: Standalone Message vs. Chat
Table 2: Traffic consumption in client
Low user activity
medium user activity
High user activity
Chart: Traffic Consumption （KB）
| low packet loss | high packet loss
session mode | 191.58 | 288.54
Standalone | 102.34 | 120.43
Chart: Traffic Consumption （KB）
| low packet loss | high packet loss
session mode | 592.26 | 771.51
Standalone | 326.89 | 360.1
Chart: Traffic Consumption （KB）
| low packet loss | high packet loss
session mode | 913.08 | 1280.02
Standalone | 709.16 | 731.18
Table 3: Power consumption in client
Low user activity
medium user activity
High user activity
Chart: Power Consumption (mAh)
| low packet loss | high packet loss
session mode | 3.25 | 8.6
Standalone | 4.22 | 5.82
Chart: Power Consumption（mAh)
| low packet loss | high packet loss
session mode | 10.86 | 21.08
Standalone | 11.27 | 13.09
Chart: Power Consumption (mAh)
| low packet loss | high packet loss
session mode | 18.12 | 34.62
Standalone | 18.52 | 20.09

## Slide 7: Standalone Message vs. Chat
We can see advantages of Standalone Message over Chat
  For user: lower consumption of power and traffic in the client
  For MNO: lower network cost of servers, less IP addresses

## Slide 8: The limitation of Pager Mode message
  As specified in CPM, The Size of Pager Mode in CPM is strictly limited to 1300 bytes
    The size of a Pager Mode CPM Standalone Message should not exceed 1300 bytes. If a CPM Standalone Message is larger than 1300 bytes, the contents of the message are not inserted into the SIP MESSAGE request but are carried via MSRP as defined in [RFC4975] and [RFC6714]. In that case, a SIP session is established between the interested parties (sender and all receivers) with MSRP as the Media Stream.
    (Note: from 5.1 CPM Standalone Message)

## Slide 9: Problem: long size of RCS Additional Headers
  In RCS 1-1 Messaging, due to so many additional Headers introduced by IMS/RCS, it is likely that the size of Pager Mode Message Header will be close to1300 bytes or even more.
    Examples
      Some special feature tags, such as system message and alias in MaaP, shell be included in many header (e.g. accept-contact, P-Perferred-Service)
        +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-application.ims.icsi.cpm.systemmsg"
        +g.3gpp.iari-ref="urn%3Aurn-7%3A3gpp-application.ims.iari.rcs.alias";require;explicit
      Some headers required by 3GPP, such as P-Access-Network-Info
        P-Access-Network-Info:3GPP-EUTRAN-TDD; utran-cell-id-3gpp=1112233C476B4321;network-provided
      Some additional CPIM headers
        In multi-device scenario, sip.instance carried in CPIM.from/CPIM.to header because Connect header is not supported in SIP MESSAGE.
Pager Mode Standalone Message can only carry very small size text content (e.g. less than 100bytes), or even worse, it will not be used in Standalone Message

## Slide 10: Question: Can we have a Pager Mode Message over 1300 bytes?

## Slide 11: Analysis on related specifications
IETF RFCs allow SIP MESSAGE exceed 1300 bytes, and SIMPLE IM does so
IETF RFCs
  SIP
    [RFC 3261] If a request is within 200 bytes of the path MTU, or if it is larger than 1300 bytes and the path MTU is unknown, the request MUST be sent using an RFC 2914 congestion controlled transport protocol, such as TCP
  SIP MESSAGE
    [RFC 3428] The size of MESSAGE requests outside of a media session MUST NOT exceed 1300 bytes, unless the UAC has positive knowledge that the message will not traverse a congestion-unsafe link at any hop, or that the message size is at least 200 bytes less than the lowest MTU value found en route to the UAS.
OMA TS
  SIMPLE IM
    the total size of the message is below 1300 bytes; or the total size of the message is greater than 1300 bytes and the IM Client has a positive knowledge of a guaranteed end-to-end connection of a ‘connection-oriented transport protocol’, as defined in [RFC 3428].

## Slide 12: Practice in Super Pager Mode Message
In China Mobile’s RCS, the size of Pager Mode message can be up to 8K
TCP is used for UNI
  PS connection, WLAN connection
UDP is used for NNI of RCS Interworking between MNOs (in testing trail)
  Interconnection over Internet between MNOs
Based on the testing result, the reliability of super Pager Mode Messages (2K-8K) is nearly equivalent to small Page Mode Message (less than 1300 bytes)
The feasibility of super Pager Mode Message has been verified

## Slide 13: Proposal: Amendment of Pager Mode Standalone Message
The size of Page Mode Standalone Message can exceed 1300 bytes (up to 8K) if the client has positive knowledge that the message will not traverse a congestion-unsafe link at any hop
It is proposed to amend the specification about Pager Mode Standalone Message in CPM
  The related CR against OMA-TS-CPM_Conversation_Function-V2_2-20170612-D is proposed , see OMA-COM-CPM-2017-0120-CR_pager_mode_amendment