## Slide 1
Companies attending workshop are listed. Joint contributors to be confirmed!
Airbus, Airwave, AT&T, BlackBerry, CESG, Ericsson, French MoI, Harris, UK Home Office, Kodiak, Motorola Solutions, NEC Europe Ltd, Telefonica O2, Qualcomm, Samsung, Selex, Sepura, Teltronic, Thales, Vodafone
Security Requirements for MCPTT
3GPP TSG SA6 Meeting #1 S6-xxxxxx
Sorrento, IT; 26th – 30th January 2015
3GPP TSG SA3 Meeting #78 S3-xxxxxx
Sorrento, IT; 26th – 30th January 2015

## Slide 2: Introduction
This presentation is a multi-company input contribution to 3GPP SA3 and SA6
A joint workshop was held between members of OMA PCPS and ETSI TCCE WG4 on 2-4 December 2014 in Cambridge, UK.
The workshop produced a high level functional architecture, and mapped this to existing OMA PCPS and TCCE stage 2 architectures which include PTT functionality
During the exercise, security requirements were identified from participants’ experience with mission critical systems,
SA3 is requested to consider these security requirements for MCPTT.

## Slide 3
SIP
registrar
Authent-ication
SIP routing
User Identity
function
Media control
Media distribut-ion
PTT services
Group manage-ment
Resource Manage-ment
SecurityManage-ment
Bearer network
PCRF
BMSC
Administration database
PGW
PGW
AS6
AS7
AS8
AP1
AP2
AP3
AP4
AP5
AP6
AP7
AP8
AP9
High Level Functional Architecture from Workshop
Client
AS3-1
AS5
AS4-1
AS4-2
AS3-2
AS1
AS2
AS9

## Slide 4: Identity considerations
Visible in bearer network
IMEI – 3GPP equipment identifier
USIM
  UICC application
  IMSI – 3GPP subscription identifier, necessary for access to 3GPP network (contained on USIM)
    Root of security
ISIM – IMS subscription identity module
  UICC application
  IMPI – Private identity to route to registrar
  IMPU – Public identity known to others
  Can reuse IMSI security, or can be separate
******************************************************************
Visible to application domain only
User + device instance specific identifier
  SIP device specific routable contact address (URI) for the user following ‘logon process’
  Multiple devices, multiple URIs per user supported
  Application level security
User Identity
  Use for logon + security credential
  Device independent
  Identity useable across multiple services
  Temporary identity for emergency situation

## Slide 5: Additional security requirements from a public safety security perspective - 1
End user organization security requirements
  Confidentiality of media from anyone outside the organization
  Authenticity of all users claiming membership of the organization and communication rights within the organization
  Confidentiality of identities and call related information from anyone outside the application space
  Individual membership of communication groups is specifically sensitive
  Need to trust the application provider to provide the communication service – but not with traffic content
  May not trust bearer provider
  Does not trust members of the public, and will communicate with the public through controlled interfaces
Implications
  User identity function is owned by end user organisation and/or application provider
    Separate user identity functions may be owned by different organizations within the same PTT application
  Interface between PTT services and User Identity Function needs authenticity and confidentiality protection
  Called user address (which may be a SIP URI) shall not be visible to the bearer network in some configurations.
  Calling user address must also not be visible to the bearer network

## Slide 6: Additional security requirements from a public safety security perspective - 2
Group management function – should be hidden from bearer network
  Expect AS5 to be encrypted
Security management function – should be hidden from the bearer network
  Expect AS9 to be encrypted
Security management function shall be able to live in a different trust domain to the rest of the application space
  E.g. in end user organisation, when another owns the application space
If SIP routing function terminates the encrypted tunnel between application and the client for control signalling, it must sit in the trusted security domain (AS2 must be encrypted through bearer network)
Media control and Media distribution paths to/from client – AS3-1, AS3-2, AS4-1 and AS4-2 to be encrypted through the bearer network

## Slide 7: Summary
From consideration of an architecture with a basis in OMA PCPS and ETSI TCCE CCA work, these additional security considerations were discussed
The companies presenting these considerations urge that these are taken into account into any MCPTT architecture solution