## Slide 1: OMA-COM-CPM-2013-0021-INP_CPM_IDs CPM IDs
Submitted To: OMA CPM
Date: 19 02 2013
Availability: Public OMA Confidential
Contact: Thinh Nguyenphu, thinh.nguyenphu@nsn.com
Bernhard Meier, bernhard.meier@ericsson.com
Thomas Scheerbarth, Thomas.Scheerbarth@telekom.de
Source: DT, NSN, Ericsson
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: CPM Conversation
CPM Conversation
CPM Session
CPM
Standalone
Message
Pager Mode
Large Msg
Mode
SIP
Message
SIP
Session
FToMSRP
Ad-Hoc Group
Pre-Defined Group
Single Recipient
Sender’s point of view
Open
Closed
Pre-determined
Join-in
1-1 Chat
Group Chat
SIP
Message
SIP
Message
SIP
Session
SIP
Session
SIP
Message
SIP
Session
CPM
Session
CPM
Session
CPM
Session
CPM
Session
CPM
Session
CPM
Session
CPM
Session
CPM
Session
Addressing
Object
CPM
Session
User
Defined
XDM
Defined
Showing messaging technology
CPM File
Transfer
FToHTTP*
HTTP
Session
HTTP
Session
HTTP
Session
HTTP
Session
* Defined in RCS, not CPM
N/A
N/A

## Slide 3: CPM Groups
CPM Pre-Defined Group:
  Identified by well known SIP URI in Shared XDM
  Controlled by policies in Shared XDM Group (OMA-TS-XDM_Group-V1_1-20120403-A)
    Can have zero or more pre-defined participants
    Defined policies on supported services (File Transfer, etc.)
  Pre-Arranged
    Controlling Function always sends INVITEs to participants
    Owner who can add or remove participants
  Join-In
    Controlling Function never sends INVITEs to participants
    Loose restrictions on who can join
    CPM Client send SIP INVITE to joint CPM Group.
CPM Ad-Hoc Group:
  Identified by a list of participants
  Controlled by Service Provider policies at the Controlling Function
    Controlling Function always sends INVITEs to participants
  Open
    In the case of CPM Session, Participants can invite others
    In the case of Standalone Message is not applicable.
  Closed
    Participants cannot invite others
    In the case of CPM Session, SDP marked with “a=chatroom” in the INVITE

## Slide 4: CPM Standalone & CPM Session IDs
CPM Standalone:
  Pager Mode: Conversation-ID, Contribution-ID, inReplyTo-Contribution-ID;
  Large Message: Conversation-ID, Contribution-ID, inReplyTo-Contribution-ID. (note: is not a CPM Session, only a SIP session)
CPM Session:
  CPM 1-1 Session: Conversation-ID, Contribution-ID, inReplyTo-Contribution-ID
    CPM File Transfer (use same procedure as CPM Session): Conversation-ID (reuse), Contribution-ID (new), inReplyTo-Contribution-ID (reuse)
  CPM Group Session: CPM Group Chat or File Transfer with group chat: Conversation-ID, Contribution-ID, inReplyTo-Contribution-ID, CPM Group Session-ID.
    CPM File Transfer (use same procedure as CPM Session): Conversation-ID (reuse), Contribution-ID (new), inReplyTo-Contribution-ID (reuse)
Extending CPM 1-1 Session to CPM Group Session: Conversation-ID (reuse), Contribution-ID (new), inReplyTo-Contribution-ID (reuse), Session-Replace (previous Contribution-ID)

## Slide 5: CPM Standalone
CPM Client
PF
CF
Create
Contribution-ID
Conversation-ID
Put ID’s in Invite
Message Storage
Contribution IDs
Conversation Ids
Conversation –ID
Contribution-ID
InReplyTo-Contribution-ID
0
IDs in INVITE
Contribution-ID
Conversation-ID
InReplyTo-Contribution-ID
PF or CF
0
Terminating
Network
Session Info Object
IDs in INVITE
Contribution-ID
Conversation-ID
InReplyTo-Contribution-ID
IDs in INVITE
Contribution-ID
Conversation-ID
InReplyTo-Contribution-ID
Note: for Pre-define group, CPM Client includes Request-URI to the address of the target CPM Pre-defined Group

## Slide 6: CPM 1-1 Session
CPM Client
PF
CF
Create
Contribution-ID
Conversation-ID
Put ID’s in Invite
Message Storage
Contribution IDs
Conversation Ids
Conversation -ID
Contribution-ID
InReplyTo-Contribution-ID
0
IDs in INVITE
Contribution-ID
Conversation-ID
InReplyTo-Contribution-ID
PF or CF
0
Terminating
Network
Session Info Object
IDs in INVITE
Contribution-ID
Conversation-ID
InReplyTo-Contribution-ID
IDs in INVITE
Contribution-ID
Conversation-ID
InReplyTo-Contribution-ID

## Slide 7: CPM Group Session
CPM Client
PF
CF
Create
Contribution-ID
Conversation-ID
Put ID’s in Invite
Message Storage
Contribution ID
Conversation –ID
Lastfocussessionid =
CPM Group Session IDs
Conversation -ID
Contribution-ID
InReplyTo-Contribution-ID
CPM Group Session ID (ifocus)
Group State Object
0
IDs in INVITE
Contribution-ID
Conversation-ID
InReplyTo-Contribution-ID
PF or CF
0
Terminating
Network
Session Info Object
IDs in INVITE
Contribution-ID
Conversation-ID
InReplyTo-Contribution-ID
Message Storage
Contribution ID
List of participants
Type of Group Session
Lastfocussessionid =
CPM Group Session IDs
IDs in INVITE
Contribution-ID
Conversation-ID
InReplyTo-Contribution-ID
Note: Extending CPM 1-1 Session to CPM Group Session: Conversation-ID (reuse), Contribution-ID (new), inReplyTo-Contribution-ID (reuse), Session-Replace (previous Contribution-ID)

## Slide 8: CPM Stand-alone Message - Pager
Message | Conversation ID | Contribution ID | InReplyTo-Contribution-ID | CPM Group Session ID
SIP MESSAGE 1 | Created by Joe: Abcd-123-456 | Created by Joe: Bcde-456-231 | - | N/A
SIP MESSAGE 2 | Reused by Joana: Abcd-123-456 | Created by Joana: Cdef-654-123 | Reused by Joana: Bcde-456-231 | N/A
SIP MESSAGE 3 | Reused by Joe: Abcd-123-456 | Created by Joe: Defa-456-231 | Reused by Joe: Cdef-654-123 | N/A
SIP MESSAGE 4 | Reused by Joana: Abcd-123-456 | Created by Joana: Efab-654-123 | Reused by Joana: Defa-456-231 | N/A
File Transfer 1 INVITE | Reused by Joe: Abcd-123-456 | Created by Joe: Face-546-231 | Reused by Joe: Efab-654-123 | New INVITE, New CPM Session
MSRP setup | - | - | - | -
MSRP data transfer | - | - | - | -
SIP MESSAGE 5 | Reused by Joe: Abcd-123-456 | Created by Joe: Bcde-456-231 | Reused by Joe: Efab-654-123 | N/A
Joe
Joana
SIP MESSAGE 1
SIP MESSAGE 2
SIP MESSAGE 4
200 OK
(“Ok, what is it?”)
(“Hey, I have a file for you”)
(“Ok send it!”)
200 OK
SIP MESSAGE 3
200 OK
(“Munich has snow!”)
200 OK
FToMSRP INVITE
200 OK
MSRP session setup
BYE (tear down FT MSRP Session)
MSRP data transfer
X
X
Chat Message 5
(“Ok got it - thanks!”)
200 OK

## Slide 9: CPM Stand-alone Message - Large
Message | Conversation ID | Contribution ID | InReplyTo-Contribution-ID | CPM Group Session ID
Message 1 | Created by Joe: Abcd-123-456 | Created by Joe: Bcde-456-231 | - | New SIP Session
Message 2 | Reused by Joana: Abcd-123-456 | Created by Joana: Cdef-654-123 | Reused by Joana: Bcde-456-231 | New SIP Session
Message 3 | Reused by Joana: Abcd-123-456 | Created by Joana: Cdef-654-123 | Reused by Joana: Cdef-654-123 | New SIP Session
File Transfer 1 INVITE | Reused by Joe: Abcd-123-456 | Created by Joe: Face-546-231 | Reused by Joe: Cdef-654-123 | New INVITE, New CPM Session
MSRP setup | - | - | - | -
MSRP data transfer | - | - | - | -
Etc… |  |  |  | 
Joe
Joana
SIP INVITE
200 OK
MSRP session setup & Data transfer
(“Hey, I have a file for you”)
BYE (tear down LMM SIP Session)
Message 1…
SIP INVITE
200 OK
MSRP session setup & Data transfer
(“Ok ready!”)
BYE (tear down LMM SIP Session)
Message 2…
FToMSRP INVITE
200 OK
MSRP session setup
BYE (tear down FT MSRP Session)
MSRP data transfer

## Slide 10: CPM 1-1 Session
Message | Conversation ID | Contribution ID | InReplyTo-Contribution-ID | CPM Group Session ID
Chat INVITE | Created by Joe: Abcd-123-456 | Created by Joe: Bcde-456-231 | - | -
MSRP setup | - | - | - | -
Chat Message 1 | - | - | - | -
Chat Message 2 | - | - | - | -
Chat Message 3 | - | - | - | -
File Transfer 1 INVITE | Reused by Joe: Abcd-123-456 | Created by Joe: Efab-546-231 | Reused by Joe: Bcde-456-231 | New INVITE New CPM Session
MSRP setup | - | - | - | Created by Joe: Face-567-876
MSRP data transfer | - | - | - | -
Chat Message 4 | Reused by Joe: Abcd-123-456 | Created by Joe: Defa-456-231 | Reused by Joe: Bcde-456-231 | -
Joe
Joana
Chat INVITE
Chat Message 1 (SEND)
Chat Message 2
Chat Message 3
FToMSRP INVITE
200 OK
MSRP session setup
(“Ok, what is it?”)
(“Hey, I have a file for you”)
(“Munich has snow!”)
(“Ok send it!”)
200 OK
MSRP session setup
BYE (tear down FT MSRP Session)
MSRP data transfer (SEND)
X
X
Chat Message 4
(“Ok got it - thanks!”)
BYE (tear down 1-1 Chat Session)

## Slide 11: CPM Group Session
Message | Conversation ID | Contribution ID | InReplyTo-Contribution-ID | CPM Session ID (Group)
Group INVITE | Created by Joe: Abcd-123-456 | Created by Joe: Bcde-456-231 | - | -
MSRP setup | - | - | - | -
Chat Message 1 | - | - | - | -
Chat Message 2 | - | - | - | -
Chat Message 3 | - | - | - | -
File Transfer 1 INVITE | Reused by Joe: Abcd-123-456 | Created by Joe: Efab-546-231 | Reused by Joe: Bcde-456-231 | New INVITE New CPM Session
MSRP setup | - | - | - | Created by Joe: Face-567-876
MSRP data transfer | - | - | - | -
Chat Message 4 | Reused by Joe: Abcd-123-456 | Created by Joe: Defa-456-231 | Reused by Joe: Bcde-456-231 | -
Joe
Joana
CF
Jenny
Group INVITE
1st MSRP Message
(“OK, ready”)
(“Hey, I have a file for you”)
2nd MSRP Message
(“Can’t wait!”)
3rd MSRP Message
FToMSRP INVITE
MSRP session setup
BYE (tear down FT MSRP Session)
MSRP data transfer
X
X
4th MSRP Message
(“Looks like y’all got it”)
MSRP Setup