## Slide 1: LwM2M Conformance Test Specification Proposal
Telecommunications Technology Association
2018.02.26
TTA

## Slide 2
Contents
ICS
Intro
Test case
Test Tool
Work Plan
Q&A
Status

## Slide 3
Intro
LwM2M Conformance Test Specification
  OMA has SCR(Static Conformance Requirement) for LwM2M
  Work Plan contribution of conformance test cases was submitted(Feb. 2017)
  TTA has developed LwM2M ICS(Implementation Conformance Status), Conformance Test Specification based on the SCR document
  TTA has published LwM2M Conformance Test Specification as Korean Standard at Dec. 2017
    (TTAK.KO-10.1035) Conformance Test Specification for LwM2M Server
    (TTAK.KO-10.1036) Conformance Test Specification for LwM2M Client
OMA
TTA

## Slide 4
Status
LwM2M Conformance Test Specification
ICS
Test Spec.
Requirement Documents
  ICS(Implementation Conformance Specification)
  Conformance Test Specification
  Testing Framework(Definition of confor. & Interop.)
    Already exist? Or Mandated in OMA?
  ICS document will be developed based on SCR.
    TTA has ICS in Korean version
  TTA will developed the conformance test spec with Korean standard
    Need to update and modify in the current version

## Slide 5
ICS
LwM2M Conformance Test Specification
ICS based on SCR

## Slide 6
ICS
LwM2M Conformance Test Specification
Structure
Roles
  Table 1. Roles
Version
  Table 2. Version
LwM2M Client Role
  Table 3. Bootstrap Interface
  Table 4. Client Registration
  Table 5. Device Management and Service Enablement
  Table 6. Information Reporting
  Table 7. Data Format
  Table 8. Security
  Table 9. Mechanism
  Table 10. Objects
LwM2M Server Role
  Table 11. Bootstrap Interface
  Table 12. Client Registration
  Table 13. Device Management and Service Enablement
  Table 14. Information Reporting
  Table 15. Data Format
  Table 16. Security
  Table 17. Mechanism
  Table 18. Objects
IXIT
Item | Role | Status | Support
1 | LwM2M Client | C.1 | Yes / No
2 | LwM2M Server | C.1 | Yes / No
3.1. Roles
Table 1. Roles
3.2. Version
Table 2. Version
Item | Version | Status | Support
1 | LwM2M v1.0 | M | Yes / No
Item | Capability | Status | Requirement | Support
1 | Support of at least one Bootstrap Mode | M | 3/1a OR 3/1b OR 3/1c OR 3/1d | Yes / No
1a | Support of Factory Bootstrap Mode | O |  | Yes / No
1b | Support of Bootstrap from Smartcard | O | 3/8 | Yes / No
3.3. LwM2M Client Role
Table 3. Bootstrap Interface
Prerequisite: 1/1
C.1: Mandatory to support at least one role of LwM2M
Table Number/Item Number
  3/1a: Support of Factory Bootstrap Mode
Status
  M: Mandatory, O: Optional, C.n: Conditional

## Slide 7
ICS(Example)
LwM2M Conformance Test Specification
Item | Capability | Status | Support
1 | Support of at least one Bootstrap Mode | M | Yes / No
1a | Support of Factory Bootstrap Mode | C.1 | Yes / No
1b | Support of Bootstrap from Smartcard | C.1 | Yes / No
1c | Support of Client Initiated Bootstrap | C.1 | Yes / No
1d | Support of Server Initiated Bootstrap | C.1 | Yes / No
2 | Support of LwM2M Server Bootstrap Information | M | Yes / No
3 | Support of LwM2M Bootstrap-Server Bootstrap Information | O | Yes / No
4 | Support of accepting Bootstrap Information transferred | M | Yes / No
5 | Support of Bootstrap Sequence | M | Yes / No
6 | Support of Bootstrap Security | M | Yes / No
7 | Support of Bootstrap from Smartcard with Secure Channel | O | Yes / No
8 | Retrieve & Process bootstrap data from Smartcard | C.2 | Yes / No
9 | Check for Bootstrap Data change in Smartcard | O | Yes / No
10 | Support of the BOOSTRAP-REQUEST operation | C.3 | Yes / No
11 | Support of the BOOTSTRAP-FINISH, BOOTSTRAP DISCOVER, BOOTSTRAP WRITE, BOOTSTRAP DELETE operations | C.4 | Yes / No
12 | Check and report Bootstrap Configuration Inconsistency | C.4 | Yes / No
Table 3. Bootstrap Interface
Prerequisite: 1/1
C.1: Mandatory to support at least one item
C.2: Mandatory If 3/1b or 3/7 is supported, otherwise excluded.
C.3: Mandatory If 3/1c is supported, otherwise excluded.
C.4: Mandatory If 3/1c or 3/1d is supported, otherwise excluded.
3.3. LwM2M Client Role

## Slide 8
Test Case
LwM2M Conformance Test Specification
Test Configuration
LwM2M_CFG_S_01
LwM2M_CFG_S_02
LwM2M Bootstrap Server,
LwM2M Server
LwM2M Client
IUT
Tester
LwM2M Server
LwM2M Client
IUT
Tester
LwM2M Server
IUT
LwM2M_CFG_C_01
LwM2M Client
IUT
Tester
LwM2M Client
IUT
LwM2M Bootstrap Server,
LwM2M Server

## Slide 9
  Test Group
    Bootstrap Interface(BOOT)
    Client Registration(CR)
    Device Management and Service Enablement Interface(DMSE)
    Information Reporting(IR)
    Security(SEC)
    Objects(OBJ)
  Test Group
Test Case
LwM2M Conformance Test Specification
Test Suite Structure(TSS)
Test Group
  Bootstrap Interface(BOOT)
  Client Registration(CR)
  Device Management and Service Enablement Interface(DMSE)
Naming Convention of Test Case Identifier
  Information Reporting(IR)
  Security(SEC)
  Objects(OBJ)
Name | Option | Interpretation
TP/<root>/<gr>/<nnn>/<ent> |  | 
<root> = root | LwM2M | LwM2M
<gr> = group | BOOT | Common Service Function
 | CR | 
 | DMSE | 
 | IR | 
 | SEC | 
 | OBJ | 
<nnn> = sequential number | 001 to 999 | -
<ent> = entity | S | Server
 | C | Client

## Slide 10
Test Case
LwM2M Conformance Test Specification
Test Case(Example)
TC ID | LwM2M-BOOT-005-S-01
Test objective | Check that the IUT supports Bootstrap mode
Reference | -
Config Id | CFG_S_01
PICS Selection | -
Initial conditions | Tester is registered in IUT.
Test Procedure | 1. IUT sends a request message to Tester. - CoAP Message: DELETE / 2. Tester sends a response message to IUT. - CoAP Message: 2.02 Deleted 3. IUT sends Bootstrap message with one or more security object instance to Tester. - CoAP Message: PUT /0/1 (Security Object Instance) 4. Tester sends a response message to IUT. - CoAP Message: 2.04 Changed. …. …. ….
Pass/Fail | IUT is successfully registered and sends correct Bootstrap information to client.

## Slide 11
Test Tool
LwM2M Conformance Test Specification
LwM2M Conformance Test Tool
  Operated on the Linux OS
  Chrome Interface
  LwM2M Client Test cases(60 cases)
  LwM2M Server Test cases(39 cases)
  Support Remote Testing
TTA is working in Test Tool Validation Process with Korean manufacturers(~Mar. 2018)
TTA will participate in TestFest with the conformance test tool.

## Slide 12
Work Plan
LwM2M Conformance Test Specification
Contribution of Skeleton for LwM2M Con. Test Spec.
Submission of Draft version(ICS and TS)
Completed (TBD)
’18.4
’18.6
’18.7
’18.12(TBD)
Review and check ambiguity of test specification in TestFest

## Slide 13
Q & A

## Slide 14: Thank you