## Slide 1: LwM2M v1.1 – Introduce and follow 3GPP CIoT implementation
Rationale : 3GPP CIoT needs updates to LwM2M v1.1
Proposal : Following new additions are to be introduced in LwM2M v1.1
  Rate Control
  Byte Control
  Connection management new resources accomodating 3GPP CIoT needs
  SCEF to LwM2M server bulk interface
  SCEF to LwM2M server message ID introduction at LwM2M layer
  Group identification for 3GPP network

## Slide 2: LwM2M v1.1 – Introduce and follow 3GPP CIoT implementation
Illustration :
  Refer existing LwM2M v1.1 TS baseline for rate control, connection management
  SCEF to Server bulk interface and message ID (OMA-DM-LightweightM2M-2016-0111-INP_Bulk_Structure_LWM2M)
  Group Identification to be illustrated for 3GPP network like a parameter in the core link format detected by LwM2M
    3GPP_GP could be a good qualified group identification which can be used for
    GP is used in resource directory IETF, when introduced in LwM2M could refer to groups towards RD, should not conflict conflict with 3GPP_GP

## Slide 3: LwM2M v1.1 – Introduce and follow 3GPP CIoT implementation
Impact :
  Bootstrap Interface : it would be interesting to extend bootstrap with message ID and 3GPP group ID
  Notification Interface : message ID and group ID
  Device Management & Service Enablement
    All commands to be extended with group ID and message ID

## Slide 4: LwM2M v1.1 – Upgrading the client with settings preserved, fallback if necessary
Rationale : During the upgrade of the LwM2M client, several requests and conditions are being foreseen for ease of use, in order to increase the interoperability standards in this part of the feature, it needs to be more formal and possibly precise.
Proposal : Following requirements to be covered in the upgrade area
  Differntiate firmware vs software
  State preserved firmware upgrade
    for storing the state for surviving upgrade, Appendix E1, E2, E3, E5, E6 to be safeguarded
  reverting back to previous firmware, a recovery possibility
    Older states (of previous requirement) before firmware upgrade should be retained for reverting back to older firmware

## Slide 5: LwM2M v1.1 – Upgrading the client with settings preserved, fallback if necessary
Illustration :
  Section to elaborate on firmware vs software
  Earlier discussions yielded a object which is survived by firmware upgrade for providing the needed functionality of preserving the states on upgrade
  Reverting to the old firmware can be done using same object which survived the firmware upgrade procedure to store essentials for reverting back to older functionality
  Bootstrap mechanisms can access the object which survives the crash
  LwM2M server(s) could have access to the object though specific mechanisms to understand the presence of the object during starting handshake.

## Slide 6: LwM2M v1.1 – ACL to work on resource level
Use Case : ACL to work at resource level in order provide controls for specific resources towards one server whereas restrict the access of adjacent resources by that LwM2M server
Business need : Operators would like to assign resource level control for LwM2M servers to keep the access restrictions on objects for their internal and external exposure based on servers.

## Slide 7
Use Case : Client Hold Off Timer necessary relating to the server object. This is to ensure that the client is able to register after certain seconds as indicated in the client hold off timer.
Business need : The client hold off timer ensures that the client registers with that LwM2M server after certain time duration. This is to ensure the relevant systems in the backend areas, gets ready for coordinating with the device as soon as the device registers. When supporting multiple LWM2M server instances it is sometime necessary to have a configurable timer ( seconds) with which the client waits after being bootstrapped to register the first time with each to the server instances. This provides an opportunity for a provisioning system to learn of the deviceID and bs/ created credentials and provision them to the proper server instances prior to client registering.
LwM2M v1.1 – Client HoldOff Timer

## Slide 8
Client
Prov.Svr
Svr1
/bs
Svr2
Prov. Svr Sends Subscription info to /bs ( IMSI, MSISDN, ) endpoint name not yet known due to removable UICC.
Client powers up attempt /bs sending in endpoint name. /bs svr learns of endpoint name (IMEI-MSIDN)
/bs svr sends back endpoint name, IMSI, MSISDN, and credentials
/bs svr sends to client svr 1 URL and credentials, and svr 2 URL and credentials
Prov svr. Sends endpoint name, MSIDN, credentials, subscription information, APN etc.
Prov. Svr. Sends endpoint name, MSIDN, credentials, and configuration template to Application/repository svr.
Client registers with Svr 1 (mgmt)
Svr1(mgmt) sends network configuration, APNs, checks firmware etc.
Client registers with Svr 2 ( application/repository)
Svr2( application/repository) sends observation template to client configuring it for operation.
Svr 1 hold off-timer starts
Svr 2 hold off-timer starts
Svr 1 hold off-timer expires.
Svr 2 hold off-timer expires.
LwM2M v1.1 – Client HoldOff Timer