## Slide 1: OMA-DM-LightweightM2M-2018-xxxx-INP_virtual_notify_object Proposal to Support Virtual Notify Object
Submitted To: DM
Date: 16 Jan. 2018
Availability: Public OMA Confidential
Contact: Padmakumar.Subramani@nokia.com, mojan.mohajer@u-blox.com
Source: Nokia, u-blox
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Requirements
Providing a mechanism for atomic reporting of resources across different objects in a single client notification message
In LwM2M v1.0.x this requirement can only be met by one of two methods:
  Defining the data model such that to unnaturally group resources into objects for reporting purposes rather than logical relationships and coherence
  Defining additional/redundant objects that are simply duplicating existing resources of other objects
It is proposed to extend LwM2M v1.1 functionality to support grouping of resource links into generic virtual object instances where they can be observed and notified in a single operation.
Based on application requirements the server can create instances of virtual objects and populate it with a set of links to resources of other objects that it can then observe together.

## Slide 3: Virtual Notify Object Definition (Option 1)
Notification Attributes are configured in the Notify Object for each resource that has a link to from this instance of Notify Object. This allows other notify conditions to be configured independently on the actual resources for separate notifications if required.
ID | Resource Name | Instances | Type | Operations
0 | NotificationGroupID | Single | Integer | RW
1 | ResourceLinks | Multiple | Resource Links | RW
2 | NotifyConditions1 | Multiple | String | W
3 | ObservationEnabled | Single | Boolean | W
4 | MinReportInterval | Single | Integer | W
5 | MaxReportInterval | Single | Integer | W
6 | NotifyCriteriaMet | Single | Boolean | R

## Slide 4: Virtual Notify Object Definition (Option 2)
Notification Attributes are attached to the actual resources and setup through usual WRITE-ATTRIBUTE operation.
ID | Resource Name | Instances | Type | Operations
0 | NotificationGroupID | Single | Integer | RW
1 | ResourceLinks | Multiple | Resource Links | RW
3 | ObservationEnabled | Single | Boolean | W
4 | MinReportInterval | Single | Integer | W
5 | MaxReportInterval | Single | Integer | W
6 | NotifyCriteriaMet | Single | Boolean | R

## Slide 5: Resource Description and Usage
NotificationGroupID
  Used by the server to identify a given notification resource group across multiple clients. Server can use distinct IDs for each grouping of resources in different clients and use unicast or multicast addressing with filtering to access/control relevant instances in all clients, irrespective of object instance IDs assigned in each client.
ResourceLinks
  Array of links to resources across other objects that will be observed and notified through this instance of Virtual Notify Object
NotifyConditions (Option 1 only)
  Array of Notification Class Attributes settings corresponding to resources listed in ResourceLinks. For each entry in ResourceLinks there will be a corresponding string similar to URI query format used in LwM2M v1.0x Write-Attribute operation prior to a normal observe request. If no specific notification class attribute is required for a given resource link, its position in the array will be set to an empty string.

## Slide 6: Resource Description and Usage
ObservationEnabled
  Used by the server to stop/start notifications from the client for this instance of NotifyObject without having to cancel the observation. The client is expected to stop evaluating observation criteria when Notifications are disabled.
MinReportInterval
  Similar to Pmin, specifies the minimum interval between each notification from this instance of Notify Object; any individual Pmin configured by the server in NotifyConditions (option 1) or attached to the resource (Option 2) will be ignored and. Value 0 indicates no interval is configured
MaxReportInterval
  Similar to Pmax, specifies maximum period between the notifications from this instance; any individual Pmax configured by the server in NotifyConditions (option 1) or attached to the resource (Option 2) will be ignored. Value 0 indicates no interval is configured
NotifyCriteriaMet
  Will be set to True by the client every time one or more of notification conditions are met and will be reset after notification is sent or ObservationEnabled is set to FALSE.

## Slide 7: Example Client with Notify Conditions
Client with Objects
Notification condition
  Temperature > 28 C
  Temperature < 25  C
  Humidity < 65%
  Battery Level
Object Name | Object ID | Number of Instances
Server | 1 | 1
Device | 3 | 1
IPSO Temperature Sensor | 3303 | 2
IPSO Humidity Sensor | 3304 | 1
Virtual Notify | 99 | 1

## Slide 8: Notify Object Content for Example Client
ResourceLinks Instances | Content
/99/0/1/0 | /3303/0/5700
/99/0/1/1 | /3303/1/5700
/99/0/1/2 | /3304/0//5700
/99/0/1/3 | /3/0/9
NotifyConditions Instances | Content
/99/0/2/0 | "lt=25;gt=28"
/99/0/2/1 | "lt=25;gt=28"
/99/0/2/2 | "lt=65"
/99/0/2/3 | ""
Other Resources | Content
NotificationGroupID | 1234
ObservationEnabled | TRUE
Pmin | 0
Pmax | 604800
NotifyCriteriaMet | FALSE
Option 1 Only

## Slide 9: Server Operations to Start Example Client Notifications
LwM2M Operation to start Observation:
  ObserveComplex /99/0
CoAP Method to start Observation:
  FETCH CoAP://www.example.com
  Token: 0xF1
  Content-Format: application/vnd.oma.lwm2m+json
  Accept: application/vnd.oma.lwm2m+json
  Observe: 0
  {"e" :[
  {"n" : "/99/0“}]
  }

## Slide 10: Example Client Notifications
LwM2M Notify where Temperature Sensor 0 reading has triggered notification
Two possible options for client notification message
  Client performs full mapping and includes reference to actual resources in its notification message
  Client only reports values against each of the resource links and the full mapping is done at the server, resulting in smaller notify messages
Mapping done by the client | Mapping done by the Server
Notify {"e" :[ {"bn" : "/3303/", "n": "0/5700", "v": 30}, {"n": “1/5700", "v": 26}, {"bn" : “/", "n": “3304/0/5700", "v": 75}, {"n": “3/0/9", "v": 90} ] } | Notify {"e" :[ {"bn" : "/99/0/", "n": "0", "v": 30}, {"n": "1", "v": 26}, {"n" : "2", "v": 75}, {"n": "3", "v": 90} ] }

## Slide 11: Example Client Notifications Mapping to CoAP
Mapping done by the client | Mapping done by the Server
CoAP Response 2.05 Token: 0xF1 Observe: 10 Content: {"e" :[ {"bn" : "/3303/", "n": "0/5700", "v": 30}, {"n": "1/5700", "v": 26}, {"bn" : "/", "n": "3304/0/5700", "v": 75}, {"n": "3/0/9", "v": 90} ] } | CoAP Response 2.05 Token: 0xF1 Observe: 10 Content: {"e" :[ {"bn" : "/99/0/", "n": "0", "v": 30}, {"n": "1", "v": 26}, {"n" : "2", "v": 75}, {"n": "3", "v": 90} ] }

## Slide 12: Issues to Be Decided
Option 1 or Option 2 for configuring Notification attributes?
Can potentially remove MinReportInterval and MaxReportInterval resources and replace with following rules for the client to follow:
  Use the smallest Pmin in case of multiple Pmin where each resource has different Pmin attached
  Use the smallest Pmax in case of multiple Pmax where each resource has different Pmax attached
Is new Observe Operation required, ObserveComplex, or can reuse existing one even though the rules are slightly different.
Is it acceptable to observe an instance of the virtual object and rely on change in NotifyCriteriaMet resource to trigger the notification but not include that resource itself in the NOTIFY message
What happens if one of the resources that has link to from Notify Object is removed? Should client autonomously set the ObservationEnabled flag to FALSE, and stop sending notification or delete the instance of Notify Object that is pointing to that resource?