## Slide 1: OMA-DM-LightweightM2M-2018-0062-INP_SwMgmt_v11
Submitted To: OMA-DM
Date: 2018 Dec 14th
Availability: Public OMA Confidential
Contact: Padmakumar.Subramani@nokia.com
Source: DMSE WG
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Software Management v1.1
Software Management 1.1
  To merge firmware update and Sw mgmt. objects
    Introduce manifest standardization
  Create links to software component from the new combined object
Proposal is to update firmware update object to a new version
  Add missing resources relevant for component
  Introduce manifest (and remove redundancy in software management)
Add user input wait resource
Add automatic flow for upgrade

## Slide 3: Firmware Update updates

## Slide 4: Firmware Update updates

## Slide 5: Firmware Update updates

## Slide 6
Firmware Update updates
To add resources from Software Mgmt Object 9
  Resource 10 (resource 5 of sw mgmt. 1.0) - Checkpoint
    Read, Single, Optional, Objlnk,<blank>,<blank>
    Description : Link to a Checkpoint“ object which allows to specify conditions/dependencies for a software update. E.g. power connected, sufficient memory, target system.
  Resource 11 (resource 6 of sw mgmt. 1.0) - Uninstall
    Execute,Single, optional, -, <blank>, <blank>
    Description : Uninstalls the software package. This executable resource may have one argument. If used with no argument or argument is 0, the Package is removed from the Device. If the argument is 1 (“ForUpdate”), the Client MUST prepare itself for receiving a Package used to upgrade the Software already in place. Update State is set back to INITIAL state.

## Slide 7
Firmware Update updates
To add resources from Software Mgmt Object 9
  Resource 12 – Upgrade Wait (New)
    RW, Single, Optional, Interger, 0-65535, Seconds
    Description : wait time in seconds before upgrading the package as defined in this object. Note this resource does not impact the software components and its actions
  Resource 13 (resource 13 of sw mgmt. 1.0) – Package Setting
    RW, Single, Optional, Objlnk, <blank>, <blank>
    Description : Link to “Package Settings” object which allows to modify at any time software configuration settings. This is an application specific object.
    Note: OMA might provide a template for a Package Settings object in a future release of this specification.

## Slide 8
Firmware Update updates
To add resources from Software Mgmt Object 9
  Resource 14 (resource 14 of sw mgmt. 1.0) – User Name
    W,Single, Optional, string, 0-255 bytes, <blank>
    Description : User Name for access to SW Update Package in pull mode. Key based mechanism can alternatively use for talking to the component server instead of user name and password combination.
  Resource 15 (resource 15 of sw mgmt. 1.0) – Password
    W,Single, Optional, string, 0-255 bytes , <blank>
    Password for access to SW Update Package in pull mode.
  Resource 16 (resource 17 of sw mgmt. 1.0) – Software Component Link
    R, Multiple, Optional, Objlink, <blank>, <blank>
    Description : Reference to SW Components downloaded and installed in scope of the present SW Update Package. Note: When resource 17 objlnk exist, resources 2, 3 in this table are ignored.

## Slide 9
Firmware Update updates
To add resources from Software Mgmt Object 9
  Resource 17 (resource 18 of sw mgmt. 1.0) – Software component tree length
    R, Single, Optional, Integer, 0-255, <blank>
    Description : Software Component tree length indicates the number of instances existing for this software package in the Software Component Object.
  Resource 18 – Automation (New)
    RW, Single, Optional, Boolean, <blank>, <blank>
    Description : TRUE indicates, no trigger would happen from the LwM2M server, all actions from download to upgrade should be automatically done at LwM2M Client. FALSE or this resource not present flow is as per state diagram and would follow the ability to intervene at each stage of the state as per LwM2M v1.0/1.1 TS definitions.
  (resource 8, 10, 11, 12 of sw mgmt. to be retired)

## Slide 10
Software Component Updates
To add resources from Software Component Object 14
  Resource 6 (resource 12 of sw mgmt. 1.0) – Activation State
    R, Single, Optional, Boolean, <blank> , <blank>
    Indicates the current activation state of this software: 0: DISABLED, Activation State is DISABLED if the Software Activation State Machine is in the INACTIVE state or not alive. 1: ENABLED, Activation State is ENABLED only if the Software Activation State Machine is in the ACTIVE state
  Resource 7 (resource 16 of sw. mgmt. 1.0) – Status Reason
    R, Single, Optional, String, <blank>, <blank>
    Contains the status of the actions done by the client on the SW Component(s) referred by the present SW Update Package. The status is defined in Appendix B.

## Slide 11
Software Mgmt 1.1
CoAP blockwise to be made applicable for both firmware update and sw component objects
Firmware Update would continue with existing functionality and if the resource 16 object link present then it would start to work with the components