## Slide 1: OMA-LOC-2013-0130-LPPe_2.0_CrowdSourcingAndSupl LPPe 2.0 Crowd Sourced Data over SUPL
Submitted To: LOC
Date: 18 Sep 2013
Availability: Public OMA Confidential
Contact: Ian Blair, ian.blair@csr.com
Source: CSR
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Crowd Sourcing in LPPe 2.0 over SUPL
Summary
  LPPe 2.0 will support Crowd Sourced data
  Following the discussion of OMA-LOC-2013-0088, it was determined that Crowd Sourced data should use Provide Location Information messages to transfer Crowd Sourced data to the Location Server
  LPPe used for Crowd Sourcing is likely to be seen in the context of SUPL 3.0
The purpose of this presentation is to discuss how LPPe Crowd Sourced may be signalled through an SLP that implements SUPL

## Slide 3: Use Cases
Crowd Sourcing requires the following Use cases:
Capability exchange
  An SLP supporting Crowd Sourcing needs to know (implicitly or explicitly) whether a SET supports it
Configuration
  When an SLP determines (through capability exchange) that a SET is available that supports Crowd Sourcing it may configure a SET to generate crowd sourced data reports.
Data transfer
  A SET that is configured for Crowd Sourced data reporting may then make periodic or data driven reports to the SLP
The above may be accommodated by means of one or more Generic SUPL Sessions.

## Slide 4: Generic SUPL Session
The concept of a GSS allows positioning activities initiated by either the SET or the SLP to take place at any time during the lifetime of a GSS session as long as the positioning activities are initiated by the same SUPL Agent which initiated the GSS session
Crowd Sourced data collection is effectively independent of normal positioning data collection – a GSS provides a way to do this

## Slide 5: GSS Suitability
A Generic SUPL Session (GSS) is defined as an “empty” SUPL session to be “filled” by Positioning Activities (e.g., assistance data delivery, positioning determination) related to the SUPL Agent which initiated the GSS – also of course, Crowd sourcing
A GSS is always associated with one single SUPL Agent only – we can treat the Crowd sourcing network entity similarly to a SUPL Agent.
A GSS provides a SUPL Session Framework (authentication, security, etc.) within which Positioning Activities may take place
Administrative functions like authentication, secure session establishment, etc. are performed only once during GSS establishment. Positioning Activities taking place in the course of a GSS need not invoke these functions again. – ideal for Crowd sourcing data, which may be collected over a protracted period
Positioning Activities may only be initiated by the SUPL Agent which initiated the GSS.
Positioning Activities may be executed at any time during the lifetime of a GSS.
GSS is supported in Network Initiated and SET Initiated mode.
A GSS can co-exist with other SUPL sessions and other GSSs – minimises interaction between crowd source data transfers and SUPL exchanges used for normal positioning.

## Slide 6: Network Initiated GSS for Crowd Sourcing

## Slide 7: SET Initiated GSS for Crowd Sourcing

## Slide 8: Summary and conclusion
Transfer of Crowd Sourced data, and related activities such as capability and configuration may be performed via GSS procedures
Network Initiated GSS procedures are appropriate for Network driven capability exchanges and configuration setting, together with data reporting from a SET in the same GSS session.
SET Initiated GSS procedures are appropriate for Crowd Sourced Data reporting triggered from the SET.