## Slide 1: OMA-ARC-2019-0007-INP_3GPP_MCData_RESTful_API 3GPP MCData RESTful API
Submitted To: SC
Date: 04 Apr. 2019
Availability: Public OMA Confidential
Contact: Shahram Mohajeri, sm7084@att.com
Source: AT&T
X
NO REPRESENTATIONS OR WARRANTIES (WHETHER EXPRESS OR IMPLIED) ARE MADE BY THE OPEN MOBILE ALLIANCE OR ANY OPEN MOBILE ALLIANCE MEMBER OR ITS AFFILIATES REGARDING ANY OF THE IPR’S REPRESENTED ON THE “OMA IPR DECLARATIONS” LIST, INCLUDING, BUT NOT LIMITED TO THE ACCURACY, COMPLETENESS, VALIDITY OR RELEVANCE OF THE INFORMATION OR WHETHER OR NOT SUCH RIGHTS ARE ESSENTIAL OR NON-ESSENTIAL.
THE OPEN MOBILE ALLIANCE IS NOT LIABLE FOR AND HEREBY DISCLAIMS ANY DIRECT, INDIRECT, PUNITIVE, SPECIAL, INCIDENTAL, CONSEQUENTIAL, OR EXEMPLARY DAMAGES ARISING OUT OF OR IN CONNECTION WITH THE USE OF DOCUMENTS AND THE INFORMATION CONTAINED IN THE DOCUMENTS.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at https://www.omaspecworks.org.

## Slide 2: Purpose
The purpose of this Input contribution is to inform OMA ARC and SC of a 3GPP WID which deals with specifying a RESTful API for the Mission Critical Data (MCData) Message Store which is very much the same as OMA Network Message Store (NMS) RESTful API
And also determine what is the best strategy in taking advantage of already defined OMA RESTful APIs within 3GPP’s Service Based Architecture (SBA)
  OMA NMS RESTful API is not going to be the last such API and hence a well understood approach to such cases would help the industry to better reuse standards where it makes sense. Reuse helps:
    Reduce the time it takes to specify a proven RESTful API
    Reduce implementation costs on clients & servers which used OMA’s spec
    Reduces operation headaches for MNOs

## Slide 3: 3GPP MCData Background
3GPP SA6 WG started defining the Mission Critical Data (MCData) architecture as of Rel-14
  MCData architecture utilises the 3GPP Packet Core and IMS amongst other common network functions to support mission critical services over LTE
MCData service suite provides generic capabilities and specific services enabling one-to-one and group data communications between MCData users
  Similar to RCS
MCData service can be used for public safety applications (e.g. FirstNet) and also for general commercial applications (e.g. utility companies and railways)

## Slide 4: 3GPP MCData Background (Cont’d)
MCData message store (one of the functional blocks within the MCData architecture) is used by MCData users to store their MCData communications permanently
MCData message store allows only an authorized user to access the storage area
  Similar to RCS or Messaging Apps on UE using the OMA NMS RESTful API
During an active MCData communication, the participating function on the MCData server deposits messages and files exchanged in the conversation to the user’s storage area of the MCData message store
  Similar to CPM communicating with NMS using the OMA NMS RESTful API (with some new operations)

## Slide 5: 3GPP MCData Background (Cont’d)
3GPP MCData message store interfaces (MCData-7 & MCData-8) are shown below
Operations invoked onto MCData message store over MCData-7 & MCData-8 are very much the same as what OMA has defined in NMS RESTful API
On-network functional model (3GPP- 23.282)

## Slide 6: OMA Northbound & 3GPP Southbound APIs
In the past, the general working model between OMA and 3GPP was:
  Southbound Native APIs (e.g. Diameter) defined by 3GPP
  Northbound APIs (HTTP-based RESTful) defined by OMA
  Exposure Layer (i.e. SCEF) provided network access control as well as any required protocol adaptation (e.g. HTTP to Diameter)
Exception: OMA NMS RESTful API was used in both Northbound and Southbound as the NMS enabler was defined in OMA as part of CPM architecture
  Hence, no adaptation of protocol needed by Exposure Layer
Service Exposure Model

## Slide 7: New 3GPP Northbound & Southbound APIs
3GPP has defined 5G Core network based on a Service Based Architecture (SBA)
3GPP 5G Service Based Interfaces (SBI’s) exposed by network enablers are RESTful, hence the new working model between OMA and 3GPP would most probably look be like:
  Southbound APIs defined by 3GPP Enablers are inherently RESTful
  Northbound APIs, in most cases, reuse the Southbound 3GPP RESTful APIs as is
    In some cases there maybe a need for further abstraction or aggregated Northbound RESTful APIs, which can be defined by either 3GPP or OMA (e.g. oneM2M use cases)
  Exposure Layer (i.e. SCEF and 5G NEF) would provide network access control, API disaggregation on the southbound and any required API adaptation to legacy client Apps (e.g. NMS client using OMA NMS RESTful API)

## Slide 8: Can 3GPP Reuse OMA NMS RESTful API as is?
MCData message store RESTful API defined by 3GPP is going to:
  Be based on 3GPP RESTful guidelines/principles which are very close to OMA’s but not the same
  Use different Common data structures (which are used over many SBI’s)
  Use OpenAPI 3.0 (formerly Swagger) specification to describe the RESTful API Contracts which leverages JSON Schema to describe data. A new way in the industry.
    In contrast, OMA uses XSD to specify input/output data structures since APIs needed to support XML/HTTP in addition to JSON/HTTP
    JSON examples generated using a proprietary tool and included in the TS
    JSON/HTTP is what is being used these days and hence less need for XSD
    In contrast to OpenAPI, XSD is not an API contract (i.e. doesn’t contain the endpoints, operation, input/output parameters, etc), so one has to use the XSD in conjunction with the associated TS document
As a result, OMA NMS RESTful API cannot be reused by 3GPP as is for MCData message store

## Slide 9: How Can 3GPP Take Advantage of OMA NMS RESTful API?
Ensure 3GPP MCData message store RESTful API is inspired and closely defined based on OMA NMS RESTful API spec.
  That means MCData message store in 3GPP network has a Southbound RESTful API which semantically and from RESTful Resources perspective is very close to OMA’s spec
  This allows legacy NMS client Apps still use the OMA NMS RESTful API to communicated with the 3GPP Exposure Layer (SCEF/NEF) on the Northbound
  This means Exposure Layer has a slim API adaptation function to worry about (i.e. small differences between the Northbound and the Southbound APIs)
In essence, 3GPP MCData message store RESTful API would look like the v2.0 of OMA NMS RESTful API!
  e.g. If the Operator deploys only one Network Message Store in support of both consumers and public safety applications then the new App clients can use the v2.0 version of the Northbound API while there is no impact to legacy Apps which keep using the v1.0 of the Northbound API

## Slide 10: Reusing OMA RESTful APIs Strategy in 3GPP
As an overall strategy, in order to ease API adaptation by the Exposure Layer and smoothen the migration path for Application clients from the legacy Northbound OMA RESTful APIs to newly defined 3GPP RESTful APIs, we should advocate the usage of OMA specs as guide in 3GPP
  Close reuse of the Resource Tree, HTTP operations and input/output parameters
Such strategy also benefits 3GPP Server/Enabler implementers who have already developed the OMA RESTful API
Another 3GPP RESTful API which could take advantage of the above strategy is the “OMA Notification Channel”
  Notification Channel is needed to enable NMS notifications to UE