## Slide 1: OMA LwM2M Overview
MIAMI 2015, June 8th
Thierry GARNIER, Gemalto N.V

## Slide 2: details
M2M Market
Technologies
Benefits
Ecosystem
M2M context
Useful references

## Slide 3: OMA LwM2M & M2M Market (1/2)
Since 2002, OMA DM Working Group has released a suite of specifications including:
    20+ mobile service enablers
    more than 60 Management Objects
More than 20+ Management Objects have been defined by other standardization organizations (ETSI, 3GPP,..)
OMA approach provides cost effective ways to deploy applications & services
( Risk , Fragmentation, Duplication are minimized)
In 2010, OMA DM group realized the emergence of one M2M market facet:
  always more connected objects were investing Cars, Home, and the Cities areas..
  a growing category among connected objects have :
    limited power processing & battery capacity
    reduced storage capacity, reduced size ..
  heterogeneous, fragmented and costly proprietary offers are a brake for this market

## Slide 4: OMA LwM2M & M2M Market (2/2)
Then OMA-DM WG has identified several needs :
  a need for more open and interoperable standards in the M2M arena technologies
  a need for a M2M standard able :
      to both address Device Management & Application Enablement
      to be used across various industry segments
  a need to address Constrained devices and environments, without sacrificing security
  a need for reducing M2M fragmentation offers in providing :
    faster solution development time (e.g. selected device could come with inadequate /no remote management capability)
    lower costs for M2M customers (economies of scale / leverage to innovation).
Within that scope OMA-DM group developed the Lightweight M2M Enabler providing:
  an highly innovative, slim and efficient client-server protocol
  an extendable data model
OMA LwM2M Enabler 1.0 has been released in December 2013.
Notes:     => applications regarding privacy, physical security, public safety are concerned

## Slide 5: details
M2M Market
Technologies
Benefits
Ecosystem
M2M context
Useful references

## Slide 6: OMA-LwM2M Technologies (1/7)
LwM2M Enabler defines the application layer communication protocol between a Server and a Client
  Client-Server Protocol is based on open IETF standards
      CoAP is an alternative to HTTP for RESTfull APIs in resource-constrained area
      DTLS brings TLS-like feature to the CoAP layer
    CoAP and DTLS are bound to UDP or SMS bearers
Typically :
  In LwM2M, the Server resides in a Data Center and the Client resides in the Device
  LwM2M separates Protocol Commands and Data Object (as in OMA DM 1.x and 2.0 )
LwM2M Enabler is focused on constrained M2M devices (low-power µC, low amount of Flash & RAM)
  Applicable to Cellular, 6LoWPAN, WiFi or any other IP based constrained devices or networks
  Public registry of Objects from OMA, other SDOs or enterprises
Notes:   . a LwM2M Server resides in a Data Center and can be hosted by Network Service Provider or M2M Application/Service Provider

## Slide 7: OMA-LwM2M Technologies (2/7)
Client-Server Protocol based on CoAP and DTLS IETF Standards
Extensible Object and Resource model for application semantics
  A Client has one or more Object Instances
  An Object is a collection of Resources
  A resource may be “Read”, “Written” or “Executed” and “Observed”
  A Resource may contain :
    a piece of information (value)
    a reference to an other Object Instance
  Resources can have multiple instances
Notes: CoAP protocol was defined by IETF Constrained RESTful Environment (CORE) WG: main goal was to keep message overhead small, limit fragmentation, support multicast and create a simplistic protocol for M2M.

## Slide 8: OMA-LwM2M Technologies (3/7)
4 Categories of LwM2M Operations
  Bootstrap operations
  Discovery/Registration operations
  Device Mgt & Serv. Enablement Operations
  Observe & Notify operations (Information reporting)
LwM2M Operations are mapped on :
  GET, PUT, POST and DELETE CoAP Operations
LwM2M Abstract Message Flow

## Slide 9: OMA-LwM2M Technologies (4/7)
OMA-LwM2M is based on OPEN IETF Standards
[RFC5262] CoAP main features required for LwM2M
  the 4-byte binary CoAP message header is used for Request and Response interactions.
  (12-bytes header for supporting the Information Reporting interface [NOTIFY])
  Confirmable, Acknowledgement and Reset messages MUST be supported.
  (Non-Confirmable msg MAY be used by a Client for sending Notifications)
  GET, PUT, POST and DELETE CoAP methods MUST be supported (LwM2M Operations)
  Possibility to specify the payload media type (Text, TLV, Opaque, Json)
  [RFC6347] UDP Channel Security for CoAP is DTLS
  equivalent of TLS v1.2 for HTTP modified to allow UDP unreliable and out of order transfers.
  use a subset of the Cipher Suites defined in TLS
  secure handshake with session key generation, mutual authentication, data integrity and confidentiality.
  Keying material for securing DTLS session :
    is provided during the Bootstrap phase
    is carried in a LwM2M Security Object Instance
Notes: [RFC5262] Main CoAP required Features for LwM2M
  only a small subset of options are required.
  the 4-byte binary CoAP message header is used for Request and Response interactions.
  (12-bytes header for supporting the Information Reporting interface [NOTIFY])
  Confirmable, Acknowledgement and Reset messages MUST be supported.
  (Non-Confirmable msg MAY be used by a Client for sending Notifications)
  GET, PUT, POST and DELETE CoAP methods MUST be supported (LwM2M Operations)
  A subset of CoAP Response Codes MUST be supported for LwM2M response messages
  The Content-Type option MAY be used for the media type of the payload (text, tlv, opaque, json)
Enabler specifies the option which are required for LwM2M

## Slide 10: OMA-LwM2M Technologies (5/7)
CoAP vs HTTP rational for constrained environments
  HTTP - ASCII- 55Bytes Header vs CoAP - Binary- 4Bytes header
  HTTP/TCP flow vs CoAP/ UDP flow
HTTP/TCP flow
CoAP/UDP flow

## Slide 11: AccESS CONTROL (6/7)
  When a LwM2M client is registered with more than one LwM2M Server, Access Control Object Instances are allocated for managing the Object Instances access rights

## Slide 12: OMA-LwM2M Technologies (7/7)
Technical Specification LwM2M 1.0 Released in 4Q 2013
  OMA LwM2M Enabler also specifies a set of 8 Device Management-oriented Objects
  0: Security Object -handles security aspects between LwM2M Client and Server
  1: Server -defines data and functions related to the LwM2M Server
  2: Access Control -defines the access rights which can be granted on Client Objects for a given Server
  3: Device -details device specific information
  4: Firmware -details resources on the device useful for firmware upgrades
  5: Location -groups resources providing information about the device current location
  6: Connectivity Monitoring -groups resources that assist in monitoring the status of a network connection
  7: Connection Statistics -groups resources that hold statistical information about an existing network connection
Notes: 0 : could be Bootstrap Server

## Slide 13: details
M2M Market
Technologies
Benefits
Ecosystem
M2M context
Useful references

## Slide 14: OMA-LwM2M BENEFITS
  Provides a Solution for Device and Application Management to access Constrained-Devices
  Services Providers, OEMs, end users take benefit from uniform management of constrained-devices (cost, simplicity, efficiency, multi-source)
  Complementary Solution to existing Dev Management (e.g.OMA DM, BBF-TR 069 ) in extending the range of devices which can be securely managed
  Based on Open and Interoperable Industry Standards
  Extensible Data Model and open naming authority for Objects registry (OMNA), provide wide and easy access to IoT industry
  A dynamic LwM2M ecosystem is being put in place by the community …..
Notes:   Services Providers, OEMs, end users take benefit from uniform management of constrained-devices (cost, usage and dev simplicity, communication efficiency, multi-source equipments available ..)
  Provide a simple solution to manage Dev & Application Managment in an uniform way.
  This solution is based on Open & Interoperable solution adressing constrained Env without compromission regarding security
  Simple Data Model can be extended by anybody
  Ecosystem …

## Slide 15: details
M2M Market
Technologies
Benefits
Ecosystem
M2M context
Useful references

## Slide 16: OMA-LwM2M ECOSYSTEM (1/2)
LwM2M ecosystem is growing
  IPSO Alliance is defining LwM2M objects for smart city/building applications
  OMA DM has added new functionalities/Objects to LwM2M TS 1.0 Enabler (Connectivity, Wipe and Lock, Software Mgnt, Device Capability Mgmt)
  Eclipse Foundation is providing two LwM2M open source projects (Wakaama, Leshan)
  OMA is developping a test suite for interoperability purpose
  OMA LwM2M Plug Test event
    a first event has been held with ETSI and IPSO Alliance in Nov 2013 in Las Vegas
    the second event took place 2015, Jan 26-29th in Dusseldorf, GERMANY
    a third event is likely to occur end of 2015
  OMA public available portal for supporting the LwM2M developer’s community
Focus

## Slide 17: OMA-LwM2M ECOSYSTEM (2/2)
FOCUS : OMA is proposing a web site (opened end of 2014)
OMA Developer ToolKit main content
    LwM2M Technical Specifications :Web based documents
    LwM2M Enabler Tutorial
    Simulates Client and Server functions
    Helps to analyze and modify Client/Server messages exchanges
    Client side is under development. (End of Dec 2014)
    Object Registration & Object Editor (OMNA)
    Editor tool to construct DM-MO as well as LwM2M Objects & Resources (end of Dec 2014)
    Lab Kit
    Provides a list of platforms supporting OMA LwM2M Client
    Basic examples dedicated for a given platform
  LwM2M Test Server: Sandbox
    This LwM2M Test server is maintained and provided by the Eclipse Foundation
OMA Developer ToolKit web site

## Slide 18: details
M2M Market
Technologies
Benefits
Ecosystem
M2M context
Useful references

## Slide 19: OMA-LwM2M in M2M Context
OMA has joined oneM2M as a Partner Type 2 (Sept 2012)
oneM2M uses existing Dev Mgnt Technologies : BBF TR-069 , OMA DM & OMA LwM2M
oneM2M has recently launched a Work Item on LWM2M Interworking Proxy (Jan 15)
    providing still more visibility to LWM2M (Application Service Layer)

## Slide 20: OMA-LwM2M in GSMA-IoT Context
LwM2M is likely to support GSMA-IoT CLP.03 requirements (DID4, DID5, DID6 , DID7)
Note : IoT Device Host can be a vehicle

## Slide 21: details
M2M Market
Technologies
Benefits
Ecosystem
M2M context
Useful references

## Slide 22: USEFUL References
OMA-LwM2M : OMA-TS-LightweightM2M-V1_0, December 2013 (in 2014 > 1153 downloads)
OMNA Lightweight M2M (LwM2M) Object & Resource Registry
[RFC 7252] : Constrained Application Protocol (CoAP) Shelby, Z., Hartke, K., Bormann, C., and B. Frank,June 2014
[RFC6347] , “Datagram Transport Layer Security Version 1.2”, Rescorla, E. and N. Modadugu,January 2012.
OMA–Lightweight M2M White paper : G. Klas, F. Rodermund, Vodafone; Z. Shelby,ARM; S. Akhour, J. Höller, Ericsson; 2014 (572 downloads)
IPSO Alliance
Eclipse Foundation
oneM2M TS-0005-Management_Enablement (OMA)-V-2014-08
OMA-M2Mi : OMA Management Interface for M2M V1.0

## Slide 23: Thank you